| CHANGE REQUEST |
| --- |
| Group Name:* | MAS#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-28 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution provides the DM Server Interactions for OMA DM |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0005, ver 0.2.0 |
| Clauses/Sub Clauses* | 5.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the DM Server Interactions for OMA DM 1.3 and 2.0.

### -----------------------Start of change 1-------------------------------------------

## 5.5	DM Server Interactions

This clause describes how the IN-CSE interacts with a DM Server in order to manage the devices. To interact with the DM Server, the IN-CSE needs to establish the communication session with the DM Server, translate requests/responses and notifications between the IN-CSE and the DM Server and discover the management objects in the device and Management Resources in the IN-CSE.

Note: The DM Server interaction is applicable to the case that the DM Server is external to the IN-CSE.

Note: OMA has started the work item called "Management Interface to M2M" [12] whose scope is to define requirements for an interface between the DM Server and the Machine to Machine (M2M) systems on top. This Northbound Interface (NBI) allows M2M service layer to access the DM Server functionality. The requirements for the interaction between the IN-CSE and the DM Server will be specified in [12].

### 5.5.1	Communication Session Establishment

The communication session can be initiated by the IN-CSE or by the DM Server. The IN-CSE can initiate the communication session if the IN-CSE needs to interact with the management objects in the device through the DM Server (e.g., an IN-AE sends firmware update Requests by using the [firmware] Resource in the IN-CSE). On the other hands, the DM Server can initiate the communication session if the DM Server detects changes of management objects that the DM Server manages or needs to notify events to the IN-CSE that occurred in the device. In this case, the notifications of management object changes or events can be limited to the cases that the IN-CSE has expressed interests.

The multiple communication sessions can be established between the IN-CSE and the DM Server depending on the communication environments and the protocols to be used for the communication session. The requirements for the communication session between the IN-CSE and the DM Server will be specified by [12].

### 5.5.2	Translation of Requests and Responses between IN-CSE and DM Server

This specification specifies how oneM2M service layer protocol regarding the device management shall be mapped to OMA DM protocol. The interaction between the IN-CSE and the DM Server lies between these two protocols and the Requests/Responses from those two protocols shall be properly translated by the interactions between the IN-CSE and the DM Server. Specifications for Requests/Responses translations between the IN-CSE and the DM Server is out-of-scope of this specification, and the requirements for the Requests/Responses translation will be specified by [12].

### 5.5.3	Discovery and Subscription for management objects

Being triggered by oneM2M service layer, the interactions between the IN-CSE and the DM Server can provide the following functionalities:

- Discovery of management objects in the devices of interest

- Subscription to management objects for being notified for the interested events

With the discovery and the subscription to the management objects in the device, the IN-CSE can be capable to synchronize the Management Resources with management objects in the device.

Note that requirements for the discovery and subscription for management objects will be specified by [12].

### 5.5.4	Access Control Management

For a device under managements, the IN-CSE can have multiple DM Servers that can connect to the device. Among those DM Servers, when receiving the oneM2M service layer Requests, the IN-CSE needs to select the proper DM Server that is successfully perform the received Request based on the authorities that each DM Server has. The interaction between the IN-CSE and the DM Server can be used to discover the authorities that the DM Server has.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: “oneM2M Functional Architecture”

[2]	oneM2M TS-0004: “oneM2M Protocol Specification”

[3]	oneM2M TR-0004: “Definitions and Acronyms”

[4]	“OMA Device Management Protocol”, Version 1.3, Open Mobile Alliance™, http://www.openmobilealliance.org/

[5]	“OMA Device Management Protocol”, Version 2.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

[6]	"OMA LightweightM2M”, Version 1.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

[12]	"OMA Management Interface to M2M Requirements", Version 1.0, Open Mobile Alliance™, http://www.openmobilealliance.org/

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?