## Slide 1: A sketch of the oneM2M Base Ontology - interworking aspects
Joerg Swetina
NEC Europe Ltd.
Joerg.swetina@neclab.eu
© NEC Europe Ltd. 2014
MAS-2015-0516R01

## Slide 2: Interworking oneM2M and devices in Area Network
oneM2M compliant Solution
Area Network (e.g. KNX)
real Devices in Area Network
“proxied” Devices in own oneM2M System technology
oneM2M Device
Inter working
Proxy Entity

## Slide 3: How do the “proxied” devices behave?
Interworking Proxy Entity (IPE) creates virtual, “proxied” devices as resources in the own, oneM2M compliant Solution. The IPE translates changes of resources in “proxied” devices into Area Nwk specific commands to the real devices - and vice versa.
“proxied” devices can be accessed through the mechanisms of the oneM2M System (RESTful access to oneM2M Resources)
“proxied” devices still exhibit their original information model. E.g.
  If the device in the original system (KNX) publishes a boolean-, a 3-byte-, and an integer value every 30 minutes then also the proxy does the same
oneM2M Device accessing the proxy needs to know the original (KNX) information model !
The original (KNX) information model is provided through a (KNX) specific specialization of the oneM2M Base Ontology

## Slide 4: The oneM2M base ontology: proposed Concepts
Network/Data view
Device
Function
Interface
accomplishes
offers
represents (at least one)
Operation
has Operation
WashingFunction
DryingFunction
TemperatureReading
TemperatureEvent- Reporting
LightControl
SmokeAlarming
Washing_Machine
TemperatureSensor
DoorSwitch
EnergyMeter
LightSwitch
SmokeSensor
Service
WashCycleService
Standby
SmokeAlarmService
Steers / is steered though
implements
Control-Interface
Monitoring-Interface
SetWashTemperature
StartWashing
(continuously-) display-Temperature
ToggleLightSwitch
CloseDoor
Functionality view

## Slide 5: Description of concepts (stateful)
[non-oneM2M] Device
  A device is a tangible object designed to accomplish a particular task. In order to accomplish this task, the device performs one or more functions. For example, a washing machine is designed to wash (task) and to accomplish this task it performs a washing-cycle- and a drying-cycle function.
Function (functionality view)
  A Function represents the functionality necessary to accomplish the task for which a Device is designed. A device can be designed to perform more than one function. A Function can have a State – e.g. washing colored laundry at 60 degrees.
Service (network/data view)
  A service is a representation of a function in an [Area] network that makes the function discoverable, registerable, remotely controllable by other devices in the network. A service can represent one or more functions. A Service is offered by a device that wants (a certain set of) its function(s) to be discoverable, registerable, remotely controllable by other devices in the network. A Service must specify the device that is offering the service, the function(s) to be represented, and the Interfaces (input and output data exchange) necessary to operate the service.

## Slide 6: proposed oneM2M Concepts - statefulness
Network/Data view
Device
Function
Interface
accomplishes
offers
represents (at least one)
Operation
hasOperation
WashingFunction
DryingFunction
TemperatureReading
TemperatureEvent- Reporting
LightControl
SmokeAlarming
SetWashTemperature
StartWashing
display-Temperature
ToggleLightSwitch
CloseDoor
Washing_Machine
TemperatureSensor
DoorSwitch
EnergyMeter
LightSwitch
SmokeSensor
Service
WashCycleService
Standby
SmokeAlarmService
Steers / is steered though
implements
Control-Interface
Monitoring-Interface
No State
(‚atomic‘ action)
Functionality view
Stateful
(multiple states possible)

## Slide 7: Description of concepts (non - stateful)
Operation (functionality view)
  An Operation is
    a directive that a influences the behavior (and possibly state) a certain Function – e.g. set washing temperature to xxx degrees
    Information provided by the Function – e.g. „current washing temperature“, or indication: „wash-cycle finished“
  An Operation has no state.
  Note: “Operation” is approximately equivalent to “Command” in SAREF (Smart Appliances REFerence ontology)
Interface (network/data view)
  An Interface specifies within a network the input and output data exchange necessary to operate the service. It is a implements in that network some Operation. An Interface is either
    An IO-Primitive
    or
    a Method
  Note: “Interface” is approximately equivalent to “property or state” in SAREF (Smart Appliances REFerence ontology)

## Slide 8: related SAREF Concepts
Functionality view
Network/Data view
Device
Function
Service
accomplishes
offers
represents (at least one)
hasCommand (at least one)
hasInputParameter
hasOutputParameter
StartPauseFunction
SensingFunction
EventFunction
OpenCloseFunction
LevelControlFunction
OnCommand
ToggleCommand
GetCommand
SetLevelCommand
( SetAbsoluteLevel
or SetRelativeLevel)
StepUpCommand
Washing_Machine
TemperatureSensor
EnergyMeter
SwitchOnService
Energy
Average enegy
Hot water energy
Maximun energy
Total energy
Humidity
Temperature
oneM2M: Interface
Property
oneM2M: Operation
Command

## Slide 9: proposed oneM2M Concepts - additions
Network/Data view
Device
Function
Interface
accomplishes
offers
represents (at least one)
Operation
hasOperation
WashingFunction
DryingFunction
TemperatureReading
TemperatureEvent- Reporting
LightControl
SmokeAlarming
Washing_Machine
TemperatureSensor
DoorSwitch
EnergyMeter
LightSwitch
SmokeSensor
Service
WashCycleService
Standby
SmokeAlarmService
Steers / is steered though
implements
Control-Interface
Monitoring-Interface
Fixed set consisting of:
In-Binary
In-Toggle
Out-Analogue
Out-Multistate
In-NextState
In-BLOB (binary obj.)
In-NULL (no data)
...
SetWashTemperature
StartWashing
(continuously-) display-Temperature
ToggleLightSwitch
CloseDoor
IO-Primitive
Is either of a
Method
IO-Primitive
Functionality view
Other meta- information
(e.g. latest update..)
Name/ID
Unit
provides
(for IO-Primitives and Methods)
Is identified by
hasUnit

## Slide 10: More on IO-Primitives and Methods
  IO-Primitive is a description of data transport to a device or from a device
    has a direction: ToDevice or FromDevice
    has a Name/ID
    may have a data value and a related data type
    Example: Name/ID = „desired washing temperature“, direction: „ToDevice“, data value: 40, data type: integer
    Example (of a device-initiated event): Name/ID = „finished washing!“, direction: „FromDevice“, no data value
  Method is a description of transaction with the device
    has is either invoked_in_the_device or invoked_by_the_device
    has a Name/ID
    may have IO-Promitives (which again have direction: ToDevice or FromDevice)
    Example: Name/ID = „Reboot“, direction: „ invoked_in_the device“, no IO-Primitive
  Note: if a Method is invoked_in_the_device and has IO-Primitives then
    first all data of IO-Primitives ToDevice are sent to the device as parameters of the Method
    then all data of IO-Primitives FromDevice are created as result of the execution of the Method
    (comprising a transaction at transport level)
    Example: Name/ID = „GET“, direction: „ invoked_in_the device“
      IO-Primitive ToDevice: Name/ID = „remaining_time“, direction: „ToDevice“, no data value
      IO-Primitive FromDevice: Name/ID = „remaining_time“, direction: „FromDevice“, data value = 90, data type: integer

## Slide 11: Examples of types of IO-Primitives (details tbd)
ToDevice
  TD_Binary
  TD_Integer
  TD_Analogue
  TD_ByteArray
  TD_String
  TD_NULL (no data)
  TD_MultiState
  ...
FromDevice
  FD_Binary
  FD_Integer
  FD_Analogue
  FD_ByteArray
  FD_String
  FD_MultiState
  ...

## Slide 12: Network/Data view
Interface
IO-Primitive
Service
Steers / is steered though
Method
contains 0 .. n
Device
offers
State
has zero or more
Name/ID
Is identified by
Name/ID
IO-Prim
ToDevice
Is either of
IO-Prim
FromDevice
IO-Primitive
Device
address
Can be reached in network via a
Is identified by
Is either of a

## Slide 13: Network/Data view (IPE, Area NW and NW Bus)
Device
M2M Area Network
Interworking Proxy [Application] Entity
Interworks with 1..n
Serves 0 ...k
Serves 0 .. x
Network Bus
offers
Bus Service
a Network Bus is a special (non- physical) device
For interworking purposes an IPE does not need to be part of the ontology

## Slide 14
Notes: NEC's brand statement, "Empowered by Innovation," expresses our commitment to empowering people and society through continuous innovation in every area of our businesses, fueled by our infinite passion for innovation and our customer-focused spirit of collaboration.