| Input Contribution |
| --- |
| Meeting ID* | TP#16 |
| Title:* | Modeling aspects for mash-up |
| Source:* | <Junling Mao> , <China Unicom> , <maojl11@chinaunicom.cn> <Changwei Hu>, <China Unicom>, <hucw5@chinaunicom.cn> <Peng Wang>, <China Unicom>, <wangpeng@chinaunicom.cn> |
| Uploaded Date:* | 2015-03-10 |
| Document(s) Impacted* | oneM2M-TR-0007-Study_on_Abstraction_and_Semantics_Enablement |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussions and adoption in the Abstraction and Semantics Technical Report. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The mash-up capability is considered to be required in oneM2M systems, since it can facilitate the access of complicated parameters which cannot be directly measured by physical sensors and support cooperative working of multiple devices. In this contribution, we give some considerations on the modelling aspects supporting mash-up.

- Discussion

According to the current device and things aspect association model in TR 0007, the mash-up relationships can be modelled in three categories.

- Things category

In this category, the mash-up relationship will be described from the perspective of things aspect. There will be a semantic rule or ontology to state the natural relationship between the mash-up things aspect and other related things aspects, e.g. the relationship between the air aspect Air quality index (AQI) and other air aspects such as PM2.5, PM10, SO2 and NO2. This is highly related to the domain ontology of air environment.

- Devices category

In this category, the mash-up relationship will be described from the perspective of devices. There will be a semantic rule or ontology to state the relationship between the operation of the mash-up devices and the operations of other devices involved in the mash-up. Fig.1 gives an example for the mash-up modelling in device category.

Fig.1 an example for mash-up modelling in device category

- Association category

In this category, the mash-up relationship will be described from the perspective of association. There will be a semantic rule or ontology to state the association between the mash-up aspect and related devices, e.g. the association between AQI and air quality related monitoring devices such as PM2.5, PM10, SO2 and NO2 monitoring devices. This type of association is more complex than the current association in TR 0007, since it will associate with multiple devices and a mash-up logic. Fig. 2 gives an example for mash-up modelling in association category.

Fig.2 an example for mash-up modelling in association category

In Table I, we give the comparisons of above modelling methods. It can be observed that modelling in devices category is preferred for the cooperative working case, and modelling in association category is more suitable for the complicated parameter sensing case. Overall, modelling in devices category seems a good choice, and modelling in association category can be considered as a supplementary method in future if necessary.

Table I. comparisons of mash-up relationship modelling

|  | Advantages | Weakness |
| --- | --- | --- |
| Things category | Natural expressions for the mash-up relationship Independent from the type of devices associated with thing aspects | hardly reflect the measured or impact quality may need to extend domain ontology |
| Devices category | easy for modelling the cooperative working of multiple devices flexible for reconstructing the mash-up of devices | not easy for reflecting the measured quality for the mash-up aspects impacted by the devices involved in mash-up. |
| Association category | facilitate reflecting the measured or impact quality flexible for reconstructing the mash-up of devices | not easy for modelling the cooperative working of multiple devices |

- Proposal

It is proposed to model the mash-up relationship in devices category and add the following content to TR 0007.

======================== Start of 1st Change ========================

#### 8.2.2.6	Modelling of mash-up devices

The basic structure for modelling Devices is described in Fig. 27 of section 8.2.2.1.In that structure, specific Device Types and successively Operation and Parameter Types are involved. The structure for modelling mash-up devices should inherit the basic structure for modelling devices, but may extend the basic structure for describing the mash-up relationship between mash-up devices and other devices involved in mash-up. A concept named Mash-up is introduced for representing the mash-up relationship.

As shown in Fig. x, the Operation of mash-up device will be linked to the Mash-up concept.  Besides Operation of mash-up device, the Mash-up concept is also associated with Operations of other devices involved in mash-up and a Mash-up logic concept.

Fig.x Structure for modelling mash-up devices

There are two types of relations between the Mash-up concept and Operations of other devices involved in mash-up. One type indicates that the Operation plays an input role in the mash-up, the other type indicates that the Operation plays an output role in the mash-up.

The Mash-up logic concept is used to describe the service logic used in the mash-up.  It will have a data type property (e.g. xsd: string) for logic expression.

# ======================== End of 1st Change ========================