| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#16.2 |
| Source:* | Martin Bauer, NEC, martin.bauer@neclab.eu Joerg Swetina, NEC, joerg.swetina@neclab.eu Ataru Kobayashi, NEC, a-kobayashi@df.jp.nec.com Omar Elloumi, Alcatel-Lucent, omar.elloumi@alcatel-lucent.com |
| Date:* | 2015-05-04 |
| Contact:* | Martin Bauer, NEC, martin.bauer@neclab.eu |
| Reason for Change/s:* | Add attribute to resources to store semantic descriptor |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0005 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0007 v2.4.0 |
| Clauses/Sub Clauses* | 8.5 Architectural Aspects |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

After some discussions, we propose to use a semantic descriptor resource for semantic descriptions of <AE>, <container> and <contentInstance> resources. ARC-2015-1844-semanticDescriptor_resourc is a CR to TS-0001 and this CR in Revision 3 is a kind of companion CR to TR-0007 to keep the overall information in the TR up-to-date.

In Section 8.5.2 we propose a general semantic descriptor attribute for the semantic annotation of  resources and give an example how it is used for the case of the Smart Appliance REFerence Ontology (SAREF) that has been defined by TNO on a contract from the European Commission, and which will be published as a normative specification by ETSI Smart M2M using the oneM2M platform. Some further study may be required to identify exactly which resources should have this attribute and whether multiple, more specific semantic attributes should be defined. At the moment, we do not have a clear view on how the semantic information should be split up into different attributes and what the implications of such a  step for semantic functionality, e.g. discovery would be. Depending on the outcome of the discussion, we plan to provide a CR to TS-0001 for TP#17.

### -----------------------Start of change 1-------------------------------------------

## 8.5	Architectural Aspects

### 8.5.2	Semantic Description of Resources

#### 8.5.2.1 Overview

As identified in the requirements, Sermantic Annotation within the oneM2M platform is of key importances for supporting semantic functionalities within the oneM2M platform. In the following subsections a semantic descriptor is introduced.

#### 8.5.2.2 Semantic Descriptor

Resources of type <AE>, <container> and <contentInstance> optionally have a semantic descriptor resource, which is further described in section 8.5.2.3. This is shown in figure 8.5.2.2-1,  where <resource> only refers to resources of type <AE>, <container> and <contentInstance>.

Figure 8.5.2.2-1: semanticDescriptor resource

#### 8.5.2.3	Resource semanticDescriptor

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description can be provided according to ontologies. The semantic information is used  by the semantic functionalities of the oneM2M system and is also available to applications or CSEs

Figure 8.5.2.3-1: Structure of <semanticDescriptor> resource

The <semanticDescriptor> resource contains the child resources specified in table 8.5.2.3-1.

Table 8.5.2.3-1: Child resources of <semanticDescriptor> resource

| Child Resources of <semanticDescriptor> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See [i.39], clause 9.6.8 where the type of this resource is described. |

The <semanticDescriptor> resource contains the attributes specified in table 8.5.2.3-2.

Table 8.5.2.3-2: Attributes of <semanticDescriptor> resource

| Attributes of <semanticDescriptor> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See [i.39], clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See [i.39], clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See [i.39], clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See [i.39], clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See [i.39], clause 9.6.1.3 where this common attribute is described |
| creationTime | 1 | RO | See [i.39], clause 9.6.1.3 where this common attribute is described |
| expirationTime | 1 | RW | See [i.39], clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See [i.39], clause 9.6.1.3 where this common attribute is described |
| labels | 0..1 (L) | RW | See [i.39], clause 9.6.1.3 where this common attribute is described |
| creator | 0..1 | RO | The AE-ID of the entity which created the resource. This can also be the CSE-ID of the IN-CSE if the IN-CSE created the resource. |
| descriptor | 1 | RW | The semantic description of the resource whose child resource the <semanticDescriptor> resource is. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	ETSI TS 102 690: "Machine-to-Machine communications (M2M); Functional architecture".

[i.2]	ETSI TR 101 584: "Machine-to-Machine communications (M2M); Study on Semantic support for M2M Data".

[i.3]	Open Geospatial Consortium.

NOTE:	Available at http://www.opengeospatial.org/.

[i.4]	Open Geospatial Consortium, Sensor Web Enablement DWG.

NOTE:	Available at http://www.opengeospatial.org/projects/groups/sensorwebdwg.

[i.5]	Open Geospatial Consortium, Sensor Web Enablement architecture, August 2008.

[i.6]	Open Geospatial Consortium, Observations and Measurements.

NOTE:	Available at http://www.opengeospatial.org/standards/om.

[i.7]	Open Geospatial Consortium, OpenGIS Sensor Model Language (SensorML).

NOTE:	Available at http://www.opengeospatial.org/standards/sensorml.

[i.8]	Open Geospatial Consortium, OpenGIS Transducer Markup Language (TML) Encoding Specification.

NOTE:	Available at http://www.opengeospatial.org/standards/tml.

[i.9]	Open Geospatial Consortium, Sensor Observation Service.

NOTE:	Available at http://www.opengeospatial.org/standards/sos.

[i.10]	Open Geospatial Consortium, Sensor Planning Service (SPS).

NOTE:	Available at http://www.opengeospatial.org/standards/sps.

[i.11]	Open Geospatial Consortium, Sensor Alert Service.

NOTE:	Available at http://www.opengeospatial.org/standards/requests/44.

[i.12]	W3C Semantic Sensor Network Incubator Group.

NOTE:	Available at http://www.w3.org/2005/Incubator/ssn/wiki/Main_Page.

[i.13]	Open Geospatial Consortium, Sensor Web Interface for IoT SWG.

NOTE:	Available at http://www.opengeospatial.org/projects/groups/sweiotswg.

[i.14]	Open Geospatial Consortium Best Practice, Semantic annotations in OGC standards.

NOTE:	Available at http://www.opengeospatial.org/node/1790.

[i.15]	Open Geospatial Consortium, Geography Markup Language.

NOTE:	Available at http://www.opengeospatial.org/standards/gml.

[i.16]	Semantic Sensor Network XG Final Report, W3C Incubator Group Report 28 June 2011.

NOTE:	Available at http://www.w3.org/2005/Incubator/ssn/XGR-ssn/.

[i.17]	Open Geospatial Consortium, Sensor Web Enablement DWG.

NOTE:	Available at http://www.opengeospatial.org/projects/groups/sensorwebdwg.

[i.18]	SSN Suggested Key Ontology Intro Attributes.

NOTE:	Available at http://www.w3.org/2005/Incubator/ssn/wiki/SSN_Suggested_Key_Ontology_Intro_Attributes.

[i.19]	W3C Semantic Sensor Network Incubator Group, Semantic Sensor Network Ontology.

NOTE	Available at http://www.w3.org/2005/Incubator/ssn/ssnx/ssn.

[i.20]	DUL ssn.

NOTE:	Available at http://www.w3.org/2005/Incubator/ssn/wiki/DUL_ssn.

[i.21]	HGI02029: "Smart Home Architecture and System Requirements".

[i.22]	W3C OWL Working Group, OWL 2 Web Ontology Language Document Overview.

NOTE:	Available at http://www.w3.org/TR/owl2-overview/.

[i.23]	W3C SPARQL Working Group, SPARQL 1.1 Overview.

NOTE:	Available at http://www.w3.org/TR/sparql11-overview/.

[i.24]	Jack Rusher, TripleStore, Semantic Web Advanced Development for Europe (SWAD-Europe), Workshop on Semantic Web Storage and Retrieval - Position Papers.

NOTE:	Available at http://www.w3.org/2001/sw/Europe/events/20031113-storage/positions/rusher.html.

[i.25]	oneM2M-TR-0001-UseCase: "oneM2M Use cases collection".

[i.26]	Resource Description Framework (RDF): "Concepts and Abstract Syntax".

NOTE:	Available at http://www.w3.org/TR/rdf-concepts/.

[i.27]	RDF Vocabulary Description Language 1.0: "RDF Schema".

NOTE:	Available at http://www.w3.org/TR/rdf-schema/.

[i.28]	SPARQL Query Language for RDF.

NOTE:	Available at http://www.w3.org/TR/rdf-sparql-query/.

[i.29]	Web Ontology Language (OWL).

NOTE:	Available at http://www.w3.org/2001/sw/wiki/OWL.

[i.30]	Dbpedia.

NOTE:	Available at http://dbpedia.org/About.

[i.31]	Turtle: Terse RDF Triple Language. Eric Prud'hommeaux and Gavin Carothers. W3C Last Call Working Draft, 10 July 2012.

NOTE:	Available at http://www.w3.org/TR/2012/WD-turtle-20120710/.
Latest version available at http://www.w3.org/TR/turtle/.

[i.32]	OWL Syntaxes.

NOTE:	Available at http://ontogenesis.knowledgeblog.org/88?kblog-transclude=2.

[i.33]	Rule Interchange Format (RIF) overview (second version).

NOTE:	Available at http://www.w3.org/TR/2013/NOTE-rif-overview-20130205/.

[i.34]	SWRL: A Semantic Web Rule Language Combining OWL and RuleML (Version 0.5).

NOTE:	Aavailable at http://www.daml.org/2003/11/swrl/.

[i.35]	SPIN - Overview and Motivation.

NOTE:	Available at http://www.w3.org/Submission/spin-overview/.

[i.36]	oneM2M Drafting Rules.

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

[i.37]	oneM2M TS 0002: "onM2M Requirements".

[i.38]	Broadband Forum TR-069: "CPE WAN Management Protocol v1.1".

[i.39]	oneM2M TS 0001: "oneM2M Functional Architecture".

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?