| CHANGE REQUEST |
| --- |
| Meeting:* | MAS 17 |
| Source:* | Modacom Co. (TTA) |
| Date:* | 2015-05-20 |
| Contact:* | Gyu Myoung Lee, <Modacom>, <gmlee@modacom.co.kr> Yongjin Kim, <Modacom>, <cap@modacom.co.kr> Woo Seop Rhee, <Modacom>, <wsrhee@modacom.co.kr> |
| Reason for Change/s:* | TR-007 text for 8.5.2 R01 addresses comments at MAS#17. R02 uses a template of CHANGE REQUEST and addresses additional comments at MAS#17. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0005 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0007V2.4.0 |
| Clauses/Sub Clauses* | Section 8.5.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Background

From the last TP-15, the MAS group started to discuss architectural issues considering oneM2M based on requirements analysis. Through several meetings, there were contributions related to a high-level architectural model as a starting point.

Modacom [1] proposed a way for oneM2M architectural design to support semantics. There are two basic considerations as shown in Figure 1: 1) Semantic Engine with semantic core functions and 2) Enhanced functionalities for Semantics.

Figure 1. Discussion for oneM2M architecture [1]

As a high-level architectural model for oneM2M semantics, Modacom proposed three different blocks for functional entities in the CSE.

- Semantic engine

- Semantic enabled functions

- Other functions in CSE

Similarly, NEC [2] proposed a similar architectural approach as shown in Figure 2. In the NEC contribution, more specifically the semantic enabled functions in Modacom contribution can be divided into the follwoing two groups:

- CSFs requiring semantic enhancement / adaptation

- CSFs possibly requiring semantic enhancement / adaption

NOTE – Probably we need further discussion for “possibly requiring” to make more clear candidate CSFs for semantic enhancement / adaption. Furthermore we should consider how to support semantics to exsiting CSFs from architectural persfective.

Figure 2. A proposal for Common Service Functions (CSFs) [2]

Although the MAS group is still discussing details of the new semantic engine CSF and additional roles of existing CSFs considering semantics, we believe that the MAS group has reached a consensus to adopt the new semantic engine CSF.

Based on our discussion, we need to start documantaion for architectural model and invite contributions for further architectural work in the ABS TR.

References

[1] MAS-2015-0005, “Proposals for Semantics Architecture from Requirements Analysis”

[2] MAS-2015-0528, “oneM2M Semantic CSF Functionality”

- Proposal

The ABS TR (v-2.4.0) has the section for architectural aspects (Section 8.5) to presents architectural recommendations for, or potential constraints to, the oneM2M architectural design. However, the section still remains blank to be filled.

Thefore, from the above backgroud, we propose to add the new text for oneM2M architectural design considering semanatics in Section 8.5.2 of the ABS TR (v-2.4.0) as follows.

### -----------------------Start of change 1 -------------------------------------------

## 8.5	Architectural Aspects

### 8.5.2	oneM2M architectural design considering semanatics

oneM2M architecture for the Common Service Layer in the M2M system specifies a Common Service Entity (CSE) with Common Services Functions (CSFs). The CSFs provide services to the Application Entities (AEs) via the Mca reference point and to other CSEs via the Mcc reference point. CSEs interact with the underlying Network Service Entity (NSE) via the Mcn reference point.

For supporting semantics in oneM2M architecture, core functionalities of semantics (i.e., semantic engine) should reside inside the CSE for interaciting the AEs via the Mca reference point and provide semantic interworking with other CSEs via the Mcc reference point. Then, oneM2M system can handle ontologies and semantic information through interacting with various CSFs in support of semantics engine in the CSE.

Figure X illustrate a high-level architectural model for semantics from the exsitng oneM2M architecture.

Figure X: A high-level architectural model for oneM2M semantics

The semantic related CSFs can be logically divided into the following groups:

- Semantic engine: The semantic engine provides core functionalilites in the generic functional model of Figure 11 to support semantics.

- Semantic enabled functions: Enhanced functionalities for semantics are required to exsiting CSFs through a direct link with semantic engine.

  - CSFs requiring semantic enhancement / adaptation: data management & repository, discovery, location

  - CSFs possibly requiring semantic enhancement / adaption: group management, registration, security, subscription and notification

### ----------------------- End of change 1 -------------------------------------------