| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#17 |
| Source:* | NTT |
| Date:* | 2015-05-18 |
| Contact:* | Yoshihisa Ito, NTT, ito.yoshihisa@lab.ntt.co.jp |
| Reason for Change/s:* | Propose an analysis of information model in ECHONET |
| CR against: Release* |  |
| CR against: WI* | Active <Work Item number> WI-0017 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0017 V.0.2.0 |
| Clauses/Sub Clauses* | 5.1, 5.2, 2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes an analysis of information model in ECHONET.

## -----------------------Start of change 1-------------------------------------------

### 5.1.3	ECHONET/ECHONET Lite  (ECHONET Consortium)

The ECHONET is an open communication proximity network protocol that supports smart house and Home Enegy Management System. The specification of the ECHONET is determined by the ECHONET Consortium[i.8]. ECHONET Lite[i.9]. has been released as a modiafication of the ECHONET mainly by removing the underlying network layer technology on the ECHONET.

ECHONET  specify  the information model called  “Deivce Object”[i.10].  Device Object represents the property sets for ECHONET devices.  Over 90 types of devices for device object  have been currently defined and been updated from time to time. An example of ECHONET device object  is shown as figure5.1 3-1.

Figure 5.1.3-1: Information Model in ECHONT Device Object

As shown in figure 5.1.3-1,  the device objects consist of  “Super Class” which represents common properties among all devices and “Device Class” which represents specific properties for its own device type (ex.washing machine, lighting, .. etc.).

## -----------------------End of change 1---------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 5.2.1	Design Principle: Approach 1

Based on the analysis work for the AllJoyn (section 5.1.1) , HomeKit  (section 5.1.2) and ECHONET (section 5.1.3), design principles of the abstract information model are as follows:

## -----------------------End of change 2---------------------------------------------

## -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

[i.8]   	ECHONET Specification Ver.2.11 (http://www.echonet.gr.jp/english/spec/spec_v211_e.htm)

[i.9]   	ECHONET Lite Specification Ver.1.11 (http://www.echonet.gr.jp/english/spec/spec_v111_lite_e.htm)

[i.10]   	ECHONET APPENDIX, Detailed Requirements for ECHONET Device Objects (http://www.echonet.gr.jp/english/spec/spec_app_f_e.htm)

## -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?