| CHANGE REQUEST |
| --- |
| Meeting:* | MAS 18 |
| Source:* | Martin Bauer, NEC Europe Ltd. (ETSI), martin.bauer@neclab.eu Joerg Swetina, NEC Europe Ltd. (ETSI), joerg.swetina@neclab.eu Ataru Kobayashi, NEC Corporation (TTC), a-kobayashi@df.jp.nec.com |
| Date:* | 2015-06-14 |
| Contact:* | Martin Bauer, NEC Europe Ltd. (ETSI), martin.bauer@neclab.eu |
| Reason for Change/s:* | Add semantic filter criteria, thus enabling semantic discovery. |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0007 and v2.5.1 |
| Clauses/Sub Clauses* | 8.5.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR introduces a semantic filter criteria for filtering resources based on their semantic description.In particular, the filter criteria enables the semantic discovery of resources based on the semantic description contained in the <semanticDescriptor> child resources.

This can be seen as a companion CR to ARC-2015-2019-SemanticFilterCriteria, which introduces the semantic filter criteria to TS-0001. In this TR-0007 contribution, there is a more detailed explanation and some examples based on (RDF) triples and SPARQL, which is at the moment not specified in TS-0001 – but it needs to be clarified, whether we want to specify this in Stage 2 or Stage 3.

### -----------------------Start of change 1-------------------------------------------

## 8.5	Architectural Aspects

### 8.5.4	Semantic Filtering and Discovery

In Section 8.5.3, the <semanticDescriptor> resource has been introduced. One of the key functionalities generating value from the semantic descriptions contained in such resources is enabling semantic filtering. Semantic filtering is especially relevant if an application wants to discover resources and specifies the characteristics of the resources it is interested in.

Previously, filtering has been supported by having filter criteria on attributes (see [i.1], Table 8.1.2-1). By adding support for <semanticDescriptor> child resources containing the semantic description, a filter criteria has to be added that pertains to this semantic descriptions. Table 8.5.4-1 shows the definition of the semantics filter criteria. There can be multiple instances, which according to the general semantics for evaluating filter criteria, means that an "OR" semantics applies, i.e. the overall result for the semantics filter criteria is true if one or more of the semantic filters matches the semantic description.

Table 8.5.4-1: semantics Filter Criteria

| semantics | 0..n | The semantic description contained in one of the <semanticDescriptor> child resources matches the specified semantic filter. |
| --- | --- | --- |

Since the representation of the semantic descriptions has not been specified in the architecture, the definition of the semantics filter criteria there remains on a high abstraction level as well. It has to be decided, whether the architecture description has to become more specific in this respect, or whether this is left for stage 3.

For the purpose of this technical report, the assumption is that the semantic descriptions are specified as RDF triples – in whatever representation, e.g. RDF/XML, Turtle. The semantics filter criteria can thus be specified as SPARQL requests that are executed on each of the semantic descriptions. The interpretation is that the semantic filter evaluates to true whenever the execution of the SPARQL request provides one or more results and false otherwise.

In the following,two examples are shown. The semantic descriptors are given as triples.For readability the ontology concepts and instances are shown with namespaces, but the namespace and prefix definitions are omitted. The entries are shown as subject-predicate-object triples, or domain- object property-range as used in the definition of OWL object properties.

Example 1: Filter for AE resources representing devices that measure temperature.

Semantic Descriptor of Device 1 AE

my:MyDevice1 			rdf:type 						base:Device

my:MyDevice 1			base:hasService 				my:MyService1

my:MyService1 			base:hasFunctionality 		my:MyFunctionality1

my:MyFunctionality1 	rdf:type	 					base:Measuring

my:MyFunctionality1 	base:refersTo					my:MyAspect1

my:myAspect1			rdf:type						aspect:Temperature

Semantic Descriptor of Device 2 AE

my:MyDevice2 			rdf:type 						base:Device

my:MyDevice2 			base:hasService 				my:MyService2

my:MyService2 			base:hasFunctionality 		my:myFunctionality2

my:myFunctionality2	rdf:type	 					base:Controlling

my:myFunctionality2	base:refersTo					my:myAspect2

my:myAspect2			rdf:type						aspect:Temperature

SPARQL Request 1

SELECT ?device

WHERE { ?device rdf:type base:Device .

?device base:hasService ?service .

?service base:hasFunctionality ?functionality .

?functionality rdf:type base:Measuring .

?functionality base:refersTo ?aspect .

?aspect rdf:type instance:Temperature  }

SPARQL Execution Results

(on  Device1 semantic description) --> my:myDevice1

(on Device 2 semantic description) --> empty

This means that the AE resource that is described by  my:myDevice1 will be included in the result set, whereas the AE resource described by my:MyDevice2 	will not be included.

Note, that the following SPARQL request would yield the same result in our case, but without checking whether the functionality is actually offered by a device (base:Device). The core concept identifying what is being represented by the resource (in this case a device) could be specified in the ontologyRef attribute.

SPARQL Request 2

SELECT ?functionality

WHERE {  ?functionality rdf:type base:Measuring .

?functionality base:refersTo ?aspect .

?aspect rdf:type instance:Temperature  }

SPARQL Execution Results

(on  Device1 semantic description) --> my:myDevice1

(on Device 2 semantic description) --> empty

Example 2: Filter for contentInstance resources that contain a temperature value in Celsius with an accuracy of +/- 1°C.

Semantic Descriptor of Temperature 1 contentInstance

my:myTemperature123			rdf:type						aspect:Temperature

my:myTemperature123			tempOnt:hasUnit				tempOnt:Celsius

my: myTemperature123			tempOnt:has Accuracy		0.9

Semantic Descriptor of Temperature 2 contentInstance

my:myTemperature234			rdf:type						aspect:Temperature

my:myTemperature234			tempOnt:hasUnit				tempOnt:Celsius

my: myTemperature234			tempOnt:has Accuracy		1.5

Semantic Descriptor of Temperature 3 contentInstance

my:myTemperature345			rdf:type						aspect:Temperature

my:myTemperature345			tempOnt:hasUnit				tempOnt:Fahrenheit

my: myTemperature345			tempOnt:has Accuracy		0.5

SPARQL Request

SELECT ?temperatureInstance

WHERE {  ?temperatureInstance rdf:type tempOnt:Temperature  .

?temperatureInstance tempOnt:hasUnit tempOnt:Celsius .

?temperatureInstance tempOnt:hasAccuracy ?accuracy

FILTER (?accuracy <= 1.0) }

SPARQL Execution Results

(on  Temperature1 description) --> my:myTemperature123

(on Temperature 2 description) --> empty  – not accurate enough

(on Temperature 3 description) --> empty – not in Celsius

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change n-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change n---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?