| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#19 |
| Source:* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| Date:* | 2015-09-07 |
| Contact:* | <name>, <company>, <contact info> |
| Reason for Change/s:* | Update of TS-0012 section 7.1.1 Instantiation of classes of the oneM2M Base Ontology Note, that agreement on modelling Operations in ARC is needed before concluding on this section. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0025 - Generic Interworking MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0012 v.0.4.1 |
| Clauses/Sub Clauses* | 7.1.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

<Provide an introduction containing the problem(s) being solved, and a summary list of proposals.  Discuss any risk of breaking backwards compatibility with last published version of the impacted TS.>

### -----------------------Start of change 1-------------------------------------------

### 7.1.1	Instantiation of classes of the oneM2M Base Ontology and derived external ontologies in the oneM2M System:

#### 7.1.1.1	General on instantiating classes of the Base Ontology in the oneM2M System

If a class of the Base Ontology (or a sub-class thereof) is instantiated in a oneM2M resource (i.e. <AE> or <Container> or <ContentInstance>) then this oneM2M resource shall have a child resource of type <SemanticDescriptor>.

That <SemanticDescriptor>  resource shall

- contain an instantiation of the class in the data of its descriptor attribute.

- contain an Ontology-Ref attribute that identifies the class in the referenced ontology

Editor’s Note: it is unclear if a Ontology-Ref is required.

- contain instantiations of Object- and Data Properties for which the class is a domain class.

#### 7.1.1.2	Instantiation of individual classes of the Base Ontology

- The Device class of the oneM2M Base Ontology (or a sub-class thereof) shall be instantiated in resources of type <AE> in the oneM2M System. The descriptor attribute of the related  <SemanticDescriptor> shall contain the RDF description of the Device instance:

Editor’s Note: need to provide RDF description of here,

Editor’s Note: need to be able to have a <Node> resource mapped to a Device

Note: Also the InterworkedDevice class of the oneM2M Base Ontology (or a sub-class) is instantiated as resources of type <AE>. However in this case the <AE> represents a “proxied” device, the application logic (APP-ID) is provided through the Interworking Proxy Entity (IPE).

- The AreaNetwork class (or a sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the InterworkedDevice class instance

- The Data Properties “anTechnologyCommunicationProtocol”, “anTechnologyPhysicalStandard” and “anTechnologyProfile” are instantiated in the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the InterworkedDevice class instance

- The Service class (or a sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the Device class instance

- The Functionality class (or sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the Device instance

- The Command class (or sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the Device instance

- The instantiation of an Object Property “isExposedByOperation” shall contain a reference to the resource of type <container/ Operation> that instantiates the Operation

- The Operation class (or sub-classes) shall be instantiated in a resource of type < container/ Operation> that is a child-resource of the <AE> that instantiates the Service. The descriptor attribute of the <SemanticDescriptor> child resource of the <container/Operation>  shall contain the RDF description of the Operation instance

  - The instantiation of an Object Property “exposesCommand” shall contain a reference to the resource of type <AE> that instantiates the Command

- The Input and Output class (or sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <container/Operation> of the Operation instance that is related via the “hasInput” / “hasOutput” Object Property

- The related Data Property “hasDataTypeAndRange” (that indicates the permissible data type and range of the content of the “Input” or “Output” instance) shall be instantiated in the the <SemanticDescriptor> child resource of the <container/Operation> of the Operation instance that is related via the “hasInput” / “hasOutput” Object Property.

- The OperationState class (or sub-class) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <container/Operation> of the Operation instance that is related via the “hasOperationState” Object Property

  - The related Data Property “hasDataTypeAndRange” (that indicates the permissible data type and range of the content of the “OperationState” instance) shall be instantiated in the the <SemanticDescriptor> child resource of the <container/Operation> of the Operation instance that is related via the “hasOperationState” Object Property.

- The Method class (or sub-classes) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <container/Operation> of the Operation instance.

Note: in the oneM2M System only the following instances of the Method class exist: CREATE, UPDATE, RETRIEVE

- The Target class (or sub-classes) shall be instantiated in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the < container/Operation > of the Operation instance.

The instance of the Target class related to the Operation class via the “hasTarget” Object Property shall contain a URI that is constructed as follows:

  - {Resource identifier of the < container/Operation> of the of the Operation instance}

- The instance of the Target class related to the Input- Output- or OperationState class via the “hasInputTarget” / “hasOutputTarget” / “hasOperationStateTarget” Object Property shall contain a URI that is constructed as follows:

  - {Resource identifier of an attribute / child-resource of the <container/Operation> of the Operation instance, specific to the Input- Output- or OperationState class}

Editor’s Note: all instantiations related to  Operation, Input/Output/State require agreement on modelling Opertations in ARC and are FFS.

- The Aspect class (or sub-classes) shall be instantiated either

- in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <AE> of the Device instance that contains the Functionality that refers to this Aspect

- or

- in the data of the descriptor attribute of the <SemanticDescriptor> child resource of the <container> of the Thing instance that contains the Value that concerns this Aspect

- The Thing class (or sub-classes) shall be instantiated in resources of type <container>. 
The descriptor attribute of the related  <SemanticDescriptor> shall contain the RDF description of the Thing instance

  - An instantiation of an Object Property “hasThingRelation” shall contain a reference to the resource (of type <container> in case of a Thing, of type <AE> in case of a Device) that instantiates the range class of the Object Property.

  - Note: this reference could refer to a resource of type <container> in case of relating to a Thing, or of type <AE> in case of a Device (as a sub-class of Thing)

- The Value class (or sub-classes) shall be instantiated in resources of type <container> as a child-resource of the resource to which it relates via the “hasThingProperty” Object Property.

- Note: this resource could be a resource of type <container> in case of relating to a Thing, or of type <AE> in case of a Device (as a sub-class of Thing)

- The descriptor attribute of the <SemanticDescriptor> child resource of the Value <container> shall contain the RDF description of the Value instance.

  - The related Data Property “hasDataTypeAndRange” (that indicates the permissible data type and range of the content of the “Value” instance) shall be instantiated in the the <SemanticDescriptor> child resource of the Value <container>.

  - The related Object Property “hasThingProperty” shall be instantiated in the descriptor attribute of the <SemanticDescriptor> of the <container> of the related “Thing” instance.

Note: the data of the Value instance can be accessed by the usual CRUDN operations

- The MetaData class (or sub-classes) shall be instantiated in the descriptor attribute of the <SemanticDescriptor>

- of the Value instance related via the “hasMetaData” Object Property

- or

- of the Aspect instance related via the “canHaveMetaData” Object Property

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change n-------------------------------------------

<If the text is new text, turn on "Track Changes" and start typing or paste the new text>

<If the CR is changing existing text.

- Select the text from the latest baseline TS or TR.

- Turn  "Track Changes" off.

- Paste the existing text from the baseline.

- Turn "Track Changes" on.

- Make the proposed changes.>

### -----------------------End of change n---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?