| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#19 |
| Source:* | Modacom |
| Date:* | 2015-08-30 |
| Contact:* | Gyu Myoung Lee, <Modacom>, <gmlee@modacom.co.kr> Yongjin Kim, <Modacom>, <cap@modacom.co.kr> Woo Seop Rhee, <Modacom>, <wsrhee@hanbat.ac.kr> Quyet H. Cao, <Institut Mines-Telecom>, <quyet.cao_huu@telecom-sudparis.eu> |
| Reason for Change/s:* | Introducing for common mapping principles between the Base Ontology and external ontologies |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0025 - Generic Interworking MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0012 v.0.4.1 |
| Clauses/Sub Clauses* | 7/7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

- Background

At the previous TP meetings, we had discussed mapping issues between the Base Ontology and external ontologies such as SAREF and SSN. Although there were several discussions for the preliminary text on mapping rules between Base Ontology and SAREF as an intial attempt, the text was not agreed as we need further discussion on this issues.

On the other hand, we had agreed to add the section (Section 7.2 in the TS-0012-V-0.4.1) for common mapping principles with various external ontologies before specifying mapping rules for a specific ontology at the last TP 18 meeting.

In this regards, we would like to identify important principles for ontology mapping for updating Section 7.2.

- Proposal

In this contribution, we propose 3 common mapping principles between the Base Ontology and external ontologies to update the Section 7.2 in the TS-0012 as follows. Based on this, we would like to further identify common mapping principles and invite relevant contributions to develop specific mapping rules for candidate external ontologies to map with the Base Ontolgy.

Reference

[1] OWL Web Ontology Language Reference, Available at http://www.w3.org/TR/owl-ref/

### -----------------------Start of change 1-------------------------------------------

# 7	Instantiation of the Base Ontology and external ontologies to the oneM2M System

## 7.2	Common mapping principles between the Base Ontology and external ontologies

The base ontology can be mapped to other external ontologies (e.g., SAREF, SSN, etc.).  The following priciples are applied for the mapping between ontologies:

- Principle 1 – Classes Mapping (owl:equivalentClass) :

- Making the statement X owl:equivalentClass Y essentially means that two named classes are synonymous, i.e. that all instances of class X are instances of class Y and vice versa.

- Using this principle, two classes specified in different ontologies are declared to be equivalent.

- Principle 2 – Properties Mapping (owl:equivalentProperty):

- The owl:equivalentProperty construct can be used to state that two properties have the same property extension. Syntactically, owl:equivalentProperty is a built-in OWL property with rdf:Property as both its domain and range.

- Using this principle, if two properties are declared to be equivalent, they relate an individual to the same set of other individuals.

- Principle 3 – Class Instances Mapping (owl:sameAs):

- The property owl:sameAs is used to state that two individuals (i.e. class instances) are the same.

- Using this principle, two class instances specified in different ontologies are declared to be equivalent.

### -----------------------End of change 1---------------------------------------------