| CHANGE REQUEST |
| --- |
| Meeting:* | MAS#19 |
| Source:* | KETI |
| Date:* | 2015-09-07 |
| Contact:* | Minwoo Ryu, Jaeho Kim, Sungchan Choi, Ting Martin Miao, KETI, minu@keti.re.kr |
| Reason for Change/s:* | Introducing semantic instances management functionality |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-5 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0007 V.2.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The current document introduces semantic instances management functionality which enables to provide basic operations for managing the semantic instance including create, update, delete etc. The operations to be provided by the semantic instance management functionality are mapped to oneM2M primitives. The semantic instance management functionality is recommended to be added in the section of Key functionalities for Semantics.

### -----------------------Start of change 1-------------------------------------------

### 7.1.2.12	Semantic Instances Management

#### 7.1.2.12.1	Overview

The management of semantic instances stored in the semantic descriptor resource shall be one of key functionalities for semantics especially when it comes to dealing with the create, update and delete operations against semantic instances. A simple way to deal with the update of semantic instances is to overwrite the whole semantic descriptor resource which might lead to data redundancy problem. An more efficient approach shall provide for handling the management of semantic instances. We propose a semantic instances management approach which is based on functionalities offered by SPARQL.

#### 7.1.2.12.2	SPARQL Update Language

SPARQL 1.1 specified by W3C is used to facilitate querying and manipulating RDF graph content on the Web or in a RDF store. A SPARQL update language is specified to support two categories of update operations on a Graph Store, i.e. Graph Update and Graph Management. In the current document, Graph Update is introduced to manage the addition or removal of triples from some graphs within the Graph Store. The introduction on Graphy Management is out of the scope of current document.

In the following subsections a list of graph update operations offered by SPARQL are introduced.

#### 7.1.2.12.2.1	INSERT DATA Operation

The INSERT DATA operation is typically used to add some new triples, given inline in the request, into a graph stored in the Graph Store. If the graph does not exist and it can not be created for any reason, then a failure MUST be returned.

The operation can be executed by running this command:  INSERT DATA triple_name  { GRAPH <g>  {PAYLOAD}}

where triple_name is the name of a graph into which you want to create new triples.

Many exeception cases can be handled such as:

- If the data with triple_name is requested to insert a graph that does not exist in the Graph Store, then the graph should be created if creation of a new graph is permitted, otherwise failure message will be responded.

- If the triple_name is NULL, then the default graph is presumed.

Examples are presented at Annex B to demonstrate how INSERT DATA operation works.

##### 7.1.2.12.2.2	DELETE DATA Operation

The DELETE DATA operation is responsible for removing some triples, given inline in the request, from a graph stored in the Graph Store.

The operation can be executed by running this command:  DELETE DATA triple_name  { GRAPH <g>  {PAYLOAD}}.

As with INSERT DATA, DELETE DATA is meant for deletion of ground triples which results in that triple_name that contains blank nodes is disallowed in DELETE DATA operations.

Examples are presented at Annex B to demonstrate how DELETE DATA operation works.

##### 7.1.2.12.2.3	DELETE/INSERT Operation

The DELETE/INSERT operation can be used to remove or add triples from/to the Graph Store based on bindings for a query pattern specified in a WHERE clause.  In other words, the DELETE/INSERT operation can be used to overwrite a specific triples stored in a Graph Store. According to the definition of DELETE/INSERT operation, DELETE and INSERT operation are executed sequently and if the DELETE clause is omitted then only INSERT operation only inserts data. Same action happens as INSERT operation is omitted.

In order to fit our requirement for updating (overwriting) a specific semantic instance, we assume that both DELETE/INSERT operation shall be executed sequently and guarantee that DELETE and INSERT are supposed to always be executed.

#### 7.1.2.12.3	SPARQL Graph Store HTTP Protocol

To achieve the goal of managing the semantic instance, SPARQL 1.1 shall enable to support the Hypertext Transfer Protocol (HTTP) for the distributed updating and fetching of RDF graph content stored in a Graph Store. To this end, assumptions on HTTP shall be made as follows:

- identification of resources via Request IRI (Internationalized Reference Identifier)and the IRI of a graph in a Graph Store,

- manipulation of resources through representations via the use of an RDF graph representation as input to RDF graph management actions, and

- self-describing messages via the inherent characteristics of RDF as the framework for a Self-Describing Semantic Web.

The Graph Store HTTP protocol specifies the semantics of HTTP operations for managing a Graph Store. In particular, it provides operations for removing, creating, and replacing RDF graph content as well as for adding RDF statements to existing RDF graph content.

Each graph requires an IRI to enable the control by the HTTP client. Within the graph store, each graph except the default graph shall be associated with a graph IRI.

#### 7.1.2.12.4	SPARQL Graph Management Operations

The current section introduces the use of the HTTP verbs to determine the operation performed on RDF content. In the case of an operation that manages the default graph, the SPARQL Update operation will not include any mention of a graph while in the case of an operation that manages a specific graph, the identity  <graph_uri> can be understood to be either the request IRI or the IRI indirectly specified visa the query components.

Assumptions on the HTTP header

#### 7.1.2.12.4.1	HTTP PUT

A SPARQL HTTP Put request is mapped to oneM2M CREATE request primitive and store the enclosed RDF payload as RDF graph content.

The operation can be executed by running this command:

- Case1: a specific graph is targeted by <graph_uri>

PUT / oneM2M/semanticDescriptor?graph=_graph_uri_.. HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DROP SILENT GRAPH <graph_uri>;

INSERT DATA { GRAPH <graph_uri> { .. RDF payload .. } }

- Case2: the default graph is targeted

PUT / oneM2M/semanticDescriptor?default HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DROP SILENT DEFAULT;

INSERT DATA { .. RDF payload .. }

#### 7.1.2.12.4.2	HTTP POST

A SPARQL HTTP POST request is mapped to oneM2M UPDATE request primitive and used to merge the enclosed RDF payload into the RDF graph content identified by the request or encoded IRI.

The operation can be executed by running this command:

- Case1: a specific graph is targeted by <graph_uri>

POST / oneM2M/semanticDescriptor?graph=_graph_uri_.. HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DELETE DATA { GRAPH <graph_uri> { .. RDF payload 1.. } }

INSERT DATA { GRAPH <graph_uri> { .. RDF payload 2.. } }

- Case2: the default graph is targeted

POST / oneM2M/semanticDescriptor?default HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DELETE DATA { { .. RDF payload 1.. } }

INSERT DATA { { .. RDF payload 2.. } }

#### 7.1.2.12.4.3	HTTP DELETE

A SPARQL HTTP DELETE request is mapped to oneM2M DELETE request primitive and used to delete the RDF graph content identified by the request or encoded IRI. If there is no such RDF graph content that you request to remove in the Graph Store, the client will be responded with 404 Not Found messge.

The operation can be executed by running this command:

- Case1: a specific graph is targeted by <graph_uri>

DELETE / oneM2M/semanticDescriptor?graph=_graph_uri_.. HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DROP SILENT GRAPH <graph_uri>;

DELETE DATA { GRAPH <graph_uri> { .. RDF payload .. } }

- Case2: the default graph is targeted

DELETE / oneM2M/semanticDescriptor?default HTTP/1.1

Host: host_name_

Content-Type: text/turtle

... #RDF payload ...

DROP SILENT DEFAULT;

DELETE DATA { { .. RDF payload .. } }

### -----------------------End of change 1---------------------------------------------