## Slide 1: HGI oneM2M Presentation SDT (Smart Device Template)
Lindsay Frost, NEC
Andreas Kraft, DT
August 2015

## Slide 2: Introduction

## Slide 3: Smart Home Gateway:
HOME GATEWAY
3
D1
D2
D3
Dx
Abstraction Layer
RP2
Remote Access Agent
App 1
App N
…
RP4
Remote Access Middleware
RPx
RP1
High-level API
for
Application Developers
Driver-level Bindings
Translation to and from
Technology-specific
Aspects using SDT

## Slide 4: Goals of a Device Model Template
Easy to understand and to use
  Appliance manufacturers and domain specific orgs should not need much expertise to use it
  There must not be a need for specialized niche tools (which are typically expensive too)
  Application developers can make use of a small set of common functional elements, not adapting API code for every HAN
Comprehensive
  Template is able to express all operational information that is need to operate a specific device type
  Extensible with upcoming new requirements
Suitable for target machines
  Formal language can be effectively processed on constrained devices
4
SDT: (Apache 2.0) DEVICE MODELS RWD050
Notes: "What is a template" for the few people who have not heard it

## Slide 5: Main Idea: re-usable XML modules for describing most common functions
Power Switch (for my music box)
Description for Applications (and Programmers)
Data Model (XML)
Features,
Attributes, Info about internal states, ....
Constraints
a boolean actuator (like power switch)
a real-value sensor (like temperature sensor)
a boolean sensor (like window sensor)
Template modules of XML for
Application developers can make use of a small set of common functional elements, not adapting API code for every HAN
App
HGI offers a library of "module" elements, which conform to the ModuleClass, for the most common functions
SDT XSD

## Slide 6: SDT Version 2

## Slide 7: SDT 2.0 – UML overview
Shows details of the "constraints" implied in previous page
Documentation on each element: https://github.com/Homegateway

## Slide 8: SDT 2 Elements - Domain
Domain is the top-level component that defines all ModuleClasses and Devices of a domain.
A Domain can import definitions from other domains.
A Domain can define Modules or RootDevices, or both.
<Domain xmlns:xi="http://www.w3.org/2001/XInclude"
xmlns="http://homegatewayinitiative.org/xml/dal/2.0"
id="org.homegatewayinitiative">
<Imports>
<xi:include href="./dal-core.xml" parse="xml" />
</Imports>
<Modules>
<!-- List of Domain global Modules goes here -->
</Modules>
<RootDevices>
<!-- List of RootDevices goes here -->
</RootDevices>
</Domain>

## Slide 9: SDT 2 Elements - RootDevice
RootDevice is the definition of a physical device that may contain optional embedded sub-devices.
For each physical device on the network at least one RootDevice must be defined.
If the RootDevice is a simple device it does not include further Devices. On the other hand, if the device is a compound device, ie. it does contain embedded devices, the RootDevice defines Devices for each of the identifiable embedded devices.

## Slide 10: SDT 2 Elements - RootDevice
<RootDevice id="aRootDevice">
<Doc>Some documentation</Doc>
<Modules>
<!-- List of Modules local to the RootDevice goes here-->
</Modules>
<DeviceInfo>
<!-- The DeviceInfos for the RootDevice goes here-->
</DeviceInfo>
<Devices>
<!-- List of Sub-Devices of the RootDevice goes here-->
</Devices>
</RootDevice>
RootDevices may define own ModuleClasses or refer to predefined ModulesClasses of the same or another Domain.

## Slide 11: SDT 2 Elements - Device
Devices are optional components of a RootDevice. They represent sub-devices inside a RootDevice.
Devices may define their own ModuleClasses or extend ModulesClasses of its or another Domain.
<Device id="aDevice">
<Doc>Some documentation</Doc>
<Modules>
<!-- List of Modules local to the Device goes here-->
</Modules>
<DeviceInfo>
<!-- The DeviceInfo for the Device goes here-->
</DeviceInfo>
</RootDevice>

## Slide 12: SDT 2 Elements – ModuleClass
The ModuleClass represents the concept of a reusable module that defines the Actions, Data and Events for a single functionality of a device.
A connected device may contain or refer to single or multiple ModuleClasses to specify its inherent services it exposes.
Modules are instantiations of ModuleClasses.
ModuleClasses can be defined by a Domain or in RootDevices/Devices.

## Slide 13: SDT 2 Elements – ModuleClass
ModuleClasses defined on the Domain level can be imported, extended and used by other Domains.
New ModuleClasses can be defined by extending existing ModuleClasses from the same or other domains to add new or overriding defined Actions, Data and Events.
<ModuleClass name="BooleanState">
<Doc>Some documentation</Doc>
<Actions>
<!-- List of Actions goes here-->
</Actions>
<Events>
<!-- List of Events goes here-->
</Events
<Data>
<!-- List of DataPoints goes here-->
</Data>
</ModuleClass>

## Slide 14: SDT Version 3 Work in Progress

## Slide 15: Contributions & Comments

## Slide 16: Agreed Enhancements
Rename RootDevice/Device
  RootDevice → Device
  Device → SubDevice
Optional Components
  Reduce the number of all possible combinations
  ModuleClass, Action, Event, DataPoint

## Slide 17: Agreed Enhancements
Composite DataType
  Structs
  Arrays
Unit of Measures
  Provide base of conversation for DataTypes
  Use UCUM (Unified Code for Units of Measure)
  Conversion from applications to technologies may be performed by a DAL implementation.
Constraints
  Help to ensure the integrity of data in the underlying data model
  Addition to DataType

## Slide 18: Enhancements under discussion
Arbitrary Device MetaData instead of continuously extended DeviceInfo
  To better support semantic attributes for device capabilities
Roles
  Support technology and organizational indicated roles (e.g. client/server models)
Versioning
  Indicate the presence of different version of ModuleClasses / Capabilities
  Semantic versioning (Major.Minor.Patch)
Aggregate ModuleClasses within ModuleClasses
  Single inheritance already exists

## Slide 19: SDT 3.0 Beta - Basic Elements

## Slide 20: SDT 3.0 Beta - DataType

## Slide 21: Thank You!
Contacts
Lindsay.Frost@neclab.eu
A.Kraft@telekom.de
Duncan.Bees@homegatewayinitiative.org

## Slide 22: Backup Example Device Explained (SDT 2)

## Slide 23: Example of Appliance: "multi-socket electrical-extension-block"

## Slide 24: Example of Appliance: "multi-socket electrical-extension-block"
<?xml version="1.0" encoding="iso-8859-1"?>
<Domain xmlns:xi="http://www.w3.org/2001/XInclude"
xmlns="http://homegatewayinitiative.org/xml/dal/2.0"
id="org.homegatewayinitiative">
<!-- The following import statements include ModuleClasses from HGI,
for example, "BooleanState". -->
<Imports>
<xi:include href="./dal-core.xml" parse="xml" />
</Imports>

## Slide 25: Example of Appliance: "multi-socket electrical-extension-block"
<Modules>
<ModuleClass name="BooleanStateRD">
<Doc><tt>BooleanState</tt> is the preferred module for modelling a functionality corresponding to an underlying binary state. This module should be used to abstract away from the actual datatype and values in question. Note that the module does not define whether the execution mode is blocking or non-blocking.</Doc>
<Actions>
<Action name="get" type="boolean">
<Doc>Obtain the current associated state.</Doc>
</Action>
<Action name="setTarget">
<Doc>Set the state to the specified value.</Doc>
<Arg name="value" type="boolean">
<Doc>The desired value of the associated state.</Doc>
</Arg>
</Action>
</Actions>
<Events>
<Event name="stateChanged">
<Data>
<DataPoint name="state" type="boolean">
</DataPoint>
</Data>
</Event>
</Events>
</ModuleClass>
</Modules>

## Slide 26: Example of Appliance: "multi-socket electrical-extension-block"
<RootDevices>
<RootDevice id="MSEEB.root">
<DeviceInfo>
<Name>Multi Socket Electrical-Extension-Block</Name>
<Vendor>HGI</Vendor>
<FirmwareVersion>1.0</FirmwareVersion>
<VendorURL>http://www.homegatewayinitative.org</VendorURL>
<SerialNumber>1234.5</SerialNumber>
</DeviceInfo>
<Doc>This device is intended as a demonstration of how to
define a Root Device with multiple sub-devices.</Doc>

## Slide 27: Example of Appliance: "multi-socket electrical-extension-block"
<Modules>
<Module name="rootPowerOnOff">
<extends domain="org.homegatewayinitiative" class="BooleanStateRD"/>
<Doc>The proprietary interface for turning all switches of the extension block on and off. The action "BooleanState:get“ returns "true" when any of the sub-devices is in the state "on", otherwise it returns "false".</Doc>
</Module>
<Module name="extensionBlockDataPoints">
<Data>
<DataPoint name="firmwareVersion"
type="string"
writable="false">
<Doc>This datapoint represents the firmware version of the extension block.</Doc>
</DataPoint>
<DataPoint name="powerSwitchNames"
type="array"
writable="false">
<Doc>This datapoint is an array of strings with the names of the contained devices.</Doc>
</DataPoint>
</Data>
</Module>
</Modules>

## Slide 28: Example of Appliance: "multi-socket electrical-extension-block"
<Devices>
<Device id="switch.power.1">
<DeviceInfo>
<Name>PowerSwitch 1</Name>
<Vendor>HGI</Vendor>
</DeviceInfo>
<Doc>This sub-device is intended as a demonstration of how to use the abstract modules defined in the <em>HGI Core</em> domain.</Doc>
<Modules>
<Module name="switch">
<extends domain="hgi.dal.core" class="BooleanState"/>
</Module>
</Modules>
</Device>
<Device id="switch.power.2">
<DeviceInfo>
<Name>PowerSwitch 2</Name>
<Vendor>HGI</Vendor>
</DeviceInfo>
<Doc>This sub-device is intended as a demonstration of how to use the abstract modules defined in the <em>HGI Core</em> domain.</Doc>
<Modules>
<Module name="toggleSwitch">
<extends domain="hgi.dal.core" class="BooleanState"/>
<Actions>
<Action name="toggle">
<Doc>Toggle the associated state between True and False.</Doc>
</Action>
</Actions>
</Module>
</Modules>
</Device>
</Devices>

## Slide 29: Example of Appliance: "multi-socket electrical-extension-block"
</RootDevice>
</RootDevices>
</Domain>