## Slide 1: HAIM Data Model Issues
Group Name: MAS WG
Source: Bob Flynn, Convida Wireless (Seed.Dale@ConvidaWireless.com)
Meeting Date: 2018-07-15 (MAS36)
MAS-2017-0110-HAIM_Data_Model_issues.ppt
Notes: Other suggested titles:
“Benefits of oneM2M Standardization”

## Slide 2: Introduction
TS-0023 defines the HAIM model and many specific devices for the Home domain
Several parties are developing implementation of HAIM entities
There are questions about the intended call flows and API, as exposed to a user of the HAIM device
oneM2M is starting to develop similar models for other Verticals, therefore these questions should be addressed early before developing more specification on solutions that need some more definitions

## Slide 3: HAIM Model of Lightbulb

## Slide 4: Simple Device Light Resource Overview
All HAIM resources (red boxes) are specializations of <flexContainer> resources
Datapoints are mapped as a [customAttribute] of <flexContainer> resource
deviceLight
binarySwitch
toggle
Device
Module
Action
PowerState:Boolean
Datapoint

## Slide 5: 4 ways the IN-AE turns the light on
Message charts from Ian Sharpe, ATIS

## Slide 6: Problem Statement #1
In each of the 4 ways to turn the light on, the state of the system is different
This means that an application developed to support a HAIM lightbulb MUST be able to support ALL 4 approaches
High complexity for Application developers
This is not consistent with the goal of oneM2M – but we are really close!

## Slide 7: Proposal
Define a desired interface (from the IN-AE perspective) that the HAIM model should expose, for example:
  When an IN-AE want to change the state of a binary switch it uses the “toggle” action module. The user can issue one of three action commands:
    Turn the Light On
    Turn the Light Off
    Toggle the current state of the Light
  When the toggle action is issued, an OK response is generated regardless of the result of the action when the HAIM device successfully receives the command
  The HAIM device updates the state of the device in the “PowerState” custom attribute associated with the “action” module
  The DataPoint Attribute is ReadOnly for the IN-AE
These definitions require the following changes
  “Toggle” Action Module needs a custom attribute with values (ON, OFF, TOGGLE)
    This eliminates the defect regarding the “empty” update
  Specification that a “Blocking-Update” subscription is used because of “when the HAIM device successfully receives the command”
  Specification that the HAIM device must update a “DataPoint” based on statechanges triggered by an “Action” Module
  Clarification that “Command/Control” of a HAIM device is achieved through the “Action” Module and “State” is determined through the “DataPoint” attributes and that “client” applications of the HAIM device shall not WRITE the “DataPoint” attributes

## Slide 8: Problem Statement #2
Generally Speaking, a retrieve of information about a device is reflected in a oneM2M resource. For example, to determine if the light is on, read the “powerState” attribute
  However, a reasonable use case is a desire to force a request to directly address the device for the desired information.
  We cannot do this in oneM2M right now
Requirements
  A method to indicate in a Request that the CSE should “Go to the Device for this Retrieve”
    Similar to rcn=7 (Original Resource)
  A Retrieve retargeting method
    When the RETRIEVE request is received, the response to the originator should wait for a response from the device, and provide the data from the NoDN in the response message.
Proposal

## Slide 9: Why is this important?
  oneM2M should give application developers more end-to-end transparency so that they are able to get information directly from the device
      E.g. If a device, like a lightbulb, hosts the device state then the state needs to be available through a RESTful interface
  Provide more flexibility and optimization needed for some oneM2M deployments.
      E.g. For interworking oneM2M with other RESTful technologies that allow devices to host their own resources.
      E.g. Deployments requiring lower end-to-end latency request handling
  Examples of some other RESTful technologies that allow device apps to host their own resources include OCF, LWM2M, many CoAP based IoT deployments
ADN-AE
AE
MN-CSE
IPE
NoDN
MN-CSE
AE
NoDN
MN-CSE
AE
- MN-CSE Retargeting to AE / IPE / NoDN
Same interface can be used for all of these deployment options