| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 - Protocols |
| Title:* | CoAP Analysis Update |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Contact: | francois.ennesser@gemalto.com |
| Date:* | <2013-10-14> |
| Abstract:* | Add precisions on security to Section 7 of the Protocol Analysis document: That dealing with the CoAP Protocol |
| Agenda Item:* | Protocol Analysis |
| Work item(s): |  |
| Document(s) Impacted* | M2M Protocol Analysis Technical Report |
| Intended purpose of document:* | xx Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Replacement of Section 7.1 with the text contained herein. That section dealing with the analysis of the CoAP Protocol. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

We suggest the following additions (in revision marks below) to Section 7.1 of the Protocol Analysis TR, as highlighted below (2 additions in 7.1.9 “Security” and one in 7.2.11.2 “Constraints”).

## 7.1	CoAP - Constrained Application Protocol

- […]

### 7.1.9	Security

As CoAP realizes a subset of the features in HTTP/1.1, the security considerations of [RFC2616] are also pertinent to CoAP. This section analyzes the possible threats to the protocol.  There are a number of security limitations with CoAP, and this section will describe those in detail.  These will include:

- Protocol Parsing, Processing URIs

- Proxying and Caching

- Risk of amplification

- IP Address Spoofing Attacks

- Cross-Protocol Attacks

- Constrained node considerations

COAP uses DTLS1.2 and security keys generated by DTLS are used to protect CoAP level messages. Some constraints associated with DTLS are as follows:

- It may be challenging to support DTLS in constrained M2M devices that have limited memory (such as RAM ~ 10 KB) and processing power. This is the reason for the current IETF initiative “DTLS In Constrained Environments” (DICE) initiative (http://www.ietf.org/proceedings/87/slides/slides-87-dice-0)

- Use of DTLS (handshake protocol) results in high overhead in the network and that may not be desirable.

- No clear standardized definition of a constrained DTLS profile

- No efficient support of multicast with IP DTLS. The multicast suitability of CoAP are lost when using DTLS (point-to-point). On this aspect, there are also initiatives attempting  to find solutions, e.g. “DTLS-based multicast security for Low power Lossy Networks” (http://tools.ietf.org/id/draft-keoh-tls-multicast-security-00.txt)

- No standardized approaches for (dynamic) key management for group based communication

### 7.1.11	Benefits and Constraints

#### 7.1.11.1  Benefits

- It is a lightweight application layer protocol designed for constrained devices (such as devices with 8-bit microcontroller and limited memory) and constrained  networks (such as low power, low data rate, lossy networks that use IEEE802.15.4)

- It runs over UDP and avoids overhead of TCP

- It is easy to do HTTP – CoAP translation

Editor’s Note: To be completed

#### Constraints

- Constraints associated with DTLS (as listed in the Security subsection)

- No standardized framework for authorization and access control for CoAP exists as of now. The IETF draft “Access Control Framework for constrained environments” (http://datatracker.ietf.org/doc/draft-selander-core-access-control/?include_text=1)  attempts to resolve this issue.

- No explicit support for real-time IoT application at present.

Editor’s Note: To be completed