| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO WG |
| Title:* | MQTT protocol binding TS baseline – v 0.1.0 sections 5 and 6 |
| Source:* | MQTT protocol binding TS rapporteur |
| Contact: | Peter Niblett, peter_niblett@uk.ibm.com |
| Date:* | 2014-02-19 |
| Abstract:* | This proposes some content for TS-0010, the oneM2M MQTT protocol binding. Changes in R01 Modifications requested at TP-9 PRO meeting (e.g. splitting the old 5.2.1 pattern into two) Using more normative language (and changing must to shall) A few editorial corrections |
| Agenda Item:* | TBD |
| Work item(s): | WI 0014 – MQTT Protocol Binding |
| Document(s) Impacted* | TS-0010 MQTT Protocol Binding Technical Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to make the attached v0.1.0 draft as the oneM2M MQTT binding TS baseline. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 5.1	Use of MQTT

This clause profiles the way that the MQTT protocol is used by the Binding. For more information on MQTT itself see Appendix A or refer to the MQTT specification [1].

MQTT includes reliability features which allow recovery from loss of network connectivity without requiring explicit involvement of the applications that are using it, however to do this it requires an

MQTT requires an underlying network protocol that provides ordered, lossless, bi-directional connections, but the MQTT specification [1] does not mandate a particular underlying protocol. For the purposes of the current specification, we restrict the choice of underlying protocol: it shall be one of the following:

- Raw TCP/IP [3]

- TCP/IP with Transport Level Security (TLS)  [4]

- WebSocket [5] – either with or without the use of TLS

The binding makes use of MQTT to provide reliable two-way communications between two parties (AEs and CSEs). It uses the following features of MQTT:

- Durable Sessions, providing Store and Forward in cases where network connectivity is not available

- MQTT’s “QoS 1” message reliability level. This provides reliability without incurring the overhead implied by QoS 2.

- NAT traversal (neither of the two parties is required to have prior knowledge of the other party’s IP address)

- Dynamic topic creation and wild-carded subscription filters

It does not use the following features:

- One-to-many publish/subscribe

- Retained Messages

- Will Messages

- QoS 0 or QoS 2 message reliability levels

## Binding overview

The MQTT protocol binding specifies how the Mca or Mcc request and response messages are transported across the MQTT protocol. Both communicating parties (AEs and CSEs) typically make use of an MQTT client library, and the communications are mediated via the MQTT server.  There is no need for the client libraries or the server to be provided by the same supplier, since the protocol they use to talk to each other is defined by the MQTT specification [1].

Furthermore, the binding does not assume that the MQTT client libraries or server implementations are necessarily aware that they are being used to carry Mca, Mcc or any other oneM2M-defined primitives.

The binding is defined in terms of the MQTT protocol flows that take place between the client libraries and the MQTT server in order to effect the transport of an Mca or Mcc message

The next four sections show the four configurations in which the MQTT binding can be used

Note: Other configurations are possible, but they are currently out of scope (this is FFS).

### 5.2.1		AE to IN

This configuration, illustrated in Figure 5.1, allows an AE to connect to an IN via MQTT.

Figure 5.1 Using MQTT between AE and IN-CSE

The MQTT server is co-located with the IN-CSE and allows connection of the ADN-AEs (typically devices) and/or IN-AEs.   It can store and forward messages if there’s a gap in the connectivity with the devices. Note that the AEs each establish their own separate TCP/IP connection with the MQTT server. Thus the server must have an accessible IP address, but AEs need not have.

### 5.2.2		AE to MN

This configuration, illustrated in Figure 5.2, allows an ADN-AE to connect to an IN via MQTT.

Figure 5.2 Using MQTT between AE and MN-CSE

### This configuration is very similar to the AE-IN configuration shown in 5.2.1, except that the MQTT server is hosted on the MN rather than the IN.  Onwards connection to the IN-CSE is via a different transport protocol.

### 5.2.3		MN to IN

This configuration, illustrated in Figure 5.3, allows an MN to connect to an IN via MQTT.

Figure 5.3 Mcc using MQTT between MN and IN

The MQTT server is co-located with the IN-CSE and allows connection of the MNs (typically in-field gateway boxes).   It can store and forward messages if there’s a gap in the connectivity with the gateways. Note that the MNs each establish their own separate TCP/IP connections with the MQTT server. Thus the server must have an accessible IP address, but MNs need not have.

### 5.2.4		AE to MN to IN

This configuration, illustrated in Figure 5.4, is a combination of the previous two.

Figure 5.4 Mca and Mcc both using MQTT

In this configuration the two MQTT servers are independent from each other (that is to say they don’t have a shared topic space). Any interactions between the ADN-AE and the IN-CSE are mediated by the MN-CSE.

# 6	Protocol Binding

In this section we define the key elements of the binding:

- How a CSE or AE connects to MQTT

- How an Originator (CSE or AE) formulates a Request as an MQTT message, and transmits it to its intended Receiver

- How a Receiver listens for incoming Requests, and how it formulates and transmits a Response

- How the Mca and Mcc CRUD operations map to MQTT messages

## Connecting to MQTT

- In order to communicate, the two client parties (AE and CSE or CSE and CSE) shall connect to a common MQTT server. The MQTT server shall be hosted in one of the two nodes, following one of the configuration patterns shown in clause 5.2

NOTE: Other configuration patterns are FFS.

Once each party has located the address of the MQTT server, it then connects to it using the standard MQTT Connect protocol packet.  The following additional considerations apply:

- The Connect packet contains a Client Id as described in section A.3.2. The Client Ids have to be unique at least among all clients that connect to a given MQTT server instance (this is a requirement imposed by the MQTT protocol). This condition will be satisfied if an AE uses its App-Inst-ID and a CSE uses its CSE-ID. See Clause 7 of TS-0001 [2] for a discussion of these Identifiers. The prefix A:: or C:: shall be added to the ID to show whether it is an App-Inst-ID or a CSE-ID as these ID spaces are not distinct.

- A client shall set the “Clean Session” flag in the Connect Packet to false. This means that MQTT Session state related to that client will be retained by the MQTT Server in the event of a disconnection (deliberate or otherwise) of that client.

- A client shall not set the “Will Flag”, so Will Messages are not enabled

- A client may choose to provide a non-zero MQTT KeepAlive value or to provide a KeepAlive of 0 (this disables the MQTT KeepAlive)

NOTE: An Infrastructure Provider might wish to specify and enforce a policy that sets a lower bound on the KeepAlive that can be used on portions of its network. The mechanisms for this are FFS.

- The MQTT server may require that a client provides a User Name and a password (or other credential). For more information see Clause 7.

NOTE: We might want to use the Will Message to allow a client’s connection status to be tracked. This is FFS.

NOTE: Also FFS is a discussion of connection strategy, for example a client might choose to keep the MQTT connection open permanently (restarting it as soon as possible after any unforeseen connection loss), it might choose to connect only when it wants to act as an Originator, or it might choose to connect on some kind of schedule.

Once a client has connected to the MQTT server it can then communicate (subject to authorisation policies) with any other client connected to its server. There is no need for it to create another connection if it wants to communicate with a different counter-party.

When a client determines that it no longer wishes to participate in an MQTT Session with its MQTT Server it shall perform the following steps:

- Disconnect from that server, if it is currently connected

- Reconnect with the cleanSession flag set to true

- Disconnect again

These steps delete any state that the MQTT server might be holding on behalf of the client.

## Sending and Receiving Messages

### 6.2.1 	Request and Response Messages

MQTT does not have a data model to describe or constrain the content of its Application Message payloads (to that extent it is similar to a TCP socket).  Mca and Mcc request messages shall be serialized into XML following the serialization process defined in the Core Protocol specification [3].

Since oneM2M messages are idempotent, they should be sent with MQTT QoS 1.

Note: MQTT messages are subjected to a theoretical maximum message size of 256M, but it is good practice not to send messages that are bigger than a few Megabytes. If a larger amount of data needs to be sent, it should be segmented into multiple messages.

NOTE: This is FFS and is something that might need to be addressed in the Core Protocol specification

### 6.2.2 	Sending a Request

A request is transmitted by sending it as an MQTT Publish protocol packet to the MQTT Server. It uses a Topic that identifies the Receiver of the request. The precise structure of this Topic is FFS, but an initial suggestion is:

/oneM2M/req/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the target resource (it is assumed that this includes the AE or CSE id)

- “req” is a literal string identifying this as a request.

NOTE: It might be useful to include some other components in the topic name, such as the Operation type. In particular it might be useful to include a <fr> field for security purposes. This is FFS

### 6.2.3 	Listening for and responding to a Request

A Receiver listens for requests arriving via MQTT by subscribing to its Topic (as described in the previous section).

When it receives a request, the receiver shall check the request expiration timestamp (if any) contained in the request, since it is possible that that time might have passed while the message was being stored by MQTT.

It then transmits a response by sending an MQTT Publish packet to a response topic. This takes the form

/oneM2M/resp/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the originator of the request (or the rd information from the request)

- “resp” is a literal string identifying this as a response.

The originator (or other interested party) must subscribe to this topic if it is to see the response.

### Mapping the CRUD operations

Each MQTT message bearing a oneM2M Request shall contain the  <op> parameter to indicate whether it is a Create, Read, Update or Delete. The topic used indicates target resource ID. In the case or Read, Update or Delete this is straightforward, as there should be a resource already in existence. In the case of Create, the Originator will publish to a topic that hasn’t previously been used, so in order to see that (and thus be able to process the Create), the CSE will subscribe using the wildcarded topic filter /oneM2M/req/#.