| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#9.2 |
| Title:* | Design principle |
| Source:* | Barbara Pareglio, NEC (Barbara.pareglio@neclab.eu) |
| Contact: |  |
| Date:* | 2014-03-7 |
| Abstract:* | Introduce all the attributes from the architecture document |
| Agenda Item:* | Input contribution |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | oneM2M-TS-0004-Protocols-V-0.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Below are samples of the styles to be used in this document

- Introduction

Added and introduction section for the design principle in order to introduce what a primitive is, what is the expectation of designing an API and what is included in this document.

- Proposal

The contribution proposes to add an introduction chapter and to modify a bit the design principle. The proposal is also to change SHOULD to SHALL where applicable.

================================= START 1st CHANGE =================================

## Resource Attributes specified in oneM2M

OneM2M system shall support the Attributes described in the following clauses. All resource attributes are specified in [6].

## Resource attributes

Resource Attributes are defined and described in [6].The type and values shall be supported according to the description given in table 6.1.1.1-1.

The attributes are specified by trhe following information in the table:

- Attribute Name: indicates the name of the Attribute from [6]

- Short Name: indicates the acronym for the correspondent Attribute

- Data type: indicate the used type for the attribute, simple data types are defined in section 6.2.1 and complex data types are defined in section 6.2.2.

- Default: specifies the default value of the attribute as set by hosting CSE if no specific value was provided in the operation CREATE or UPDATE request, or if the provided value was unacceptable for the hosting CSE. In all those cases the hosting CSE is allowed to set a value.

- Value restrictions: indicates if the value of the attributes has a specific limitation.

.

Table 6.1.1.1-1	Resource attributes

| Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- |
| [objectAttribute] |  |  |  |  |  |
| accessControlPolicyID | aRI | xs:string | NONE If the attribute is absent, all the entities that correspond to ancestor resources shall have the full set of permissions | See TBD |  |
| activate |  |  |  |  |  |
| activateStatus |  |  |  |  |  |
| aggregationURI |  | xs:anyURI |  |  |  |
| announceAttribute | aA | xs:string | NONE |  |  |
| announceTo | aT | xs:anyURI | NONE |  |  |
| App-ID |  | xs:string |  |  |  |
| App-Inst-ID |  | xs:string |  |  |  |
| applicableEventCategory | aEC |  |  |  |  |
| areaNwkId |  |  |  |  |  |
| areaNwkType |  |  |  |  |  |
| attached |  |  |  |  |  |
| backOffParameters | bOP |  |  |  |  |
| batchNotify |  |  |  |  |  |
| batteryLevel |  |  |  |  |  |
| batteryStatus |  |  |  |  |  |
| capabilityActionStatus |  |  |  |  |  |
| capabilityName |  |  |  |  |  |
| channelHandle |  |  |  |  |  |
| cmdType |  |  |  |  |  |
| collectedEntityID |  |  |  |  |  |
| collectingEntityID |  |  |  |  |  |
| collectPeriod |  |  |  |  |  |
| consistencyStrategy | cS |  |  |  |  |
| content | c | Content | NONE |  |  |
| content | ? | ? |  |  |  |
| contentSixe | cS | xs:long | Set by the CSE to the actual size of the received content of the instance |  |  |
| creationTime | cT | xs:dateTime | Generated by the hosting SCE. The value is set to the actual time of creation of the resource. |  |  |
| creator | cr | xs:anyURI | Generated by the hosting |  |  |
| cseBase | bRt | xs:anyURI |  |  |  |
| CSE-ID |  | xs:string |  |  |  |
| cseType | csT | TBD |  |  |  |
| currentByteSize | nb | xs:long | Set to the actual number of bytes of data stored in the Container resource | Limited by maxByteSize attribute of the same container resource |  |
| currentNrOfInstances | ni | xs:long | Set to the actual number of instances resource in the Container | Limited by maxNrOfInstances attribute of the same container resource |  |
| currentNrOfMembers | nM | xs:long |  |  |  |
| data |  |  |  |  |  |
| dataSize |  |  |  |  |  |
| deactivate |  |  |  |  |  |
| defaultDelAggregation |  |  |  |  |  |
| defaultOpExecTime |  |  |  |  |  |
| defaultRequestExpTime | dRqET |  |  |  |  |
| defaultRespPersistence |  |  |  |  |  |
| defaultResultExpTime | dRsET |  |  |  |  |
| defEcValue | dev |  |  |  |  |
| deliveryMetaData |  |  |  |  |  |
| description |  | xs:string |  |  |  |
| deviceLabel |  |  |  |  |  |
| deviceType |  |  |  |  |  |
| devId |  |  |  |  |  |
| devType |  |  |  |  |  |
| disable |  |  |  |  |  |
| enable |  |  |  |  |  |
| eventCat |  |  |  |  |  |
| eventEnd |  |  |  |  |  |
| eventID |  |  |  |  |  |
| eventID |  |  |  |  |  |
| eventStart |  |  |  |  |  |
| eventType |  |  |  |  |  |
| execDelay |  |  |  |  |  |
| execDisable |  |  |  |  |  |
| execEnable |  |  |  |  |  |
| execFrequency |  |  |  |  |  |
| execMode |  |  |  |  |  |
| execNumber |  |  |  |  |  |
| execReqArgs |  |  |  |  |  |
| execResult |  |  |  |  |  |
| execStatus |  |  |  |  |  |
| execTarget |  |  |  |  |  |
| expirationTime | eT | xs:dateTime | Default determined by CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |  |  |
| factoryReset |  |  |  |  |  |
| filterCriteria |  | FilterCriteria |  |  |  |
| fwVersion |  |  |  |  |  |
| groupName | gN | xs:string | NONE |  |  |
| hostedCSEID |  | Link |  |  |  |
| hwVersion |  |  |  |  |  |
| install |  |  |  |  |  |
| installStatus |  |  |  |  |  |
| interimEventNotify |  |  |  |  |  |
| labels | lBs | xs:string | NONE |  |  |
| lastModifiedTime | lMT | xs:dateTime | NONE |  |  |
| latest | lt | xs:anyURI | Set by the CSE to the URI of the latest added instance resource to the container | Limited to the URI of the instances resources in the container |  |
| latestNotify |  |  |  |  |  |
| lifespan |  |  |  |  |  |
| limitsDelAggregation | lDA |  |  |  |  |
| limitsOpExecTime | lOET |  |  |  |  |
| limitsRequestExpTime | lRqET |  |  |  |  |
| limitsRespPersistence | lRP |  |  |  |  |
| limitsResultExpTime | lRsET |  |  |  |  |
| link | ln | Link | NONE |  |  |
| listOfDevices |  |  |  |  |  |
| listOfNeighbors |  |  |  |  |  |
| locationContainerID |  | xs:anyURI |  |  |  |
| locationContainerName |  | xs:string |  |  |  |
| locationID | LID | xs:anyURI | NONE |  |  |
| locationServer |  |  |  |  |  |
| locationSource |  |  |  |  |  |
| locationTargetId |  |  |  |  |  |
| locationUpdatePeriod |  |  |  |  |  |
| logActionStatus |  |  |  |  |  |
| logData |  |  |  |  |  |
| logStart |  |  |  |  |  |
| logStop |  |  |  |  |  |
| logTypeId |  |  |  |  |  |
| manufacturer |  |  |  |  |  |
| maxBufferSize | mBS |  |  |  |  |
| maxByteSize | mb | xs:long | Default determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |  |  |
| maxInstanceAge | ma | xs:duration | Default determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |  |  |
| maxNrOfInstances | mi | xs:long | Default determined by CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |  |  |
| maxNrOfMembers | nM | xs:long | Default determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |  |  |
| memAvailable |  |  |  |  |  |
| memberAccessRightID | mAR | xs:string |  |  |  |
| memberList |  | AnyURIList |  |  |  |
| memberType | mT | MemberType | NONE |  |  |
| memberTypeValidated | mTV | xs:boolean | NONE |  |  |
| memTotal |  |  |  |  |  |
| metaInformation |  |  |  |  |  |
| mgmtDefinition |  | xs:string |  |  |  |
| minReqVolume | mRV |  |  |  |  |
| model |  |  |  |  |  |
| name |  | xs:string |  |  |  |
| nodeID |  | Link |  |  |  |
| nodeLink |  | Link |  |  |  |
| notificationDeliveryPriority |  |  |  |  |  |
| notificationEventCat |  |  |  |  |  |
| notificationStoragePriority |  |  |  |  |  |
| notificationStructure |  |  |  |  |  |
| notificationURI |  | xs:anyURI |  |  |  |
| objectID |  | xs:anyURI |  |  |  |
| objectPath |  |  |  |  |  |
| ontologyRef |  | xs:anyURI |  |  |  |
| operation |  |  |  |  |  |
| operationCounter |  |  |  |  |  |
| operationResult |  |  |  |  |  |
| order | or |  |  |  |  |
| originator |  |  |  |  |  |
| otherConditions |  |  |  |  |  |
| parentID | pID | xs:anyURI | NONE | See TBD |  |
| pointOfAccess | pOA | AnyURIList |  |  |  |
| priorSubscriptionNotify |  |  |  |  |  |
| privileges | ps | Privileges |  |  |  |
| rateLimit |  |  |  |  |  |
| reboot |  |  |  |  |  |
| requestCharacteristics |  |  |  |  |  |
| requestContentNotification |  |  |  |  |  |
| requestContext | rctxt |  |  |  |  |
| requestEventCategory | IEC |  |  |  |  |
| requestOrigin | roig |  |  |  |  |
| requestReachability |  | xs:boolean |  |  |  |
| requestStatus |  |  |  |  |  |
| resourceType | rT | ResourceType | NONE | See TBD |  |
| scheduleElement |  | Schedule |  |  |  |
| selfPrivileges | sP | Privileges |  |  |  |
| sleepDuration |  |  |  |  |  |
| sleepInterval |  |  |  |  |  |
| source |  |  |  |  |  |
| statModel |  |  |  |  |  |
| statsCollectID |  |  |  |  |  |
| status |  | xs:boolean | TRUE = active, FALSE=inactive |  |  |
| status | ?? | ?? | Editor’s note: this is a different status of active/inactive |  |  |
| storagePriority | sP |  |  |  |  |
| subscriberID |  |  |  |  |  |
| subsGroup |  |  |  |  |  |
| subsSer&RoleList |  |  |  |  |  |
| supportedResourceType | sRT | SupporteResourceType |  |  |  |
| target |  |  |  |  |  |
| target |  |  |  |  |  |
| targetNetwork | tNet |  |  |  |  |
| transactionType |  |  |  |  |  |
| Trigger-Recipient-ID |  | TBD |  |  |  |
| typeOfContent | tOC | ContentType | NONE |  |  |
| update |  |  |  |  |  |
| updateStatus |  |  |  |  |  |
| URL |  | xs:anyURI |  |  |  |
| version |  |  |  |  |  |
| versionTag | vT | xs:nonNegativeInteger | 0 |  |  |

  - Editor’s Note: The attributes listed in the table are examples and FFS.

  - Editor's Note:  How to choose the local time zone at timestamp is FFS.

================================= END 1st CHANGE =================================

# Comments

Or define the complex type with 2 value