| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3(Protocol WG) |
| Title:* | HTTP Protocol Bindings basic flow |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-04-08 |
| Abstract:* | This contribution proposed definitions of Actors R01: reflect offline comments given. R02: reflect comments given (removing security related behavior, and clean up texts regarding registration for notification) R03: further comments are given form NEC&InterDigital |
| Agenda Item:* | HTTP Binding TS |
| Work item(s): | WI-0013 |
| Document(s) Impacted* | TS-0009 (HTTP Protocol Binding) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG3 members should agree on proposal. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Fundamental part of HTTP protocol binding should be discussed based on proposed basic flow.

--- START OF CHANGES ---

# 5.	Overview

This clause describes fundamental procedures which are required o CSE, when it processes requests for performing CRUD+N operations against ‘oneM2M Resource’, using ‘HTTP-REST binding’.The CSE implements the mechanism to accept Notification messages on behalf of the AE. This mechanism is enabled with ‘AE Registration’ at the begging of the system use.

The Local CSE also works to guard of the oneM2M system against unauthorized access from AEs, such as DoS attacks. The CSE will heck the identity of an AE, and should allow the request to operate upon only from successfully registered AE.
Editor’s Note: definition and explaination of local CSE need to revised.

The issued request on ‘HTTP-REST binding’ sshould be processed in one of two ways. There is ‘Blocking Request’ and ‘Non-Blocking Request’. The targeted CSEshould return a final result for ‘Blocking Request’ as an HTTP responses, and it should not return a final result for ‘Non-Blocking Request’. In case of ‘Non-blocking Request’ , the targeted CSE should return a response only if the request is accepted (e.g. ‘202 Accepted’ status) or not, then Originator should fetch the final result of the request when the request were completed.

## 5.1	Actors

--- END OF CHANGES ---