| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Device Triggering for 3GPP |
| Source:* | NEC, NTT Docomo, Intel |
| Contact: | Barbara Pareglio (Barbara.Pareglio@neclab.eu) , Tetsuo Inoue (t-inoue@fp.jp.nec.com) , Syed Husain (shusain2016@gmail.com) , Puneet Jain, Intel, puneet.jain@intel.com |
| Date:* | 2014-04-09 |
| Abstract:* | The contribution provide a mapping of the commands for Device Triggering on Tsp interface of 3GPP |
| Agenda Item:* | Input Contribution |
| Work item(s): |  |
| Document(s) Impacted* | TS-0004 v0.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree to include the new clauses in the TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

Right now the template of the TS does not include any clause that should contain underlying network specific interfaces and how to map oneM2M information into features/interfaces from the underlying network.

2	Proposal

This contribution proposes to add new clauses that cover only Device Triggering feature for 3GPP network by means of Tsp.

### -----------------------Start of change 1-------------------------------------------

## X.Y	Device Triggering

## X.Y.1 Providing Device Triggering service by means of 3GPP networks

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP [TS 23.682]. The specification for the interface Tsp is described in [TS 29.368]. Tsp interface uses Diameter Base Protocol as specified in [IETF RFC 3588], in order to use such an interface the CSE shall act as a Diameter client as described in [RFC 6733].

## X.Y.1.1 Device Action Request command

When a CSE needs to issue a device triggering request from MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (see [TS 29.368]). Following tables provide an overview of the parameters and the parameter values needed for the DAR command.

Note: the values of the parameters indicated in the “Value” column need to be mapped to the specific 3GPP data type

Table x.y.1.1-1: AVPs in Device Action Request (DAR) command

| AVP name | AVP description | 3GPP Data Type | AVP (Attribute Value Pair) Code | Value |
| --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [RFC 3588]) | UTF8String | 263 | CSE implementation specific |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [TS 29.368 caluse 6.1.3] | Enumerated | 274 | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and according to [TS 29.368] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | NO_STATE_MAINTAINED (see [TS 29.368]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [RFC 3588]) | DiamIdent | 264 | CSE implementation specific |
| Origin-Realm | It identifies the Realm of the originator of theDiameter message (see [RFC 3588]) | DiamIdent | 296 | CSE implementation specific |
| Destination-Realm | It identifies the realm the message is to be routed to. (see [RFC 3588]) | DiamIdent | 283 | Domain Identifier part from M2M-Ext-ID |
| Destination-Host | The absence of the Destination-Host causes the message to be sent to any Diameter server supporting the application within the specified realm. (see [RFC 3588]) | DiamIdent | 293 | NULL |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [RFC 3588]) | Unsigned32 | 278 | CSE implementation specific |
| Device-Action | It contains the specific action for the device (see [TS 29.368]) | Grouped | 3001 | Specific format described in table x.y.1.1-2 |
| Proxy-Info | It’s a grouped AVP which provides the proxy state and host (see [RFC 3588]) | Grouped | 284 | CSE implementation specific |
| Route-Record | The identity added in this AVP is be the same as the one received in the Origin-Host (see [RFC 3588]) | DiamIdent | 282 | Not applicable |

Table x.y.1.1-2: AVPs in Device Action AVP (Grouped AVP)

| AVP name | AVP description | 3GPP Data Type | AVP Code | Value |
| --- | --- | --- | --- | --- |
| External-Id | It is the identifier of the device as specified in [TS 29.336] | UTF8String | 3111 | M2M-Ext-ID |
| MSISDN | It is the identifier of the device as specified in [TS 29.329] | OctetString | 701 | M2M-Ext-ID |
| SCS-Identifier | It identifies the CSE issuing the request (see [TS 29.368]) | OctetString | 3104 | CSE-ID |
| Reference-number | It uniquely identifies a transaction (see [TS 29.368]) | Unsigned32 | 3007 | CSE implementation specific Editor’s note: possibility to maybe use M2M-Request-ID is FFS |
| Action-Type | It informs the MTC-IWF of the required action | Enumerated | 3005 | 1 (Device Trigger Request) |
| Trigger-Data |  | Grouped | 3003 | See table x.y.1.1-3 |
| Validity-Time | The validity time in seconds for the specific action requested. (see [TS 29.368]) | Unsigned32 | 448 | CSE implementation specific |

NOTE: either external-Id or MSISDN shall be used, not both.

Table x.y.1.1-3: AVPs in Trigger Data AVP (Grouped AVP)

| AVP name | AVP description | 3GPP Data Type | AVP Code | Value |
| --- | --- | --- | --- | --- |
| Payload | It contains the payload to be transferred to the addressed device. (see [TS 29.368]) | OctetString | 3004 | NULL Furhter values can be defined (FFS) Editor’s Note: in the current TS-0001does not specify how to use payload. |
| Priority-Indication | It identifies priority of the device trigger. (see [TS 29.368]) | Enumerated | 3006 | CSE implementation specific (possible values are 0 or 1) |
| Application-Port-Identifier | It uniquely identifies the triggering entity addressed in the device. (see [TS 29.368]) | Unsigned32 | 3010 | Trigger-Recipient-ID |

## X.Y.1.2 Device Action Answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (see [TS 29.368]). The relevant parameters for a CSE are the following ones:

- Result-Code AVP: see [RFC 3588] for detail.

- Session-Id AVP: see [RFC 3588] for detail.

- Other AVPs for Diameter Base Protocol: see [RFC 3588] for detail.

Following AVPs are set in Device-Notification AVP (Grouped AVP):

- Either MSISDN or External-Id: the CSE shall check that the identifier of the target CSE is correct.

- SCS-Identifier: the CSE shall check that the value corresponds to its CSE-ID.

- Reference-Number: the CSE can use this value for correlating the DAA with the corresponding Device-Action-Request command issued previously by the CSE.

- Action-Type: the CSE shall check that the value is se to 1 (Trigger Request) as same value of DAR command;

- Request-Status: see table x.y.1.2-1 for the list of possible value.

Table x.y.1.2-1: Result Status

| Result-Satatus value | name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that device action requested is confirmed. |
| 201 | TEMPORARYERROR | See [TS 29.368] for detail. |
| 101 | INVALIDPAYLOAD | See [TS 29.368] for detail. |
| 102 | INVEXTID | See [TS 29.368] for detail. |
| 103 | INVSCSID | See [TS 29.368] for detail. |
| 104 | INVPERIOD | See [TS 29.368] for detail. |
| 105 | NOTAUTHORIZED | See [TS 29.368] for detail. |
| 106 | SERVICEUNAVAILABLE | See [TS 29.368] for detail. |
| 107 | PERMANENTERROR | See [TS 29.368] for detail. |
| 108 | QUOTAEXCEEDED | See [TS 29.368] for detail. |
| 109 | RATEEXCEEDED | See [TS 29.368] for detail. |

## X.Y.1.3 Device Notification Request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (see [TS 29.368]). The relevant parameters for a CSE are the following ones:

- Result-Code: see [RFC 3588] for detail.

- Session-Id AVP: see [RFC 3588] for detail.

- Other AVPs for Diameter Base Protocol: see [RFC 3588] for detail.

- Following AVPs are set in Device-Notification AVP (Grouped AVP):

- Either MSISDN or External-Id: the CSE shall check that the identifier of the target CSE is correct.

- SCS-Identifier: the CSE shall check that the value corresponds to its CSE-ID.

- Reference-Number: the CSE can use this value for correlating the DNR with the corresponding Device-Action-Request command issued previously by the CSE.

- Action-Type: the CSE shall check that the value is se to 2 (Delivery Report);

- Delivery-Outcome: see table x.y.1.2-2 for the list of possible value

Table x.y.1.3-1: Delivery Outcome

| Delivery-Outcome value | name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that the device action request was successfully completed. |
| 1 | EXPIRED | See [TS 29.368] for detail. |
| 2 | TEMPORARYERROR | See [TS 29.368] for detail. |
| 3 | UNDELIVERABLE | See [TS 29.368] for detail. |
| 4 | UNCONFIRMED | See [TS 29.368] for detail. |

## X.Y.1.4 Device Notification Answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (see [TS 29.368]). The relevant parameters for a CSE are the following ones:

- Auth-Application-ID: set to 16777309  as indicated in in [TS 29.368])

- Auth-Session-State: set to NO_STATE_MAINTAINED as indicated in [TS 29.368]

- Other AVPs for Diameter Base Protocol: see [RFC 3588] for detail, the value of such AVP is CSE implementation specific.

### -----------------------End of change 1---------------------------------------------

# Comments

3gpp does not specify  for MSISDN what it is.

CSE implementation specific for MSISDN case.