| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#10 |
| Title:* | primitives |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-3-28 |
| Abstract:* | The contribution provides description to primitives in oneM2M. |
| Agenda Item:* | TBD |
| Work item(s): | WI0009 |
| Document(s) Impacted* | TS0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into TS0004 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# 8	Primitives

## 8.1	Introduction

Primitives are service layer messages transmitted over the Mca and Mcc reference points. The Create, Update, Retrieve, Delete and Notify method is mapped to one or more primitives. The primitive is then further mapped to transportation layer protocols such as HTTP, CoAP or MQTT for the transmission. The primitive is independent from the transportation protocols.

Figure 8.1-1: primitive overview

The Originator sends requests to Receiver through primitives. The Originator may be AE or CSE. The Receiver may be a CSE. The primitive is addressing one of the resources residing in the CSE by carrying the URI of the resource. The Receiver then further determines if it needs to act as an Originator to forward the primitive to another Receiver, or it needs to handle the primitive and send a response back.

The CRUD+N method shall each consists of one request/indication and one response/confirm primitives.

Communication between an originator and a receiver in the method domain shall be performed with the following primitives: request, indication, response and confirm;

Communication between an originator and a receiver in the transport domain shall be performed using a data transfer function;

## 8.2	Primitives modelling

Primitives shall be are modelled as follows:

A primitive shall be a data structure that describes with appropriate attributes a specific procedure request or answer in both originator and receiver entities;

A primitive shall consist of:

Control part: contains attributes required for the processing of the request or response.

Optional payload part: description of user data. This is usually the representation of the resource or the value of the attribute in partial addressing case;

A request primitive shall contain the attribute "to" in order to provide the destination where to deliver the mapped specific protocol message;

The request and the indication shall be modelled as one primitive called "requestIndication" which is used in two directions (incoming and outgoing);

The response and the confirm shall be modelled as one primitive called "responseConfirm" which is used in two directions (incoming and outgoing).

Figure 8.1-2: Primitives modelling

## 8.3	Primitive principles

Primitives shall be atomic. When two concurrent primitives affect the same resource directly, one primitive shall finish completely before the second one starts. This ensures, for example, that a primitive execution can validate the existence of a resource, and then in later execution of that primitive be assured that the resource was not removed by another primitive executing at the same time.

The primitives for CRUD methods shall be addressing certain resources by addressing the URI of the resource. When create of update the resource, the representation the resource shall be contained in the Payload part of the primitive. Base on the representation of the resource, the Hosting CSE of the addressed resource can create or update the whole resource without further information needed.

The handling of primitives shall be idempotent. Which means no matter how many times the same primitive are targeted to the same resource, the resource shall not change after the first handling of the primitive.