| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Identifiers |
| Source:* | Barbara Pareglio, NEC, Barbara.pareglio@neclab.eu |
| Contact: |  |
| Date:* | 2014-03-28 |
| Abstract:* | Propose to add a section in the TS to cover the identifiers |
| Agenda Item:* | Input Contribution |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 v0.3.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree to include the new clauses in the TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

Right now the template of the TS does not include any clause about the identifiers that are defined in TS-001.

2	Proposal

This contribution proposes to add new clauses that cover the identifiers and the data format.

### -----------------------Start of change 1-------------------------------------------

# oneM2M Protocols / API Overview

## Introduction

This technical specification describes message formats and procedures to communicate with oneM2M compliant M2M Platform System.

This specification describes:

- Data representation for communication protocol messages

- Normal and exceptional procedure

- Status codes

- Guidelines for drafting APIs

## M2M Identifiers

## This clause describes all identifiers from [6] and the data types used to represent them.

Table 6.2-1: M2M Identifiers

| Identifier | Data Type | Description | Examples |
| --- | --- | --- | --- |
| M2M-SP-ID | String or AnyType | It is a globally unique ID that identifies the M2M Service Provider. The definition and assignment of such an ID is outside the scope of oneM2M | <M2M-SP-ID>SP.X.Y</M2M-SP-ID> |
| App-ID | String | It identifies the application outside of oneM2M, in general it is identified with the application name. The definition and assignment of such an ID is outside the scope of oneM2M | <App-ID>myApp</App-ID> |
| App-Inst-ID | AnyURI See clause X.X | It is a globally unique ID that identifies a specific instance of an AE. The definition and assignment of such an ID is in scope of oneM2M. Clause XXX describes how this identifier is assigned to an instance of AE. | <App-Inst-ID> uri:123455</App-Inst-ID> |
| CSE-ID | AnyURI See clause X.X | It is a globally unique ID that identifies a specific instance of a CSE. The definition and assignment of such an ID is in scope of oneM2M Clause XXX describes how this identifier is assigned to an instance of CSE. | <CSE-ID> uri:56478</CSE-ID> |
| M2M-Node-ID | OctectString See clause X.X | It is a globally unique ID that identifies the M2M Node. The definition and assignment of such an ID is outside the scope of oneM2M. |  |
| M2M-Sub-ID | AnyURI | It is a globally unique ID that identifies the M2M Subscriber. The definition and assignment of such an ID is in scope of an M2M Service Provider and it is therefore outside the scope of oneM2M. | <M2M-Sub-ID>uri:4338448</M2M-Sub-ID> |
| M2M-Request-ID | unsignInt or long? | It is a unique ID that identifies the single request, such an ID is required to be global an all reference point with the exception of the Mca, where the ID is only required to be unique within the CSE where the AE sends the request. Then if the request needs to be sent further the receiving CSE shall add it only CSE-ID to it. |  |
| M2M-Ext-ID | ExternalID See X.Y | It is an ID used by the M2M Service Provider to identify the CSE-ID for requesting services from an underlying network that are addressing the CSE-ID. A single CSE-ID may have several M2M-Ext-IDs, one for each underlying network. It is required to be unique within the used underlying network. |  |
| UNetwork-ID | AnyURI | It is a unique ID withing the M2M Service Provider domain and it identifies the specific underlying network. | <UNetwork-ID>uri: 666</UNetwork-ID> |
| Trigger-Recipient-ID | TBD | It is unique only within the execution environment of the device. It represents the CSE that is the target of the device triggering service requested from the underlying network. |  |
| M2M-Serv-ID | TBD | It is unique only within a M2M Service Provider domain. It identify the service offered by the M2M Service Provider. |  |

## Data Types and Definitions

For wide acceptance by industrial markets, this specification describes structured and non-structured data for oneM2M Protocol using XML Schema Language (aka XSD)[3].

Note that the actual data format is depends on chosen Protocol Bindings. Each protocol binding specification will specify the mapping rule between XSD version of data definitions and its native data format.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## Data Types use in oneM2M

This clause defines the complex data types that are used by oneM2M API.

6.3.1.1 ExternalID

This type represents the M2M-Ext-ID.

# Table 6.3.1.1-1

| Name | Type | Description |
| --- | --- | --- |
| UNetwork-ID | AnyURI | The identifier of the underlying network provider for which the external Identifier can be used. |
| Id | AnyURI | The identifier of the node for the underlying network provider |

### -----------------------End of change 2---------------------------------------------