| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Identifiers |
| Source:* | Barbara Pareglio, NEC, Barbara.pareglio@neclab.eu |
| Contact: |  |
| Date:* | 2014-03-28 |
| Abstract:* | Propose to add a section in the TS to cover the identifiers |
| Agenda Item:* | Input Contribution |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 v0.3.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree to include the new clauses in the TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

Right now the template of the TS does not include any clause about the identifiers that are defined in TS-001.

2	Proposal

This contribution proposes to add new clauses that cover the identifiers and the data format.

After discussion the following points have been changed:

- Description of the IDs refers to TS-0001 for the moment since it can still change.

- Created a common data type for the IDs, but not defined for the moment

### -----------------------Start of change 1-------------------------------------------

# oneM2M Protocols / API Overview

## Introduction

This technical specification describes message formats and procedures to communicate with oneM2M compliant M2M Platform System.

This specification describes:

- Data representation for communication protocol messages

- Normal and exceptional procedure

- Status codes

- Guidelines for drafting APIs

## M2M Identifiers

## This clause describes all identifiers from [6] and the data types used to represent them.

Table 6.2-1: M2M Identifiers

| Identifier | Data Type | Description | Examples |
| --- | --- | --- | --- |
| M2M-SP-ID | M2M-Id See clause X.X | It is a globally unique ID as defined in [6] | SP.X.Y |
| App-ID | M2M-Id See clause X.X | The Identifier is defined in [6] | myApp |
| AE-ID | M2M-IdSee clause X.X | It is a globally unique ID as defined in [6] | 123455 |
| CSE-ID | M2M-IdSee clause X.X | It is a globally unique ID as defined in [6] | 56478 |
| M2M-Node-ID | M2M-Id See clause X.X | It is a globally unique ID as defined in [6] |  |
| M2M-Sub-ID | M2M-Id See clause X.X | It is a globally unique ID as defined in [6]. | 4338448 |
| M2M-Request-ID | M2M-Id See clause X.X | It is a unique ID as defined in [6] |  |
| M2M-Ext-ID | ExternalID See 6.3.1.1 | The identifier is defined in [6] |  |
| UNetwork-ID | M2M-ID See clause X.X | It is a unique ID as defined in [6] | 666 |
| Trigger-Recipient-ID | TBD See clause X.X | It is as defined in [6] |  |
| M2M-Serv-ID | TBD | It is defined in [6] |  |

## Data Types and Definitions

For wide acceptance by industrial markets, this specification describes structured and non-structured data for oneM2M Protocol using XML Schema Language (aka XSD)[3].

Note that the actual data format is depends on chosen Protocol Bindings. Each protocol binding specification will specify the mapping rule between XSD version of data definitions and its native data format.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## Data Types use in oneM2M

This clause defines the complex data types that are used by oneM2M API.

6.3.1.1 ExternalID

This type represents the M2M-Ext-ID.

# Table 6.3.1.1-1

| Name | Type | Description |
| --- | --- | --- |
| UNetwork-ID | M2M-Id | The identifier of the underlying network provider for which the external Identifier can be used. |
| Id | AnyURI | The identifier of the node for the underlying network provider |

6.3.1.1 M2M-Id

TBD.

### -----------------------End of change 2---------------------------------------------