| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#10.0 |
| Title:* | Stage 3 text for <mgmtCmd> |
| Source:* | InterDigital |
| Contact: | Catalina Mladin, InterDigital, catalina.mladin@interdigital.com Phil Brown, InterDigital, phil.brown@interdigital.com |
| Date:* | 2014-04-07 |
| Abstract:* | Contribution proposes Stage 3 resource, primitive and procedure definitions for <mgmtCmd> |
| Agenda Item:* | 6. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Note: Yellow highlighting indicates text that is already part of TS-0004 v0.3.0

### -----------------------Start of proposed text 1 -------------------------------------------

### 6.3.4	<mgmtCmd> Resources and Procedures

#### 6.3.4.1	<mgmtCmd> Resource

The <mgmtCmd> resource shall contain the following child resource and attributes.

Table 6.3.4.1-1: mgmtCmd resource description

| Attribute Names | Presence in createReq | Presence in updateReq | Presence in response | Description |
| --- | --- | --- | --- | --- |
| execInstanceReference | NP | NP | M | Reference to child resource created by the hosting CSE when the parent is created |
| resourceType (rT) | M | n/a | M | See table 6.2.3.1-1 |
| parentID (pID) | M | n/a | M | See table 6.2.3.1-1 |
| expirationTime | M | n/a | M | See table 6.2.3.1-1 |
| accessControlPolicyID | O | n/a | O | See table 6.2.3.1-1 |
| labels | O | O | O | See table 6.2.3.1-1 |
| creationTime | NP | NP | M | See table 6.2.3.1-1 |
| lastModifiedTime | NP | NP | M | See table 6.2.3.1-1 |
| link | M | n/a | M | See table 6.2.3.1-1 |
| announceTo | M | n/a | M | See table 6.2.3.1-1 |
| announcedAttribute | M | n/a | M | See table 6.2.3.1-1 |
| cmdType | M | O | M | See table 6.3.4.1-2 |
| execEnable | M | NP | M | See table 6.3.4.1-2 |
| description | O | O | O | See table 6.3.4.1-2 |
| execReqArgs | O | O | O | See table 6.3.4.1-2 |

Table 6.3.4.1-2: Description of mgmtCmd specific attributes

| Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- |
| cmdType | N/A | xs:enumeration | TBD | "RESET" "REBOOT" "UPLOAD" "DOWNLOAD" "SCHEDULEDOWNLOAD" "SCHEDULEINFORM" "SCHEDULEDUCHANGE" |  |
| execEnable | N/A | xs:string | TBD | TBD |  |
| description | N/A | xs:string | NONE | TBD |  |
| execReqArgs | N/A | xs:anytype | TBD | NONE |  |

#### 6.3.4.2	<mgmtCmd> Primitives and Procedures

##### 6.3.4.2.1	mgmtCmdCreate

###### 6.3.4.2.1.1	mgmtCmdCreateRequest

This procedure is used for creating an <mgmtCmd> resource. This primitive shall comply with the following tables.

Table 6.3.4.2.1.1-1: Applicability of mgmtCmdCreateRequest

| Applicable interfaces | Mca | Mcc | Mcc’ | Mcn |
| --- | --- | --- | --- | --- |
| Originator | AE | ASN/MN-CSE | n/a | n/a |
| Receiver | IN-CSE | IN-CSE | n/a | n/a |

Table 6.3.4.2.1.1-2: mgmtCmdCreateRequest

| Primitive attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| requestingEntity | M | AE or ASN/MN-CSE that requests the creation of an <mgmtCmd> resource |
| targetID | M | The URI of the target entity where the <mgmtCmd> resource shall be created |
| primitiveType | M | MGMTCMD_CREATE_REQUEST |
| Resource | Mandatory/Optional | Description |
| mgmtCmd | M | The <mgmtCmd> resource representation |

The Originator shall execute the following steps in order:

- Primitive specific operation: If the Originator is an ASN/MN-CSE (i.e. a remote entity), the Originator shall generate the <mgmtCmd> resource representation based on the information of management commands on the remote entity.

- "Compose RequestIndication primitive".

- "Send a RequestIndication to the receiver CSE".

- "Wait for ResponseConfirm primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful ResponseConfirm" and then "Send ResponseConfirm primitive". The corresponding statusCode shall be included in the ResponseConfirm primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- "Check validity of resource representation for CREATE".

- "Create the resource".

- "Create a successful ResponseConfirm".

- "Send ResponseConfirm primitive".

###### 6.3.4.2.1.2	mgmtCmdCreateResponse (successful)

This response is triggered by the mgmtCmdCreateRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.1.2-1: mgmtCmdCreateResponse (successful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_CREATE_RESPONSE |
| statusCode | M | Provides Success code STATUS_CREATED |
| resourceURI | M | The URI assigned to the <mgmtCmd> resource that was created |
| Resource | Mandatory/Optional | Description |
| mgmtCmd | O | Full representation of the created <mgmtCmd> resource, if any of the provided attributes were modified by the hosting CSE |

###### 6.3.4.2.1.3	mgmtCmdCreateResponse (unsuccessful)

This response is triggered by the mgmtCmdCreateRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.1.3-1: mgmtCmdCreateResponse (unsuccessful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_CREATE_RESPONSE |
| errorInfo | M | Provides Error information |

##### 6.3.4.2.2	mgmtCmdRetrieve

###### 6.3.4.2.2.1	mgmtCmdRetrieveRequest

This procedure is used for retrieving the content of an <mgmtCmd> resource. This primitive shall comply with the following tables.

Table 6.3.4.2.2.1-1: Applicability of mgmtCmdRetrieveRequest

| Applicable interfaces | Mca | Mcc | Mcc’ | Mcn |
| --- | --- | --- | --- | --- |
| Originator | AE | ASN/MN-CSE | n/a | n/a |
| Receiver | IN-CSE | IN-CSE | n/a | n/a |

Table 6.3.4.2.2.1-2: mgmtCmdRetrieveRequest

| Primitive attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| requestingEntity | M | Entity which requests the retrieving |
| targetID | M | The URI of the <mgmtCmd> resource to be retrieved |
| primitiveType | M | MGMTCMD_RETRIEVE_REQUEST |

The Originator shall execute the following steps in order:

- "Compose RequestIndication primitive".

- "Send a RequestIndication to the receiver CSE".

- "Wait for ResponseConfirm primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful ResponseConfirm" and then "Send ResponseConfirm primitive". The corresponding statusCode shall be included in the ResponseConfirm primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- "Read the addressed resource".

- "Create a successful ResponseConfirm".

- "Send ResponseConfirm primitive".

###### 6.3.4.2.2.2	mgmtCmdRetrieveResponse (successful)

This response is triggered by the mgmtCmdRetrieveRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.2.2-1: mgmtCmdRetrieveResponse (successful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_RETRIEVE_RESPONSE |
| statusCode | M | Provides Success code STATUS_OK |
| Resource | Mandatory/Optional | Description |
| mgmtCmd | M | Full representation of the retrieved <mgmtCmd> resource |

###### 6.3.4.2.2.3	mgmtCmdRetrieveResponse (unsuccessful)

This response is triggered by the mgmtCmdRetrieveRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.2.3-1: mgmtCmdRetrieveResponse (unsuccessful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_RETRIEVE_RESPONSE |
| errorInfo | M | Provides Error information |

##### 6.3.4.2.3	mgmtCmdUpdate

###### 6.3.4.2.3.1	mgmtCmdUpdateRequest

This request is used for updating the full representation of an <mgmtCmd> resource or only part of an <mgmtCmd> resource using partial addressing. This primitive shall comply with the following tables.

Table 6.3.4.2.3.1-1: Applicability of mgmtCmdUpdateRequest

| Applicable interfaces | Mca | Mcc | Mcc’ | Mcn |
| --- | --- | --- | --- | --- |
| Originator | AE | ASN/MN-CSE | n/a | n/a |
| Receiver | IN-CSE | IN-CSE | n/a | n/a |

Table 6.3.4.2.3.1-2: mgmtCmdUpdateRequest

| Primitive attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| requestingEntity | M | Entity which requests the updating |
| targetID | M | The URI of the <mgmtCmd> resource to be updated |
| primitiveType | M | MGMTCMD_UPDATE_REQUEST |
| Resource | Mandatory/Optional | Description |
| mgmtCmd | M | The <mgmtCmd> resource representation |

###### The Originator shall execute the following steps in order:

###### "Compose RequestIndication primitive".

###### "Send a RequestIndication to the receiver CSE".

###### "Wait for ResponseConfirm primitive".

###### The receiver shall execute the following steps in order. In case of error in any of the steps below, the receiver shall execute "Create an unsuccessful ResponseConfirm" and then "Send ResponseConfirm primitive". The corresponding statusCode shall be included in the ResponseConfirm primitive.

###### "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

###### "Check existence of the addressed resource".

###### "Check authorization of the requestingEntity based on accessPolicyControlID".

###### "Check the syntax of received message".

###### "Check validity of the resource representation for UPDATE".

###### "Update the addressed resource".

###### "Create a successful response Confirm".

###### "Send response Confirm primitive".

###### 6.3.4.2.3.2	mgmtCmdUpdateResponse (successful)

This response is triggered by the mgmtCmdUpdateRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.3.2-1: mgmtCmdUpdateResponse (successful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_UPDATE_RESPONSE |
| statusCode | M | Provides Success code STATUS_OK |
| Resource | Mandatory/Optional | Description |
| mgmtCmd | M | Full representation of the retrieved <mgmtCmd> resource, if any of the provided attributes were modified by the hosting CSE |

###### 6.3.4.2.3.3	mgmtCmdUpdateResponse (unsuccessful)

This response is triggered by the mgmtCmdUpdateRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.3.3-1: mgmtCmdUpdateResponse (unsuccessful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_UPDATE_RESPONSE |
| errorInfo | M | Provides Error information |

##### 6.3.4.2.4	mgmtCmdDelete

###### 6.3.4.2.4.1	mgmtCmdDeleteRequest

This procedure is used for deleting an <mgmtCmd> resource. This primitive shall comply with the following tables.

Table 6.3.4.2.4.1-1: Applicability of mgmtCmdDeleteRequest

| Applicable interfaces | Mca | Mcc | Mcc’ | Mcn |
| --- | --- | --- | --- | --- |
| Originator | AE | ASN/MN-CSE | n/a | n/a |
| Receiver | IN-CSE | IN-CSE | n/a | n/a |

Table 6.3.4.2.4.1-2: mgmtCmdDeleteRequest

| Primitive attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| requestingEntity | M | Entity which requests the deleting |
| targetID | M | The URI of the <mgmtCmd> resource to be deleted |
| primitiveType | M | MGMTCMD_DELETE_REQUEST |

The Originator shall execute the following steps in order:

- "Compose RequestIndication primitive".

- "Send a RequestIndication to the receiver CSE".

- "Wait for ResponseConfirm primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful ResponseConfirm" and then "Send ResponseConfirm primitive". The corresponding statusCode shall be included in the ResponseConfirm primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessPolicyControlID".

- "Check the syntax of received message".

If the Originator is an IN-AE and the requested <mgmtCmd> resource includes pending management commands previously initiated on the remote entity and the pending command is cancellable, the Receiver shall perform steps 5-7; otherwise, steps 5-7 shall be skipped.

- "Identify the managed remote entity and the management protocol".

- "Establish a management session with the remote entity".

- "Management Command Conversion and Execution".

- "Delete the addressed resource".

- "Create a successful ResponseConfirm".

- "Send ResponseConfirm primitive".

###### 6.3.4.2.4.2	mgmtCmdDeleteResponse (successful)

This response is triggered by the mgmtCmdDeleteRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.4.2-1: mgmtCmdDeleteResponse (successful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_DELETE_RESPONSE |
| statusCode | M | Provides Success code STATUS_OK |

###### 6.3.4.2.4.3	mgmtCmdDeleteResponse (unsuccessful)

This response is triggered by the mgmtCmdDeleteRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.4.3-1: mgmtCmdDeleteResponse (unsuccessful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_DELETE_RESPONSE |
| errorInfo | M | Provides Error information |

##### 6.3.4.2.5	mgmtCmdExecute

###### 6.3.4.2.5.1	mgmtCmdExecuteRequest

This procedure is used for executing a management command represented by an <mgmtCmd> resource. This primitive shall comply with the following tables.

Table 6.3.4.2.5.1-1: Applicability of mgmtCmdExecuteRequest

| Applicable interfaces | Mca | Mcc | Mcc’ | Mcn |
| --- | --- | --- | --- | --- |
| Originator | AE | n/a | n/a | n/a |
| Receiver | IN-CSE | n/a | n/a | n/a |

Table 6.3.4.2.5.1-2: mgmtCmdExecuteRequest

| Primitive attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| requestingEntity | M | AE which requests to execute a management command represented by an <mgmtCmd> resource |
| targetID | M | The URI to address the "execEnable" attribute of an <mgmtCmd> resource, or the URI provided as the value of the "execEnable" attribute |
| primitiveType | M | MGMTCMD_UPDATE_REQUEST |

The Originator shall execute the following steps in order:

- "Compose RequestIndication primitive".

- "Send a RequestIndication to the receiver CSE".

- "Wait for ResponseConfirm primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful ResponseConfirm" and then "Send ResponseConfirm primitive". The corresponding statusCode shall be included in the ResponseConfirm primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessPolicyControlID".

- "Check the syntax of received message".

- "Identify the managed remote entity and the management protocol".

- "Establish a management session with the remote entity".

- "Management Command Conversion and Execution".

- "Create a successful ResponseConfirm".

- "Send ResponseConfirm primitive".

###### 6.3.4.2.5.2	mgmtCmdExecuteResponse (successful)

This response is triggered by the mgmtCmdExecuteRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.5.2-1: mgmtCmdExecuteResponse (successful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_UPDATE_RESPONSE |
| statusCode | M | Provides Success code STATUS_CREATED |
| resourceURI | M | URI of the <execInstance> resource which is created as a result of command execution |

###### 6.3.4.2.5.3	mgmtCmdExecuteResponse (unsuccessful)

This response is triggered by the mgmtCmdExecuteRequest. The CSE primitive shall comply with the following table.

Table 6.3.4.2.5.3-1: mgmtCmdExecuteResponse (unsuccessful case)

| Primitive Attribute | Mandatory/Optional | Description |
| --- | --- | --- |
| primitiveType | M | MGMTCMD_UPDATE_RESPONSE |
| errorInfo | M | Provides Error information |

### -----------------------End of proposed text 1 -------------------------------------------