| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3(Protocol WG) |
| Title:* | CRUD mapping on HTTP |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-03-31 |
| Abstract:* | This contribution proposed mapping of CRUD operations for HTTP-REST protocol binding |
| Agenda Item:* | HTTP Binding TS |
| Work item(s): | WI-0013 |
| Document(s) Impacted* | TS-0009 (HTTP Protocol Binding) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG3 members should agree on proposal. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Widely known as CRUD operation will be commonly used in RESTful system.

This contribution proposes to define CRUD operations as operation primitive for HTTP binding.

### -----------------------Start of change 1-------------------------------------------

## 5.2	Basic Flow (Non-Blocking Request)

<Text>

The following text is to be used when appropriate:

## 5.x	CRUD Operations on HTTP bindings

CRUD (Create/Retrieve/Update/Delete) operations against M2M Resource Types are defined in in ‘oneM2M Core Protocol TS’.

This clause describes common part of procedure in HTTP protocol binding for each CRUD operations.

5.x.1	Create oneM2M Resource

Creating oneM2M Resource is performed by HTTP request with ‘POST’ method.

This operation is possible to create new instance of targeted oneM2M resource.

5.x.2	Retrieve  oneM2M Resource

Retrieving oneM2M Resource is performed by HTTP request with ‘GET’ method.

This operation is possible to read the attribute values of existing oneM2M resource.

5.x.3	Update oneM2M Resource

Updating oneM2M Resource is performed by HTTP request with ‘PUT’ method.

This operation is possible to replace attribute values of existing oneM2M resource.

5.x.4	Delete oneM2M Resource

Deleting oneM2M Resource is performed by HTTP request with ‘DELETE’ method.

This operation is possible to delete specific instance of oneM2M resource.

### -----------------------End of change 1---------------------------------------------