| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#10.0 |
| Title:* | Generic primitives and procedures |
| Source:* | QUALCOMM Incorporated (TIA) |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com Josef Blanz, jblanz@qti.qualcomm.com Wolfgang Granzow, wgranzow@qti.qualcomm.com |
| Date:* | 2014-04-07 |
| Abstract:* | This contribution proposes generic primitive formats and procedures. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

WG3 has not developed an agreed template for primitives. There was a suggestion to re-use ETSI primitive format. We can definetely re-use a lot from ETSI stage 3 document, however, we should try to minimize the redundant procedures and repetitions of the similar primitive format tables.

ETSI stage 3 defines each primitive depending on the resource and operation types (CRUD). Also,  most of the procedures for Originator and Receiver are quite common.

This contribution proposes “generic primitive formats and procedures” so that we can define stage 3 more efficiently.

--------------------- Start of proposed modified text -------------------

### 6.x.x.x Generic Primitives and Procedures

6.x.x.x.1 Create

6.x.x.x.1.1 CreateRequest

This primitive is used for creating a resource on a Receiver CSE. The primitive shall comply with the following.

# Table 6.x.x.x.1-1: CreateRequest

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | CREATE_REQUEST |
| To | M | M | URI of the target resource where the new resource should be created (parent resource) |
| From | M | M | ID of the Originator (either the AE or CSE) |
| RequestIdentifier | M | M | Unique identifier for a Request |
| ResourceType | M | M | The type of the resource to be created |
| Content | M | M | Resource representation to be created |
| ResourceName | O | O | Name of the resource to be provided by the Originator |
| OriginalTimestamp | O | O | when the message was built |
| RequestExpirationTimestamp | O | O | when the request message expires |
| ResultExpirationTime | O | O | when the result message expires |
| OperationExecutionTime | O | O | the time when the specified operation is to be executed by the target CSE. |
| ResponseType | O | O | indication that the Request was accepted, or include the operation result |
| ResultDestination | O | O | either a reference to where the result is stored, or the result is sent to the Originator |
| ResultPersistence | O | O | the duration for which the reference containing the responses is to persist |
| ResultContent | O | O | the expected components of the result |
| EventCategory | O | M | indicates how and when the system should deliver the message |
| DeliveryAggregation | O | O | aggregation of requests to the same target CSE is to be used |
| GroupRequestIdentifier | O | O | Identifier added to the group request that is to be fanned out to each member of the group |
| FilterCriteria | NP | NP | conditions for filtered retrieve operation |

The Originator shall execute the following steps in order:

- "Compose Request primitive".

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding statusCode shall be included in the Response primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- "Check validity of resource representation for CREATE".

- "Create the resource".

- If the resource is the announce-able resource type, then “Announce the resource”.

- "Create a successful Response".

- "Send Response primitive".

6.x.x.x.1.2 CreateResponse (successful case)

This response is triggered by the CreateRequest. The primitive shall comply with the following.

# Table 6.x.x.x.1-2: CreateResponse, successful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | CREATE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | O | O | address for the temporary storage of end node Responses. |
| Content | O | O | the address and/or the content of the created resource |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.1.3 CreateResponse (unsuccessful case)

This response is triggered by the CreateRequest. The primitive shall comply with the following.

# Table 6.x.x.x.1-3: CreateResponse, unsuccessful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | CREATE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | NP | NP | address for the temporary storage of end node Responses. |
| Content | NP | NP | the address and/or the content of the created resource |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.2 Retrieve

6.x.x.x.2.1 RetrieveRequest

This procedure is used for retrieving the information stored for any of the attributes for a resource at the Receiver CSE.The primitive shall comply with the following.

# Table 6.x.x.x.2-2: RetrieveRequest

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | RETRIEVE_REQUEST |
| To | M | M | URI of the target resource |
| From | M | M | ID of the Originator (either the AE or CSE) |
| RequestIdentifier | M | M | Unique identifier for a Request |
| ResourceType | NP | NP | The type of the resource to be created |
| Content | NP | NP | Resource representation to be created |
| ResourceName | NP | NP | Name of the resource to be provided by the Originator |
| OriginalTimestamp | O | O | when the message was built |
| RequestExpirationTimestamp | O | O | when the request message expires |
| ResultExpirationTime | O | O | when the result message expires |
| OperationExecutionTime | O | O | the time when the specified operation is to be executed by the target CSE. |
| ResponseType | O | O | indication that the Request was accepted, or include the operation result |
| ResultDestination | O | O | either a reference to where the result is stored, or the result is sent to the Originator |
| ResultPersistence | O | O | the duration for which the reference containing the responses is to persist |
| ResultContent | O | O | the expected components of the result |
| EventCategory | O | M | indicates how and when the system should deliver the message |
| DeliveryAggregation | O | O | aggregation of requests to the same target CSE is to be used |
| GroupRequestIdentifier | O | O | Identifier added to the group request that is to be fanned out to each member of the group |
| FilterCriteria | O | O | conditions for filtered retrieve operation |

The Originator shall execute the following steps in order:

- "Compose Request primitive".

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding statusCode shall be included in the Response primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- "Read the addressed resource".

- "Create a successful Response".

- "Send Response primitive".

6.x.x.x.2.2 RetrieveResponse (successful case)

This response is triggered by the RetrieveRequest. The primitive shall comply with the following.

# Table 6.x.x.x.2-3: RetrieveResponse, successful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | RETRIEVE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | O | O | address for the temporary storage of end node Responses. |
| Content | M | M | content of the resource retrieved |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.2.3 RetrieveResponse (unsuccessful case)

This response is triggered by the RetrieveRequest. The primitive shall comply with the following.

# Table 6.x.x.x.2-4: RetrieveResponse, unsuccessful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | RETRIEVE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | NP | NP | address for the temporary storage of end node Responses. |
| Content | NP | NP | the address and/or the content of the created resource |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.3 Update

6.x.x.x.3.1 UpdateRequest

This procedure is used for updating the information stored for any of the attributes at a target resource. The primitive shall comply with the following.

# Table 6.x.x.x.3-2: UpdateRequest

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | UPDATE_REQUEST |
| To | M | M | URI of the target resource |
| From | M | M | ID of the Originator (either the AE or CSE) |
| RequestIdentifier | M | M | Unique identifier for a Request |
| ResourceType | NP | NP | The type of the resource to be created |
| Content | M | M | Resource representation to be updated |
| ResourceName | NP | NP | Name of the resource to be provided by the Originator |
| OriginalTimestamp | O | O | when the message was built |
| RequestExpirationTimestamp | O | O | when the request message expires |
| ResultExpirationTime | O | O | when the result message expires |
| OperationExecutionTime | O | O | the time when the specified operation is to be executed by the target CSE. |
| ResponseType | O | O | indication that the Request was accepted, or include the operation result |
| ResultDestination | O | O | either a reference to where the result is stored, or the result is sent to the Originator |
| ResultPersistence | O | O | the duration for which the reference containing the responses is to persist |
| ResultContent | O | O | the expected components of the result |
| EventCategory | O | M | indicates how and when the system should deliver the message |
| DeliveryAggregation | O | O | aggregation of requests to the same target CSE is to be used |
| GroupRequestIdentifier | O | O | Identifier added to the group request that is to be fanned out to each member of the group |
| FilterCriteria | NP | NP | conditions for filtered retrieve operation |

The Originator shall execute the following steps in order:

- "Compose Request primitive".

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding statusCode shall be included in the Response primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- "Check validity of resource representation for CREATE".

- "Updated the addressed resource".

- If the resource is the announce-able resource type, then “Announce the resource”.

- "Create a successful Response".

- "Send Response primitive".

6.x.x.x.3.2 UpdateResponse (successful case)

This response is triggered by the UpdateRequest. The primitive shall comply with the following.

# Table 6.x.x.x.3-3: UpdateResponse, successful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | UPDATE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | O | O | address for the temporary storage of end node Responses. |
| Content | O | O | Resource representation updated |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.3.3 UpdateResponse (unsuccessful case)

This response is triggered by the UpdateRequest. The primitive shall comply with the following.

# Table 6.x.x.x.3-4: UpdateResponse, unsuccessful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | UPDATE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | NP | NP | address for the temporary storage of end node Responses. |
| Content | NP | NP | Resource representation updated |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.4 Delete

6.x.x.x.4.1 DeleteRequest

This procedure is used by an Originator CSE or AE to delete a resource at a Receiver CSE. The primitive shall comply with the following.

# Table 6.x.x.x.4-2: DeleteRequest

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | DELETE_REQUEST |
| To | M | M | URI of the target resource |
| From | M | M | ID of the Originator (either the AE or CSE) |
| RequestIdentifier | M | M | Unique identifier for a Request |
| ResourceType | NP | NP | The type of the resource to be created |
| Content | NP | NP | Resource representation |
| ResourceName | NP | NP | Name of the resource to be provided by the Originator |
| OriginalTimestamp | O | O | when the message was built |
| RequestExpirationTimestamp | O | O | when the request message expires |
| ResultExpirationTime | O | O | when the result message expires |
| OperationExecutionTime | O | O | the time when the specified operation is to be executed by the target CSE. |
| ResponseType | O | O | indication that the Request was accepted, or include the operation result |
| ResultDestination | O | O | either a reference to where the result is stored, or the result is sent to the Originator |
| ResultPersistence | O | O | the duration for which the reference containing the responses is to persist |
| ResultContent | O | O | the expected components of the result |
| EventCategory | O | M | indicates how and when the system should deliver the message |
| DeliveryAggregation | O | O | aggregation of requests to the same target CSE is to be used |
| GroupRequestIdentifier | O | O | Identifier added to the group request that is to be fanned out to each member of the group |
| FilterCriteria | NP | NP | conditions for filtered retrieve operation |

The Originator shall execute the following steps in order:

- "Compose Request primitive".

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding statusCode shall be included in the Response primitive.

- "Re-targeting" The receiver shall not execute following steps if the request is re-targeted.

- "Check existence of the addressed resource".

- "Check authorization of the requestingEntity based on accessControlPolicyID".

- "Check the syntax of received message".

- If the resource is the announce-able resource type, then “De-Announce the resource”.

- "Delete the addressed resource".

- "Create a successful Response".

- "Send Response primitive".

6.x.x.x.4.2 DeleteResponse (successful case)

This response is triggered by the DeleteRequest. The primitive shall comply with the following.

# Table 6.x.x.x.4-3: DeleteResponse, successful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | DELETE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | O | O | address for the temporary storage of end node Responses. |
| Content | O | O | the content of the deleted resource |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

6.x.x.x.4.3 DeleteResponse (unsuccessful case)

This response is triggered by the DeleteRequest. The primitive shall comply with the following.

# Table 6.x.x.x.4-4: DeleteResponse, unsuccessful case

| Primitive attribute | M/O | Description |
| --- | --- | --- |
|  | Mca | Mcc |  |
| primitiveType | M | M | DELETE_RESPONSE |
| To | O | O | The identifier of the Originator |
| From | O | O | The identifier of the Receiver |
| RequestIdentifier | M | M | Unique identifier for a Request |
| Result | M | M | operation result: e.g. Okay, Okay and Done; Okay and Scheduled; Okay and In Progress, etc., |
| StatusCode | O | O | Status code |
| ResponseAddress | NP | NP | address for the temporary storage of end node Responses. |
| Content | NP | NP |  |
| OriginalTimestamp | O | O | when the message was built |
| ResultExpirationTime | O | O | when the result message expires |

--------------------- End of proposed modified text ---------------------