| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO 10.1 |
| Title:* | Attribute short names |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com |
| Contact: |  |
| Date:* | 2014-04-21 |
| Abstract:* | Proposal for attribute short names in oneM2M messages |
| Agenda Item:* | Contributions to TS-0004-Protocols |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | TS-0004-Protocols |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept proposal and changes |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction: Short names were proposed in WG2 “In all tables representing resource attributes, each attribute name is followed by its "short name" in brackets that shall be used in resource representations to be transferred across reference points.”

The intention was to reduce the number of bytes transferred in oneM2M message flows at the expense of making the attributes cryptic for humans to understand. (This assumed that compression software was not being used).

Generally a 3-5 letter abbreviation of the attribute name was proposed. However given the similarity among attribute names some 3-5 letter abbreviations were modified to avoid name space collisions.

Given the need to remember so many abbreviations (175 currently), it is questionable whether a developer would find any value in the 3-5 letter form.

Therefore to enable reduction in the number of bytes transferred in oneM2M message flows, it is proposed that we simply number attributes as their short form. The attribute-number attribute mapping for release 1 would be alphabetic. Thereafter the mapping would be incrementally alphabetic per release, not changing prior allocations for backwards compatibility. If an attribute is subsequently removed then the corresponding number would be retired.   The format of the number is xs: unsignedShort which would provide a namespace for 65,536 attributes.

This avoids the need to think of and agree on all the short form abbreviations and will save us time.

The proposed change is limited to Annex A (Normative): Resource attributes

As we develop the list of attributes we should not bother maintaining the numbering, we only need to re-rationalise these before release.

--------------------------------Start of change------------------------------------------------------------

Annex A (Normative): Resource attributes

Resource Attributes are specified in oneM2M TS-0001 [6]. The type and values shall be supported according to the description given in table A-1.

The attributes are specified by trhe following information in the table:

- ResourceType: indicates the resource where the attribute is used, in case that the attribute is present in all resources the tag “ALL” is used.

- Attribute Name: indicates the name of the Attribute from [6]

- Short Name: indicates the token for the correspondent Attribute. The numerical token incrementally maps to attributes in alphabetical order for each release. Previously allocated numeric values shall not change. If an attribute is subsequently removed then the corresponding number would be retired. The format of the short name is xs: unsignedShort which provides a namespace for 65,536 attributes.

- Data type: indicate the used type for the attribute, simple data types are defined in clause 6.3.1 and complex data types are defined in clause 6.3.2.

- Default: specifies the default value of the attribute as set by hosting CSE if no specific value was provided in the operation CREATE or UPDATE request, or if the provided value was unacceptable for the hosting CSE and is not specified to respond with an error then the hosting CSE is allowed to set a value.

- Value restrictions: indicates if the value of the attributes has a specific limitation.

Table A-1: Resource attributes

| ResourceType | Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| ALL except <accessControlPolicy> | accessControlPolicyID | 1 | xs:string | NONE | See TBD | If the attribute is absent, all the entities that correspond to ancestor resources shall have the full set of permissions |
| firmware | activate | 2 |  |  |  |  |
| firmware | activateStatus | 3 |  |  |  |  |
| <subscription> | aggregationURI | 4 | xs:anyURI |  |  |  |
| TBD | announceAttribute | 5 | xs:string | NONE |  |  |
| TBD | announceTo | 6 | xs:anyURI | NONE |  |  |
| <application>, <m2mServiceSubscription>, <nodeInfo> | App-ID | 7 | xs:string |  |  |  |
| <application> | App-Inst-ID | 8 | xs:string |  |  |  |
| <cmdhEcDefParamValues>, <cmdhNetworkAccessRules>, <cmdhBuffer> | applicableEventCategory | 9 |  |  |  |  |
| <areaNwkDeviceInfo> | areaNwkId | 10 |  |  |  |  |
| <areaNwInfo> | areaNwkType | 11 |  |  |  |  |
| <capabilityInstance> | attached | 12 |  |  |  |  |
| <cmdhNwAccessRule> | backOffParameters | 13 |  |  |  |  |
| <subscription> | batchNotify | 14 |  |  |  |  |
| <battery> | batteryLevel | 15 |  |  |  |  |
| <battery> | batteryStatus | 16 |  |  |  |  |
| <capabilityInstance> | capabilityActionStatus | 17 |  |  |  |  |
| <capabilityInstance> | capabilityName | 18 |  |  |  |  |
| <pollingChannel> | channelHandle | 19 |  |  |  |  |
| <mgmtCmd> | cmdType | 20 |  |  |  |  |
| <statsCollect> | collectedEntityID | 21 |  |  |  |  |
| <statsCollect> | collectingEntityID | 22 |  |  |  |  |
| <statsCollect> | collectPeriod | 23 |  |  |  |  |
| <group> | consistencyStrategy | 24 |  |  |  |  |
| <instance> | content | 25 | Content | NONE |  |  |
| <request> | content | 26 | ? |  |  |  |
| <instance> | contentSize | 27 | xs:long |  |  | Set by the CSE to the actual size of the received content of the instance |
| ALL | creationTime | 28 | xs:dateTime |  |  | Generated by the hosting SCE. The value is set to the actual time of creation of the resource. |
| TBD | creator | 29 | xs:anyURI |  |  | Generated by the hosting |
| <remoteCSE> | cseBase | 30 | xs:anyURI |  |  |  |
| <CSEBase>, <remoteCSE>, <nodeInfo> | CSE-ID | 31 | xs:string |  |  |  |
| <CSEBase> and <remoteCSE> | cseType | 32 | TBD |  |  |  |
| <container> | currentByteSize | 33 | xs:long |  | Limited by maxByteSize attribute of the same container resource | Set to the actual number of bytes of data stored in the Container resource |
| <container> | currentNrOfInstances | 34 | xs:long |  | Limited by maxNrOfInstances attribute of the same container resource | Set to the actual number of instances resource in the Container |
| <group> | currentNrOfMembers | 35 | xs:long |  |  |  |
| <delivery> | data | 36 |  |  |  |  |
| <eventConfig> | dataSize | 37 |  |  |  |  |
| firmware | deactivate | 38 |  |  |  |  |
| <cmdhEcDefParamValues> | defaultDelAggregation | 39 |  |  |  |  |
| <cmdhEcDefParamValues> | defaultOpExecTime | 40 |  |  |  |  |
| <cmdhEcDefParamValues> | defaultRequestExpTime | 41 |  |  |  |  |
| <cmdhEcDefParamValues> | defaultRespPersistence | 42 |  |  |  |  |
| <cmdhEcDefParamValues> | defaultResultExpTime | 43 |  |  |  |  |
| <cmdhDefEcValue> | defEcValue | 44 |  |  |  |  |
| <delivery> | deliveryMetaData | 45 |  |  |  |  |
| <mgmtObj>, <parameters>, <mgmtCmd>, memory, software, firmware,<areaNwInfo>, <areaNwkDeviceInfo>, battery, <deviceInfo>, <deviceCapability>, <capabilityInstance>, reboot, <eventLog> | description | 46 | xs:string |  |  |  |
| <deviceInfo> | deviceLabel | 47 |  |  |  |  |
| <deviceInfo> | deviceType | 48 |  |  |  |  |
| <areaNwkDeviceInfo> | devId | 49 |  |  |  |  |
| <areaNwkDeviceInfo> | devType | 50 |  |  |  |  |
| <capabilityInstance> | disable | 51 |  |  |  |  |
| <capabilityInstance> | enable | 52 |  |  |  |  |
| <delivery> | eventCat | 53 |  |  |  |  |
| <eventConfig> | eventEnd | 54 | xs:dateTime |  |  |  |
| <eventConfig>, <statsCollect> | eventID | 55 |  |  |  |  |
| <eventConfig> | eventStart | 56 | xs:dateTime |  |  |  |
| <eventConfig> | eventType | 57 |  |  |  |  |
| <execInstance> | execDelay | 58 |  |  |  |  |
| <execInstance> | execDisable | 59 |  |  |  |  |
| <mgmtCmd> | execEnable | 60 |  |  |  |  |
| <execInstance> | execFrequency | 61 |  |  |  |  |
| <execInstance> | execMode | 62 |  |  |  |  |
| <execInstance> | execNumber | 63 |  |  |  |  |
| <mgmtCmd>, <execInstance> | execReqArgs | 64 |  |  |  |  |
| <execInstance> | execResult | 65 |  |  |  |  |
| <execInstance> | execStatus | 66 |  |  |  |  |
| <execInstance> | execTarget | 67 |  |  |  |  |
| <subscription> | expirationCounter | 68 |  |  |  |  |
| ALL, except <CSEBase>, <instance> and <parameters> | expirationTime | 69 | xs:dateTime |  |  | The value may be determined by CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |
| <reboot> | factoryReset | 70 |  |  |  |  |
| <subscription> | filterCriteria | 71 | FilterCriteria |  |  |  |
| <deviceInfo> | fwVersion | 72 |  |  |  |  |
| <group> | groupName | 73 | xs:string | NONE |  |  |
| <node> | hostedCSEID | 74 | Link |  |  |  |
| <deviceInfo> | hwVersion | 75 |  |  |  |  |
| firmware | install | 76 |  |  |  |  |
| firmware | installStatus | 77 |  |  |  |  |
| <subscription> | interimEventNotify | 78 |  |  |  |  |
| ALL | labels | 79 | xs:string | NONE |  |  |
| ALL | lastModifiedTime | 80 | xs:dateTime | NONE |  |  |
| <container> | latest | 81 | xs:anyURI |  | Limited to the URI of the instances resources in the container | Set by the CSE to the URI of the latest added instance resource to the container |
| <subscription> | latestNotify | 82 |  |  |  |  |
| <delivery> | lifespan | 83 |  |  |  |  |
| <cmdhLimits> | limitsDelAggregation | 84 |  |  |  |  |
| <cmdhLimits> | limitsOpExecTime | 85 |  |  |  |  |
| <cmdhLimits> | limitsRequestExpTime | 86 |  |  |  |  |
| <cmdhLimits> | limitsRespPersistence | 87 |  |  |  |  |
| <cmdhLimits> | limitsResultExpTime | 88 |  |  |  |  |
| TBD | link | 89 | Link | NONE |  |  |
| <areaNwInfo> | listOfDevices | 90 |  |  |  |  |
| <areaNwkDeviceInfo> | listOfNeighbors | 91 |  |  |  |  |
| <locationPolicy> | locationContainerID | 92 | xs:anyURI |  |  |  |
| <locationPolicy> | locationContainerName | 93 | xs:string |  |  |  |
| <container> | locationID | 94 | xs:anyURI | NONE |  |  |
| <locationPolicy> | locationServer | 95 |  |  |  |  |
| <locationPolicy> | locationSource | 96 |  |  |  |  |
| <locationPolicy> | locationTargetId | 97 |  |  |  |  |
| <locationPolicy> | locationUpdatePeriod | 98 |  |  |  |  |
| <eventLog> | logActionStatus | 99 |  |  |  |  |
| <eventLog> | logData | 100 |  |  |  |  |
| <eventLog> | logStart | 101 |  |  |  |  |
| <eventLog> | logStop | 102 |  |  |  |  |
| <eventLog> | logTypeId | 103 |  |  |  |  |
| <deviceInfo> | manufacturer | 104 |  |  |  |  |
| <cmdhBuffer> | maxBufferSize | 105 |  |  |  |  |
| <container> | maxByteSize | 106 | xs:long |  |  | Determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |
| <container> | maxInstanceAge | 107 | xs:duration |  |  | Determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |
| <container> | maxNrOfInstances | 108 | xs:long |  |  | Determined by CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |
| <group> | maxNrOfMembers | 109 | xs:long |  |  | Determined by the CSE policy. If a value is provided, the CSE shall try to find an acceptable value that is as close as possible to the requested value. |
| memory | memAvailable | 110 |  |  |  |  |
| <group> | memberAccessRightID | 111 | xs:string |  |  |  |
| <group> | memberList | 112 | AnyURIList |  |  |  |
| <group> | memberType | 113 | MemberType | NONE |  |  |
| <group> | memberTypeValidated | 114 | xs:boolean | NONE |  |  |
| memory | memTotal | 115 |  |  |  |  |
| <request> | metaInformation | 116 |  |  |  |  |
| <mgmtObj>, <parameters>, memory, software, firmware,<areaNwInfo>, <areaNwkDeviceInfo>, battery, <deviceInfo>, <deviceCapability>, <capabilityInstance>, reboot, <eventLog> | mgmtDefinition | 117 | xs:string |  |  |  |
| <cmdhNwAccessRule> | minReqVolume | 118 |  |  |  |  |
| <deviceInfo> | model | 119 |  |  |  |  |
| <application>,<cmdhPolicy>, software, firmware | name | 120 | xs:string |  |  |  |
| <node>, <nodeInfo> | nodeID | 121 | Link |  |  |  |
| <CSEBase> and <application> | nodeLink | 122 | Link |  |  |  |
| <subscription> | notificationDeliveryPriority | 123 |  |  |  |  |
| <subscription> | notificationEventCat | 124 |  |  |  |  |
| <subscription> | notificationStoragePriority | 126 |  |  |  |  |
| <subscription> | notificationStructure | 127 |  |  |  |  |
| <subscription> | notificationURI | 128 | xs:anyURI |  |  |  |
| <mgmtObj>, <parameters>, memory, software, firmware,<areaNwInfo>, <areaNwkDeviceInfo>, battery, <deviceInfo>, <deviceCapability>, <capabilityInstance>, reboot, <eventLog> | objectID | 129 | xs:anyURI |  |  |  |
| <mgmtObj>, <parameters>, memory, software, firmware,<areaNwInfo>, <areaNwkDeviceInfo>, battery, <deviceInfo>, <deviceCapability>, <capabilityInstance>, reboot, <eventLog> | objectPath | 130 |  |  |  |  |
| <application>, <container>, <instance> | ontologyRef | 131 | xs:anyURI |  |  |  |
| <request> | operation | 132 |  |  |  |  |
| <request> | operationResult | 133 |  |  |  |  |
| <cmdhDefEcValue>, <cmdhLimits> | order | 134 |  |  |  |  |
| <request> | originator | 135 |  |  |  |  |
| <cmdhNwAccessRule> | otherConditions | 136 |  |  |  |  |
| ALL, except <CSEBase> | parentID | 137 | xs:anyURI | NONE | See TBD |  |
| <CSEBase>, <remoteCSE> and <application> | pointOfAccess | 138 | AnyURIList |  |  |  |
| <subscription> | priorSubscriptionNotify | 139 |  |  |  |  |
| <accessControlPolicy> | privileges | 140 | Privileges |  |  |  |
| <subscription> | rateLimit | 141 |  |  |  |  |
| <reboot> | reboot | 142 |  |  |  |  |
| <cmdhDefEcValue>, <cmdhLimits> | requestCharacteristics | 143 |  |  |  |  |
| <cmdhDefEcValue>, <cmdhLimits> | requestContextNotification | 144 |  |  |  |  |
| <cmdhDefEcValue>, <cmdhLimits> | requestContext | 145 |  |  |  |  |
|  | requestEventCategory | 146 |  |  |  |  |
| <cmdhDefEcValue>, <cmdhLimits> | requestOrigin | 147 |  |  |  |  |
| <remoteCSE> | requestReachability | 148 | xs:boolean |  |  |  |
| <request> | requestStatus | 149 |  |  |  |  |
| ALL | resourceType | 150 | ResourceType | NONE | See TBD |  |
| <schedule> | scheduleElement | 151 | Schedule |  |  |  |
| <accessControlPolicy> | selfPrivileges | 152 | Privileges |  |  |  |
| <areaNwkDeviceInfo> | sleepDuration | 153 |  |  |  |  |
| <areaNwkDeviceInfo> | sleepInterval | 154 |  |  |  |  |
| delivery | source | 155 |  |  |  |  |
| <statsCollect> | statModel | 156 |  |  |  |  |
| <statsCollect> | statsCollectID | 157 |  |  |  |  |
| <cmdhPolicy>, <areaNwkDeviceInfo> | status | 158 | xs:boolean | TRUE = active, FALSE=inactive |  |  |
| <statsCollect> | status | 159 | ?? | Editor’s note: this is a different status of active/inactive |  |  |
| <cmdhBuffer> | storagePriority | 160 |  |  |  |  |
| <statsCollect> | subscriberID | 161 |  |  |  |  |
| <m2mServiceSubscription> | subsGroup | 162 |  |  |  |  |
| <m2mServiceSubscription> | subsSer&RoleList | 163 |  |  |  |  |
| <CSEBase> | supportedResourceType | 164 | SupporteResourceType |  |  |  |
| <deviceInfo> | swVersion | 165 |  |  |  |  |
| <delivery>, <request> | target | 166 |  |  |  |  |
| <cmdhNwAccessRule> | targetNetwork | 167 |  |  |  |  |
| <eventConfig> | transactionType | 168 |  |  |  |  |
| <CSEBase>, <remoteCSE> | Trigger-Recipient-ID | 169 | TBD |  |  |  |
| <instance> | typeOfContent | 170 | ContentType | NONE |  |  |
| software | update | 171 |  |  |  |  |
| software | updateStatus | 172 |  |  |  |  |
| software, firmware | URL | 173 | xs:anyURI |  |  |  |
| software, firmware | version | 174 |  |  |  |  |
| TBD | versionTag | 175 | xs:nonNegativeInteger | 0 |  |  |

# Comments

Or define the complex type with 2 value