| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#10.6 |
| Title:* | Primitive templates and procedure outlines, Section 7.2.1 |
| Source:* | QUALCOMM Incorporated (TIA) LG Electronics |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com Josef Blanz, jblanz@qti.qualcomm.com Wolfgang Granzow, wgranzow@qti.qualcomm.com Hongbeom Ahn, hongbeom.ahn@lge.com |
| Date:* | 2014-05-16 |
| Abstract:* | This contribution proposes revised text for primitive templates and procedure outlines based on the discussion at TP#10. |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

### 7.2.1 Primitive format and procedure outlines

7.2.1.1 Primitive format

7.2.1.1.1 Request primitive format

Table 7.2.1.1.1-1 summarizes the primitive parameters for Request primitive, showing any differences as applied to C, R, U, D or N operations. “M” indicates mandatory, “O” indicates optional, “NP” indicates not present, “C” indicates conditional.

# Table 7.2.1.1.1-1: Request Primitive Parameters

| Primitive Parameter | CREATE | RETRIEVE | UPDATE | DELETE | NOTIFY |
| --- | --- | --- | --- | --- | --- |
|  | M/O | M/O | M/O | M/O | M/O |
|  | Mca | Mcc | Mca | Mcc | Mca | Mcc | Mca | Mcc | Mca | Mcc |
| primitiveType (=REQUEST) | M | M | M | M | M | M | M | M | M | M |
| Operation | M | M | M | M | M | M | M | M | M | M |
| To | M | M | M | M | M | M | M | M | M | M |
| From | M | M | M | M | M | M | M | M | M | M |
| Request Identifier | M | M | M | M | M | M | M | M | M | M |
| Resource Type | M | M | NP | NP | NP | NP | NP | NP | NP | NP |
| Name | C | C | NP | NP | NP | NP | NP | NP | NP | NP |
| Content | C | C | C | C | C | C | NP | NP | M | M |
| Original Timestamp | O | O | O | O | O | O | O | O | O | O |
| Request Expiration Timestamp | C | C | C | C | C | C | C | C | C | C |
| Result Expiration Time | C | C | C | C | C | C | C | C | C | C |
| Operation Execution Time | C | C | C | C | C | C | C | C | C | C |
| Response Type | C | C | C | C | C | C | C | C | C | C |
| Result Persistence | C | C | C | C | C | C | C | C | NP | NP |
| Result Content | C | C | C | C | C | C | C | C | NP | NP |
| Event Category | C | C | C | C | C | C | C | C | C | C |
| Delivery Aggregation | C | C | C | C | C | C | C | C | C | C |
| Group Request Identifier | C | C | C | C | C | C | C | C | C | C |
| Filter Criteria | NP | NP | C | C | NP | NP | NP | NP | NP | NP |
| Discovery Result Type | NP | NP | C | C | NP | NP | NP | NP | NP | NP |

Editor’s Note: This is an initial list of primitive parameters. Parameter name, mandatory/optional or description for each parameter is FFS.

7.2.1.1.2 Response primitive format

Table 7.2.1.1.2-1 summarizes the primitive parameters for Response primitive, showing any differences as applied to C, R, U, D or N operations and unsuccessful operations. “M” indicates mandatory, “O” indicates optional, “NP” indicates not present, “C” indicates conditional.

# Table 7.2.1.1-2: Response Primitive Parameters (1/2)

| Primitive parameter | Ack | Successful CREATE | Successful RETRIEVE | Successful UPDATE |
| --- | --- | --- | --- | --- |
|  | M/O | M/O | M/O | M/O |
|  | Mca | Mcc | Mca | Mcc | Mca | Mcc | Mca | Mcc |
| primitiveType (=RESPONSE) | M | M | M | M | M | M | M | M |
| Operation | M | M | M | M | M | M | M | M |
| Response Code | M | M | M | M | M | M | M | M |
| Request Identifier | M | M | M | M | M | M | M | M |
| Content | NP | NP | C | C | M | M | C | C |
| To | C | C | C | C | C | C | C | C |
| From | C | C | C | C | C | C | C | C |
| Originating Timestamp | O | O | O | O | O | O | O | O |
| Result Expiration Timestamp | C | NP | C | C | C | C | C | C |
| Status Code | C | C | C | C | C | C | C | C |
| Response Address | C | C | C | C | C | C | C | C |

# Table 7.2.1.1-2: Response Primitive Parameters (2/2)

| Primitive parameter | Successful DELETE | Successful NOTIFY | Unsuccessful |
| --- | --- | --- | --- |
|  | M/O | M/O | M/O |
|  | Mca | Mcc | Mca | Mcc | Mca | Mcc |
| primitiveType (=RESPONSE) | M | M | M | M | M | M |
| Operation | M | M | M | M | M | M |
| Response Code | M | M | M | M | M | M |
| Request Identifier | M | M | M | M | M | M |
| Content | C | C | NP | NP | C | C |
| To | C | C | C | C | C | C |
| From | C | C | C | C | C | C |
| Originating Timestamp | O | O | O | O | O | O |
| Result Expiration Timestamp | C | C | NP | NP | C | C |
| Status Code | C | C | C | C | C | C |
| Response Address | C | C | NP | NP | NP | NP |

Editor’s Note: This is an initial list of primitive parameters. Parameter name, mandatory/optional or description for each parameter is FFS.

7.2.1.2 Description of Generic Procedures

7.2.1.2.1 Generic Resource Create Request Procedure

A Generic Resource Create Request Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing these actions and providing additional steps.

The Originator shall execute the following steps in order:

Orig-C-1.0	"Compose Request primitive".

Orig-C-2.0	"Send a Request to the receiver CSE".

Orig-C-3.0	"Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Rcv-C-1.0	“Check validity of the primitive parameters”.

NOTE: “validity” in this sentence means that the primitive parameters conform to the specification and also that it is possible for the Receiver to process the request within the constraints of the primitive parameters. For example, if there are expiration times (e.g. Request Expiration Timestamp, Result Expiration Time and Operation Execution Time) in the primitive parameters, then this step will check that it is possible to meet those expiration times in line with the configured policies of the Receiver, if any.

If the Response Type primitive parameter is set to either ‘nonBlockingRequestSynch’ or ‘nonBlockingRequestAsynch’, then the Receiver shall:

Rcv-C-2.0	"Create a Response primitive (ack)”.

Rcv-C-3.0	"Send Response primitive".

If the To primitive parameter addresses a CSE that is not the receiver CSE, then:

The Receiver shall

Rcv-C-4.1 	“Forward Request primitive”

If the Result Content primitive parameter is set to ‘nothing’, then

If the Response Type primitive parameter is set to ‘blockingRequest’ then the Receiver shall

Rcv-C-4.2 	“Create a Response primitive (ack)”.

Rcv-C-4.3 	"Send Response primitive".

The Receiver shall then

Rcv-C-4.4	“Complete the procedure”.

else the Receiver shall

Rcv-C-4.5 	“Wait for operational result”.

Rcv-C-4.6 	“Provide the received operational result to the Originator”.

Rcv-C-4.7 	"Complete the procedure".

else (if the To primitive parameter addresses the receiver CSE) then do the following steps.

Rcv-C-5.0	"Check existence of the addressed resource".

Rcv-C-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-C-7.0	"Check validity of resource representation for the given resource type

Rcv-C-8.0	"Create the resource".

Rcv-C-9.0	If the resource is the announce-able resource type and the announceTo attribute is included, then the Receiver shall “Announce the resource”.

Rcv-C-10.0	"Create a successful Response".

Rcv-C-11.0	"Send Response primitive".

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

7.2.1.2.2 Generic Resource Retrieve Request Procedure

A Generic Resource Retrieve Request Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing this procedure and providing additional steps.

The Originator shall execute the following steps in order:

Orig-R-1.0	"Compose Request primitive".

Orig-R-2.0	"Send a Request to the receiver CSE".

Orig-R-3.0	"Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Rcv-R-1.0	“Check validity of the primitive parameter”.

NOTE: “validity” in this sentence means that the primitive parameters conform to the specification and also that it is possible for the Receiver to process the request within the constraints of the primitive parameters. For example, if there are expiration times (e.g. Request Expiration Timestamp, Result Expiration Time and Operation Execution Time) in the primitive parameters, then this step will check that it is possible to meet those expiration times in line with the configured policies of the Receiver, if any.

If the Response Type primitive parameter is set to either ‘nonBlockingRequestSynch’ or ‘nonBlockingRequestAsynch’, then the Receiver shall:

Rcv-R-2.0	"Create a Response primitive (ack)”.

Rcv-R-3.0	"Send Response primitive".

If the To primitive parameter addresses a CSE that is not the receiver CSE, then:

The Receiver shall

Rcv-R-4.1 	“Forward Request primitive”

If the Result Content primitive parameter is set to ‘nothing’, then

If the Response Type primitive parameter is set to ‘blockingRequest’ then the Receiver shall

Rcv-R-4.2 	“Create a Response primitive (ack)”.

Rcv-R-4.3 	"Send Response primitive".

The Receiver shall then

Rcv-R-4.4	“Complete the procedure”.

else the Receiver shall

Rcv-R-4.5 	“Wait for operational result”.

Rcv-R-4.6 	“Provide the received operational result to the Originator”.

Rcv-R-4.7 	"Complete the procedure".

else (if the To primitive parameter addresses the receiver CSE) then do the following steps.

Rcv-R-5.0	"Check existence of the addressed resource".

Rcv-R-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-R-7.0	"Read the addressed resource".

Rcv-R-8.0	"Create a successful Response".

Rcv-R-9.0	"Send Response primitive".

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

7.2.1.2.3 Generic Resource Update Request Procedure

A Generic Resource Update Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing this procedure and providing additional steps.

The Originator shall execute the following steps in order:

Orig-U-1.0	"Compose Request primitive".

Orig-U-2.0	"Send a Request to the receiver CSE".

Orig-U-3.0	"Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Rcv-U-1.0 	“Check validity of the primitive parameters”.

NOTE: “validity” in this sentence means that the primitive parameters conform to the specification and also that it is possible for the Receiver to process the request within the constraints of the primitive parameters. For example, if there are expiration times (e.g. Request Expiration Timestamp, Result Expiration Time and Operation Execution Time) in the primitive parameters, then this step will check that it is possible to meet those expiration times in line with the configured policies of the Receiver, if any.

If the Response Type primitive parameter is set to either ‘nonBlockingRequestSynch’ or ‘nonBlockingRequestAsynch’, then the Receiver shall:

Rcv-U-2.0	"Create a Response primitive (ack)”.

Rcv-U-3.0	"Send Response primitive".

else do the following steps.

If the To primitive parameter addresses a CSE that is not the receiver CSE, then:

The Receiver shall

Rcv-U-4.1 	“Forward Request primitive”

If the Result Content primitive parameter is set to ‘nothing’, then

If the Response Type primitive parameter is set to ‘blockingRequest’ then the Receiver shall

Rcv-U-4.2 	“Create a Response primitive (ack)”.

Rcv-U-4.3 	"Send Response primitive".

The Receiver shall then

Rcv-U-4.4	“Complete the procedure”.

else the Receiver shall

Rcv-U-4.5 	“Wait for operational result”.

Rcv-U-4.6 	“Provide the received operational result to the Originator”.

Rcv-U-4.7 	"Complete the procedure".

else (if the To primitive parameter addresses the receiver CSE) then do the following steps.

Rcv-U-5.0	"Check existence of the addressed resource".

Rcv-U-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-U-7.0	"Check validity of resource representation.

Rcv-U-8.0	"Updated the addressed resource".

Rcv-U-9.0	If the announceTo attribute of the resource was requested to be changed, the Receiver  shall determine which announcements and de-announcements need to be done.

Rcv-U-10.0	"Create a successful Response".

Rcv-U-11.0	"Send Response primitive".

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

7.2.1.2.4 Generic Resource Delete Request Procedure

A Generic Resource Delete Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing this procedure and providing additional steps.

The Originator shall execute the following steps in order:

Orig-D-1.0	"Compose Request primitive".

Orig-D-2.0	"Send a Request to the receiver CSE".

Orig-D-3.0	"Wait for Response primitive".

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Rcv-D-1.0 	“Check validity of the primitive parameters”.

NOTE: “validity” in this sentence means that the primitive parameters conform to the specification and also that it is possible for the Receiver to process the request within the constraints of the primitive parameters. For example, if there are expiration times (e.g. Request Expiration Timestamp, Result Expiration Time and Operation Execution Time) in the primitive parameters, then this step will check that it is possible to meet those expiration times in line with the configured policies of the Receiver, if any.

If the Response Type primitive parameter is set to either ‘nonBlockingRequestSynch’ or ‘nonBlockingRequestAsynch’, then the Receiver shall:

Rcv-D-2.0	"Create a Response primitive (ack)”.

Rcv-D-3.0	"Send Response primitive".

If the To primitive parameter addresses a CSE that is not the receiver CSE, then:

The Receiver shall

Rcv-D-4.1 	“Forward Request primitive”

If the Result Content primitive parameter is set to ‘nothing’, then

If the Response Type primitive parameter is set to ‘blockingRequest’ then the Receiver shall

Rcv-D-4.2 	“Create a Response primitive (ack)”.

Rcv-D-4.3 	"Send Response primitive".

The Receiver shall then

Rcv-D-4.4	“Complete the procedure”.

else the Receiver shall

Rcv-D-4.5 	“Wait for operational result”.

Rcv-D-4.6 	“Provide the received operational result to the Originator”.

Rcv-D-4.7 	"Complete the procedure".

else (if the To primitive parameter addresses the receiver CSE) then do the following steps.

Rcv-D-5.0	"Check existence of the addressed resource".

Rcv-D-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-D-7.0	If the resource is announced, then “De-Announce the resource”.

Rcv-D-8.0	"Delete the addressed resource".

Rcv-D-9.0	"Create a successful Response".

Rcv-D-10.0	"Send Response primitive".

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

7.2.1.2.5 Generic Notify Procedure

A Generic Notify Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing these actions and providing additional steps.

The Notification Originator shall execute the following steps in order:

Orig-N-1.0	“Compose Notify Request Primitive”

Orig-N-2.0	“Send a Notify Request to the Receiver”

Orig-N-3.0	“Wait for Response Primitive”

The Receiver shall execute the following steps in order.

Editor’s Note: Error cases for this Notify Procedure is FFS.

Rcv-N-1.0	“Check Validity of the Primitive parameters”

Editor’s Note: The Representation of Notify Request/Response is FFS.

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.