| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP11 |
| Title:* | Primitive templates and procedure outlines modification |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-05-31 |
| Abstract:* | This contribution proposes to modify the current general procedure in a more readable way by distinguishing communication modes by blockingSync, Non-blockingSync, Non-blockingAsync |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 The contribution only provides the general procedure for Create, the procedure for the other operation can be modified based on this in a similar way. A decision is asked to accept the other general procedure based on the consensus had on this contribution. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

#### 7.2.1.2 Description of Generic Procedures

##### 7.2.1.2.1 Generic Resource Request Procedure for Originator

A generic resource Request procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing these actions and providing additional steps.

The Originator shall execute the following steps in order:

“Compose Request primitive”: Please refer to clause 7.2.2 for details.

“Send a Request to the receiver CSE”: Please refer to clause 7.2.2 for details.

“Wait for Response primitive”: Please refer to clause 7.2.2 for details. If the Originator is using blocking communication, this step should be the last step of the Originator.

Response is ACK?: This step shall be operated after getting the Response primitive from step “Wait for Response primitive”. By checking the STATUS_CODE in the Response, if the STATUS_CODE is STATUS_ACCEPTED, the Response is an acknowledgement of the Request, next step shall go to the TRUE branch. Otherwise, the Response is not an acknowledgement, next step shall go to the FALSE branch. If the Originator is using non-blocking communication or requests nothing as the content from the Response primitive, the Response primitive doesn’t contain the result of the Request primitive. The Originator receives Response with the STATUS_CODE set to STATUS_ACCEPTED.

Response contains reference to <request> resource?: Check if the Response contains reference to <request> resource. If the Originator is using non-blocking communication, the receiver of the Request will not response with the result of the request. The receiver of the Request will create locally a <request> resource and respond with the reference of the <request> resource. The result of the Request may be retrieved from the <request> resource afterwards.

“Retrieve result from the <request> resource”: See clause 7.2.2 for details.

##### 7.2.1.2.2 Generic Resource Request Procedure for Receiver

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Figure 7.2.1.2.2-1

“Check the syntax of received message”: See clause 7.2.2 for details.

Communication method? The communication method could be blocking or non-blocking. This can be told from the rt parameter of the Request. It can also be told if the Request doesn’t contain a rt parameter. The communication method is blocking if the rt parameter is blockingSync or if the rt parameter does not exist.

Resource handling procedure: Please refer to figure 7.2.1.2.2-2 for details.

“Create a successful Response”: Please refer to clause 7.2.2 for details.

“Send Response Primitive”: Please refer to clause 7.2.2 for details.

“Create <request> resource locally”: Please refer to clause 7.2.2 for details.

“Create Response Accepted”: Please refer to clause 7.2.2 for details.

“Update <request> resource”: Please refer to clause 7.2.2 for details.

Figure 7.2.1.2.2-2

The above figure describes the generic procedure to resource handling procedures.

Hosting CSE of the targeted resource?: The step checks if the receiver is the Transit CSE or the Hosting CSE of the received Request by examine the to parameter of the Request primitive. If the receiver hosts the resource that the URI in the to  parameter represents, the receiver is the Hosting CSE. Otherwise, the receiver is the Transit CSE.

“Re-targeting”: Please refer to clause 7.2.2 for details.

“Check existence of the addressed resource”: Please refer to clause 7.2.2 for details.

“Check authorization of the Originator based on accessControlPolicyID” : Please refer to clause 7.2.2 for details.

“Check validity of resource representation for the given resource type” : Please refer to clause 7.2.2 for details.

“Create/Update/Retrieve/Delete the resource” : The step represents four common operations which are “Create the resource”, “Update the resource”, “Retrieve the resource” and “Delete the resource”. Please refer to clause 7.2.2 for details.

“Announce/De-announce the resource”: The step represents two common operations which are “Annouce the resource” and “De-announce the resource”. Please refer to clause 7.2.2 for details.

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

Editor’s Note: BlockingSync, Non-blockingSync, Non-blockingAsync need to be further clarified.

# Text boxes

“Compose Request primitive”

“Send a Request to the receiver CSE”

“Wait for Response primitive”

Response is ACK?

Finish

“Retrieve result from <request> resource”

Response contains reference to <request> resource?

True

False

True

False

“Check the syntax of received message”

Communication method?

Resource handling procedures

“Create <request> resource locally”

“Create Response Accepted”

“Send Response primitve”

Blocking

Non-Blocking

Resource handling procedures

“Create a successful Response”

“Send Response Primitive”

“Update <request> resource”

Finish

Start

Finish

“Announce/De-announce the resource”

“Create/Update/Retrieve/Delete the resource”

“Check existence of the addressed resource”

“Check validity of resource representation for the given resource type”

“Check authorization of the Originator based on accessControlPolicyID”

Start

Hosting CSE of the targeted resource?

“Re-targeting”

Start