| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | CoAP Message Format |
| Source:* | Ericsson |
| Contact: | Sumit Singhal, sumit.b.singhal@ericsson.com |
| Date:* | 2014-06-17 |
| Abstract:* | This contribution proposes a new sub-section for CoAP Message Format as part of CoAP Overview. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes new sub-section for CoAP Message Format as related part to TS-0008.

--------------------- Start of proposed modified text -------------------

### 5.2 CoAP Message Format

CoAP is based on the exchange of compact messages which can be transported over the following protocols:

- UDP (Default)

- DTLS

- SMS

- TCP

- SCTP

CoAP messages are encoded in a simple binary format. CoAP message contains a fixed-size header of 4-bytes.

The header is followed by a Token value which can be 0 or 8 bytes long. The Token value is followed by a sequence of zero or more CoAP Options in TLV format. The Options field is followed by the payload part.

Figure 1 CoAP Message Format

For more details on the Header fields, Refer [1].

--------------------- End of proposed modified text ---------------------