| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#11 |
| Title:* | oneM2M Access Control Policy Structure and Evaluation |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-07-15 |
| Abstract:* | Proposing a sub-clause in the Security TS for release 1: “Access Control Policy Structure and Evaluation” |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to propose a sub-clause in Clause 7 in the Security TS for release 1.

2	Proposal

## 7.x	Access Control Policy Structure and Evaluation

### 7.x.1	Access Control Policy Structure

oneM2M access control policy language model comprises the following three components:

- Access Control Rule;

- Access Control Policy; and

- Access Control Policy set.

#### 7.x.1.1	Access Control Rule

An access control rule is the basic elementary unit of policy. It is comprised of 3-tuples that represent the originator of an access, the operation on the target resource and the context using this rule respectively. For more details about these component parameters, see Clause 9.6.2 in the oneM2M Functional Architecture [TS-0001].

#### 7.x.1.2	Access Control Policy

An access control policy is the basic elementary unit assigned to a protected resource. It is also the smallest entity that shall be presented to a PDP for evaluation. An access control policy is comprised of a set of access control rules that are all applicable to the protected resource. The evaluation results of these access control rules shall be combined by a rule combining algorithm in order to render a finial evaluation result. This finial evaluation result shall be used as the access control policy evaluation result. Rule combining algorithms are described in Section 7.x.3.

#### 7.x.1.3	Access Control Policy Set

There may be multiple access control policies are applicable to an access control decision request. These access control policies shall be organized into an access control policy set before passing to a PDP. The evaluation results of these access control policies shall be combined by a policy combining algorithm in order to render a finial evaluation result. This finial evaluation result shall be used as the policy set evaluation result. Policy combining algorithms are described in Section 7.x.3.

### 7.x.2	Access Control Request and Response

#### 7.x.2.1	Access Control Decision Request

An access control decision request is generated by a PEP and sent to a PDP for an access control decision. The main components of an access control decision request are:

- A Resource: it represents the URI of the resource which the Originator wants to access.

- An Originator: It represents the ID of the Originator and some attributes pertained to the Originator, for example the roles assigned to the Originator and/or the groups in which the Originator has memberships.

- An Operation: It represents the operation which the Originator wants to perform on the resource.

- A Context: It represents a set of attributes related to the access context, for example the IP address and/or the location of the Originator.

The resource URI contained in the Resource component shall be used to locate the target resource and then find the associated access control policies. The information contained in the Originator, Operation and Context components shall be used to evaluate the applicable access control policies and access control rules.

#### 7.x.2.2	Access Control Decision Response

An access control decision response is generated by a PDP as a response to an access control decision request that is made by a PEP. The access control decision response contains an access control decision that is the evaluation result of an access control policy set. The evaluated access control policy set is generated according to the access control decision request. The main components of an access control decision response are:

- A Decision: It represents an access control decision. The possible values for an access control decision are described in Clause 7.x.3.

- A Status: It provides extra information about the access control decision, for example information about an error occurring during the policy evaluation process.

### 7.x.3	Access Control Policy Evaluation Request and Result

#### 7.x.3.1	Access Control Policy Evaluation Request

An access control policy evaluation request is generated based on an access control decision request by a PDP. It is used to evaluate an applicable access control policy set and the access control policies and access control policy rules in the policy set by the PDP. The main components of an access control policy evaluation request are:

- An Originator: See the Originator component in Clause 7.x.2.1.

- An Operation: See the Operation component in Clause 7.x.2.1.

- A Context: See the Context component in Clause 7.x.2.1.

#### 7.x.3.2	Access Control Policy Evaluation Result

For an access control policy evaluation request, an access control policy set, policy or rule shall be evaluated to a result. The values of evaluation results defined in this specification are the same as defined in [i.7]. They are “Permit”, “Deny”, “NotApplicable” and “Indeterminate”. These values have the following meanings:

- “Permit”: An access control policy evaluation request is permitted by an access control policy set, policy or rule.

- “Deny”: An access control policy evaluation request is denied by an access control policy set, policy or rule.

- “NotApplicable”: An access control policy or rule is not applicable to an access control policy evaluation request.

- “Indeterminate”:  An error occurs during evaluating an access control policy set, policy or rule.

When the result of evaluating a rule is “Indeterminate”, an error code may be returned with the decision result for providing the cause of the error.

### 7.x.4	Access Control Rule and Policy Combining Algorithms

There may be multiple policies in a policy set or multiple rules in a policy applicable to a particular decision request. In order to render a final authorization decision, multiple evaluation results shall be combined according to some rule or policy combining algorithms. This specification adopts following four rule/policy combining algorithms defined in [i.7] with some simplification. Details about these algorithms are described in the following subsections.

- Deny-overrides

- Permit-overrides

- Deny-unless-permit

- Permit-unless-deny

#### 7.x.3.1	Deny-Overrides

The “Deny-overrides” combining algorithm is intended for those cases where a deny decision should have priority over a permit decision. This algorithm has the following behaviour.

- If any decision is “Deny”, the result is “Deny”.

- Otherwise, if any decision is “Indeterminate”, the result is “Indeterminate”.

- Otherwise, if any decision is “Permit”, the result is “Permit”.

- Otherwise, the result is “NotApplicable”.

#### 7.x.3.2	Permit-Overrides

The “Permit-overrides” combining algorithm is intended for those cases where a permit decision should have priority over a deny decision. This algorithm has the following behaviour.

- If any decision is “Permit”, the result is “Permit”.

- Otherwise, if any decision is “Indeterminate”, the result is “Indeterminate”.

- Otherwise, if any decision is “Deny”, the result is “Deny”.

- Otherwise, the result is “NotApplicable”.

#### 7.x.3.3	Deny-unless-permit

The “Deny-unless-permit” combining algorithm is intended for those cases where a permit decision should have priority over a deny decision, and an “Indeterminate” or “NotApplicable” must never be the result. This algorithm has the following behaviour.

- If any decision is "Permit", the result is "Permit".

- Otherwise, the result is "Deny".

#### 7.x.3.4	Permit-unless-deny

The “Permit-unless-deny” combining algorithm is intended for those cases where a deny decision should have priority over a permit decision, and an “Indeterminate” or “NotApplicable” must never be the result. This algorithm has the following behaviour.

- If any decision is "Deny", the result is "Deny".

- Otherwise, the result is "Permit".

### 7.x.5	Access Control Policy Evaluation

#### 7.x.5.1	Access Control Rule Evaluation

The value of a rule is calculated based on the contents of rules and decision request. The rule evaluation truth table is shown in Table 7.x.x. Information about the Match of Originator, Operation and Context is described in Section 7.

Table 7.x.x Access control rule evaluation truth table

| Originator | Operation | Context | Error | Result |
| --- | --- | --- | --- | --- |
| Match | Match | Match | No | Permit |
| Match | No-Match | Match | No | Deny |
| No-Match | Don’t care | Don’t care | Don’t care | NotApplicable |
| Don’t care | Don’t care | No-Match | Don’t care | NotApplicable` |
| Don’t care | Don’t care | Don’t care | Yes | Indeterminate |

#### 7.x.5.2	Access Control Policy Evaluation

The value of a policy shall be determined by combining its rules’ evaluation results using the specified rule-combining algorithm.

#### 7.x.5.3	Access Control Policy Set Evaluation

The value of a policy set shall be determined by combining its policies’ evaluation results using the specified policy-combining algorithm.