| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#3, WG#5 |
| Title:* | resources for mgmtObj |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | <2014-07-15> |
| Abstract:* | This contribution provides resource instance description for mgmtObj resource instances firmware, software, memory and battery in Annex D. |
| Agenda Item:* | PRO#12 and MAS#12 |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve to add proposed text to TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes to add the following description of resource data types in the annex for instances of mgmtObj.

## ----------------------- start of change 1 ---------------

#### D.2	[firmware] Resource

The detailed description can be found in clause D.2 of Architecture TS-0001 [1].

Table D.2-1 Data Type Definition of [firmware]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.2-2  Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- |
| mgmtDefinition | Fixed string “firmware” |  |  |
| objectID | See clause 7.3.13 |  |  |
| objectPath | See clause 7.3.13 |  |  |
| description | See clause 7.3.13 |  |  |
| version | xs:string |  |  |
| name | xs:string |  |  |
| URL | xs:anyURI |  |  |
| update | N/A |  |  |
| updateStatus | m2m:actionStatus |  |  |

Table D.5-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.3	[software] Resource

The detailed description can be found in clause D.3 of Architecture TS-0001 [1].

Table D.3-1 Data Type Definition of [software]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.3-2  Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- |
| mgmtDefinition | Fixed string “software” |  |  |
| objectID | See clause 7.3.13 |  |  |
| objectPath | See clause 7.3.13 |  |  |
| description | See clause 7.3.13 |  |  |
| version | xs:string |  |  |
| name | list of xs:anyURI |  |  |
| URL | xs:anyURI |  |  |
| install |  |  |  |
| uninstall |  |  |  |
| installStatus | m2m:actionStatus |  |  |
| activate |  |  |  |
| deactivate |  |  |  |
| activateStatus | m2m:actionStatus |  |  |

Table D.3-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.4	[memory] Resource

The detailed description can be found in clause D.4 of Architecture TS-0001 [1].

Table D.4-1 Data Type Definition of [memory]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.4-2  Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- |
| mgmtDefinition | Fixed string “memory” |  |  |
| objectID | See clause 7.3.13 |  |  |
| objectPath | See clause 7.3.13 |  |  |
| description | See clause 7.3.13 |  |  |
| memAvailable | xs:unsignedLong | The unit of the attribute shall be Bytes by default. |  |
| memTotal | xs:unsignedLong | The unit of the attribute shall be Bytes by default. |  |

Table D.4-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.7	[battery] Resource

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table D.7-1 Data Type Definition of [battery]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.7-2  Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- |
| mgmtDefinition | Fixed string “firmware” |  |  |
| objectID | See clause 7.3.13 |  |  |
| objectPath | See clause 7.3.13 |  |  |
| description | See clause 7.3.13 |  |  |
| batteryLevel | xsunsignedInt | Represents the current battery level as a percentage (with a range from 0 to 100). |  |
| batteryStatus | m2m:batteryStatus |  |  |

Table D.7-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

## ----------------------- end of change 1 ---------------

## ----------------------- start of change 2 ---------------

#### oneM2M Data Types

Table 6.3.2.1-1 describes oneM2M-specific Data Type definitions.

Table 6.3.2.1-1: oneM2M Simple Data Types

| XSD type name | Type Name | Description |
| --- | --- | --- |
| m2m:id | Generic ID | Used to represent generic IDs generated and used within oneM2M |
| m2m:nodeId | Node ID | Used for Node IDs. The constraints on this type are different from those on Generic IDs |
| m2m:requestId | Request ID | Used for Request IDs. This type includes the ID of the target CSE as well as a part that varies for each ID |
| m2m:externalId | External ID | Used for External IDs. This type includes the ID of the underlying network provider as well as a part that varies for each ID |
| m2m:acpType | ACP Type | Used to represent an AccessControlPolicy identifier. This can be either a URI or an opaque token |
| m2m:nhURI | Non-hierarchical URI | This is used to indicate that the URI cannot be interpreted in an hierarchical manner |
| m2m:resourceType | Resource Type | A Resource Type as defined in [6]. It is defined as an xs:string enumeration. |
| m2m:actionStatus | Action Status | An enumeration type to indicate the result of a action in management. Two xs:string values as enumeration values: Successful Failure Processing |
| m2m:batteryStatus | Battery Status | An enumeration type to indicate the statues of the battery. Values: Normal Charging Charge Complete Damaged Low Battery Not Installed Unknown |

## ----------------------- end of change 2 ---------------

# Comments

Need to harmonize External ID Data Type (see also Table 6.2-1).

No reference reference in this bookmark. Please check and update.