| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | DTLS related mapping |
| Source:* | Hitachi, |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-07-08 |
| Abstract:* | This contribution proposes CoAP protocol binding details. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

7. Security

CoAP itself does not provide protocol primitives for authentication or authorization; where this is required, it can be provided by DTLS.

Just as HTTP is secured using Transport Layer Security (TLS) over TCP, CoAP is secured using Datagram TLS (DTLS) [DTLS 1.2]. DTLS is in practice TLS with added features to deal with the unreliable nature of the UDP transport.

All CoAP messages MUST be sent as DTLS “application data”. For matching an ACK or RST to a CON message or a RST to a NON message: The DTLS session MUST be the same and the epoch MUST be the same.

Devices can close a DTLS connection when they need to recover resources but in general they should keep the connection up for as long as possible. Closing the DTLS connection after every CoAP message exchange is very inefficient.

For matching a response to a request, the DTLS session MUST be the same and the epoch MUST be the same. The response to a DTLS secured request MUST always be DTLS secured using the same security session and epoch.

Editor’s note: WG4 will provide detailed clause numbers WG3 can refer to.

--------------------- End of proposed modified text ---------------------

[DTLS 1.2]	RFC 6347 “Datagram Transport Layer Security Version 1.2”

[TLS-CCM]	RFC 6655 “AES-CCM Cipher Suites for Transport Layer Security (TLS)”

[TLS 1.2]	RFC 5246 “The Transport Layer Security (TLS) Protocol Version 1.2”

[TLS-ECC]	RFC4492 “Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS)”

[TLS-PSK]	RFC 4279 “Pre-Shared Key Ciphersuites for Transport Layer Security (TLS)

[Heartbeat]	RFC 6520 “Transport Layer Security (TLS) and Datagram Transport Layer Security (DTLS) Heartbeat Extension”

# Comments

I hope we can move these kind of details to the Security TS-0003, and this section can direct the reader to that section of TS-0008.

Move to TS-0003

The other bindings will have similar constrains. These details should be in TS-0003, since they will not be specific to CoAP.

Move to TS-0003