| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | CoAP Blockwise Transfer |
| Source:* | Ericsson |
| Contact: | Sumit Singhal, sumit.b.singhal@ericsson.com |
| Date:* | 2014-07-14 |
| Abstract:* | This contribution proposes a new sub-section for CoAP Blockwise transfer. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes new sub-section for CoAP Blockwise Transfer.

--------------------- Start of proposed modified text 1 -------------------

## 2.1	Normative references

…

[3]	IETF draft: “Blockwise transfers in CoAP”, draft-ietf-core-block-15

--------------------- End of proposed modified text 1 --------------------

--------------------- Start of proposed modified text 2 -------------------

### 5.4	Blockwise Transfers

CoAP Block [3] Option shall be used for handling cases where oneM2M resource representations will need to transfer large payloads e.g. firmware, software updates. Instead of relying on IP fragmentation, CoAP Block Option shall be used for transferring multiple blocks of information in multiple request-response pairs.

Using Block Options, larger resource representations can be fragmented and reassembled by CoAP independently of the lower layers as well as the above application. The CoAP Block1 Option shall be used to define the size of the blocks used for oneM2M requests and the CoAP Block2 Option shall be used to define the size of the blocks used for oneM2M responses. Refer [3] for further details.

--------------------- End of proposed modified text 2 --------------------