| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#12.0 |
| Title:* | Delivery resource type definition - Update |
| Source:* | QUALCOMM Incorporated (TIA) |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2014-07-29 |
| Abstract:* | This contribution proposes revised text for Resource Type delivery procedure based on the new template. |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

### 7.3.9	Resource Type delivery

#### 7.3.9.1	Introduction

In order to be able to initiate and manage the execution of data delivery in a resource-based manner, resource type delivery is defined. This resource type shall be used for forwarding requests from one CSE to another CSE when the da parameter in the request is set to ON. The detailed description can be found in clause 9.6.11 in Architecture TS [6].

Table 7.3.9.1-1 Data Type Definition of delivery

| Data Type ID | File Name | Note |
| --- | --- | --- |
| deliveryType | CDT-delivery-v1_0_0-<<date of published>>.xsd |  |

| Table 7.3.9.1-2 Common Attributes on deliveryAttribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | None |  |
| resourceID | NP | O | NP | NP | None |  |
| expirationTime | O | O | O | NP | Default is determined by Hosting CSE policy |  |
| parentID | NP | O | NP | NP | None |  |
| creationTime | NP | O | NP | NP | None |  |
| lastModifiedTime | NP | O | NP | NP | None |  |
| accessControlPolicyIDs | O | O | O | NP | Default is determined by Hosting CSE policy |  |
| labels | O | O | O | NP | Empty |  |
| stateTag | NP | O | NP | NP | 0 |  |

Table 7.3.9.1-3 Resource Specific Attributes on delivery

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| source | M | O | NP | NP | xs:anyURI | None |
| target | M | O | NP | NP | xs:anyURI | None |
| lifespan | M | O | O | NP | xs:dateTime | None |
| eventCat | M | O | O | NP | m2m:eventCat | None |
| deliveryMetaData | M | O | O | NP | m2m: deliveryMetaData | Default is determined by Hosting CSE policy |
| AggregatedRequest | O | O | O | NP | m2m:aggregatedRequest | None |

Table 7.3.9.1-4 Child resources for delivery

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| subscription | variable | 0..n | 7.3.6 |

#### 7.3.9.2	Resource Specific Procedure on CRUD Operations

This sub-clause describes request resource specific procedure on Resource Hosting CSE for CRUD operations.

#### 7.3.9.2.1	Create

The Originator shall be a CSE. This procedure follows the Genetic Resource Create Request Procedure specified in clause 7.2.1.2 with the following exceptions:

#### The Originator shall be a CSE.

#### The Originator shall use a blocking request (i.e. rt=blockingRequest).

#### 7.3.9.2.2	Retrieve

#### The Originator shall be a CSE. This procedure follows the Genetic Resource Retrieve Request Procedure specified in clause 7.2.1.2 with the following exceptions:

#### The Originator shall use a blocking request (i.e. rt=blockingRequest).

#### 7.3.9.2.3	Update

The Originator shall be a CSE. This procedure follows the Genetic Resource Update Request Procedure specified in clause 7.2.1.2 with the following exceptions:

#### The Originator shall be a CSE.

#### The Originator shall use a blocking request (i.e. rt=blockingRequest).

#### 7.3.9.2.4	Delete

The Originator shall be a CSE. This procedure follows the Genetic Resource Delete Request Procedure specified in clause 7.2.1.2 with the following exceptions:

#### The Originator shall be a CSE.

#### The Originator shall use a blocking request (i.e. rt=blockingRequest).