| INPUT CONTRIBUTION |
| --- |
| Group Name:* | MAS/PRO#12 |
| Title:* | TS-0004 Annex.D Cleanup |
| Source:* | QUALCOMM Incorporated (TIA) |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2014-07-30 |
| Abstract:* | This contribution proposes changes to Annex.D to address Editor’s Notes for chdm-related management instances and alignment with the latest TS-0001 v0.8.0. |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes moditications to Annex D. The modifications are;

- Changed the Annex title based on the TS-0001 Annex D

- References to Arc TS are corrected

- Missing <mgmtObj> resource instances are added

  - firmware

  - software

  - memory

  - areaNwkInfo

  - areNwkDeviceInfo

  - battery

  - deviceInfo

  - deviceCapability

  - reboot

  - eventLog

- Common attribute table based on the new template is added

- Resource-specific attributes tables based on the new template are added

- Data types, defaults values have been filled

- Removed Editor’s Notes from the old template.

Changes for revision R05:

- Removed Table D.12-2 with common attributes. Included a reference to clause 7.3.14 (mgmtObj) where these common attributes should be specified.

- Re-introduced square brackets “[cmdhxxxxx]” for resources in section titles

- Included more explanation into the “Defaults and constraints” column for mgmtLink and some other attributes

- Added the specific data types used for the resources in Annex D.12 to the table in clause 6.3.2

- Renamed notation of data type “listOfM2mId” to “listOfM2MID”

- Redefined data type listOfBoolean as enumerated type

Changes for revision R06:

- Correction of multiplicity of the mgmtLink in the [cmdhNetworkAccessRules] resource (from “1 or more” to “zero or more”

- listOfBoolean redefined back to a list data type rather than enumerated data type in the tables in clause 6.3.2

--------------------- Start of proposed modified text, part 1 -------------------

(Normative): <mgmtObj> Resource Instances

## Void

## Resource [firmware]

## Editor’s Note: This section needs to be assigned.

## Resource [software]

Editor’s Note: This section needs to be assigned.

## Resource [memory]

Editor’s Note: This section needs to be assigned.

## Resource [areaNwkInfo]

Editor’s Note: This section needs to be assigned.

## Resource [areaNwkDeviceInfo]

Editor’s Note: This section needs to be assigned.

## Resource [battery]

Editor’s Note: This section needs to be assigned.

## Resource [deviceInfo]

Editor’s Note: This section needs to be assigned.

## Resource [deviceCapability]

Editor’s Note: This section needs to be assigned.

## Resource [reboot]

Editor’s Note: This section needs to be assigned.

## Resource [eventLog]

Editor’s Note: This section needs to be assigned.

## Resource [cmdhPolicy]

The Resource [cmdhPolicy] represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator contains the ec (event category) parameter but not all other CMDH parameters.

The detailed description can be found in clause D.12 of Architecture TS-0001 [6].

Table D.12-1: Data Type Definition of [cmdhPolicy]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhPolicyType | CDT-cmdhPolicy-v1_0_0-<<date of published>>.xsd |  |

The common attributes of the resource type <mgmtObj> as described in clause 7.3.14 apply to the resource [cmdhPolicy] and to the resources in subclauses D.12.1 to D.12.8 below. Note that the optional <subscription> child resources are not used for CMDH policies.

Table D.12-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhPolicy” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| Description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| Name | M | O | O | NP | xs:string | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | 1 link to [cmdhDefaults] resource instance, 1 or more link(s) to [cmdhLimits] resource instance(s), 1 or more link(s) to [cmdhNetworkAccessRules] resource instance(s), 1 or more link(s) to [cmdhBuffer] resource instance(s) |

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### Resource [activeCmdhPolicy]

The resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies.

The detailed description can be found in clause D.12.1 of Architecture TS-0001 [6].

Table D.12.1-1: Data Type Definition of [activeCmdhPolicy]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| activeCmdPolicyType | CDT-activeCmdhPolicy-v1_0_0-<<date of published>>.xsd | At most one Policy instance shall be enabled at a time. |

Table D.12.1-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “activeCmdhPolicy” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| Description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | 1 link to the instance of [cmdhPolicy] resource that is active |

### Resource [cmdhDefaults]

The resource [cmdhDefaults] defines default CMDH policy values. The detailed description can be found in clause D.12.2 of Architecture TS-0001 [6].

Table D.12.2-1: Data Type Definition of [cmdhDefaults]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhDefaultsType | CDT-cmdhDefaults-v1_0_0-<<date of published>>.xsd |  |

Table D.12.2-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhDefaults” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | 1 or more link(s) to [cmdhDefEcValue] resource instance(s) |

### Resource [cmdhDefEcValue]

The resource [cmdhDefEcValue] represents a value for the ec (event category) parameter of an incoming request. The detailed description can be found in clause D.12.3 of Architecture TS-0001 [6].

Table D.12.3-1: Data Type Definition of [cmdhDefEcValue]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhDefEcValueType | CDT-cmdhDefEcValue-v1_0_0-<<date of published>>.xsd |  |

Table D.12.3-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhDefEcValue” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| defEcValue | M | O | O | NP | m2m:eventCat | None |
| requestOrigin | M | O | O | NP | m2m:listOfM2MID | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |

### Resource [cmdhEcDefParamValues]

The resource [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request. The detailed description can be found in clause D.12.4 of Architecture TS-0001 [6].

Table D.12.4-1: Data Type Definition of [cmdhEcDefParamValues]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhEcDefParamValuesType | CDT-cmdhEcDefParamValues-v1_0_0-<<date of published>>.xsd |  |

Table D.12.4-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhEcDefParamValues” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| applicableEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| defaultRequestExpTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultResultExpTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultOpExecTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultRespPersistence | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultDelAggregation | M | O | O | NP | xs:boolean | None |

### Resource [cmdhLimits]

The Resource [cmdhLimits] represents limits for CMDH related parameter values. The detailed description can be found in clause D.12.5 of Architecture TS-0001 [6].

Table D.12.5-1: Data Type Definition of [cmdhLimits]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhLimitsType | CDT-cmdhLimits-v1_0_0-<<date of published>>.xsd |  |

Table D.12.5-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhLimits” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| requestOrigin | M | O | O | NP | m2m:listOfM2MID | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |
| limitsEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| limitsRequestExpTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsResultExpTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsOpExecTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsRespPersistence | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsDelAggregation | M | O | O | NP | m2m:listOfBoolean | None |

### Resource [cmdhNetworkAccessRules]

The resource [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE. The detailed description can be found in clause D.12.6 of Architecture TS-0001 [6].

Tabla D.12.6-1:Type Definition of [cmdhNetworkAccessRules]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhNetworkAccessRulesType | CDT-cmdhNetworkAccessRules-v1_0_0-<<date of published>>.xsd |  |

Table D.12.6-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhNetworkAccessRules” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1.2 |
| Description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| applicableEventCategories | M | O | O | NP | m2m:listOfEventCat | None |
| mgmtLink | O | O | O | NP | m2m:mgmtLink | Zero or more links to [cmdhNwAccessRule] resource instance(s) |

### Resource [cmdhNwAccessRule]

The resource [cmdhNwAccessRule] defines limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests. The detailed description can be found in clause D.12.7 of Architecture TS-0001 [6].

Table D.12.7-1 Data Type Definition of [cmdhNwAccessRule]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhNwAccessRuleType | CDT-cmdhNwAccessRule-v1_0_0-<<date of published>>.xsd |  |

Table D.12.7-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhNwAccessRule” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| targetNetwork | M | O | O | NP | m2m:listOfM2MID | None |
| minReqVolume | M | O | O | NP | xs:nonNegativeInteger | Unit: byte |
| backOffParameters | M | O | O | NP | m2m: backOffParameters | Ordered sequence of 3 values: backoffTime, backoffTimeIncrement, maximumBackoffTime, Unit: ms |
| otherConditions | O | O | O | NP | xs:string | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | Link to an instance “allowedSchedule” of a <schedule> resource |

Editor’s Note: The otherConditions attribute needs to be clarified  in TS-0001 before we can determine the data type.

## Resource [cmdhBuffer]

The resource [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE. The detailed description can be found in clause D.12.8 of Architecture TS-0001 [6].

Table D.12.8-1: Data Type Definition of [cmdhBuffer]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhBufferType | CDT-cmdhBuffer-v1_0_0-<<date of published>>.xsd |  |

Table D.12.8-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | “cmdhBuffer” |
| objectID | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | xs:string | See Table 7.3.14.1-2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1-2 |
| applicableEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| maxBufferSize | M | O | O | NP | xs:nonNegativeInteger | Unit: byte |
| storagePriority | M | O | O | NP | xs:positiveInteger | The range of storage priority is from 1 to 10. |

--------------------- End of proposed modified text, part 1 -------------------

--------------------- Start of proposed modified text, part 2 -------------------

Note: the proposed additions are relative to DRAFT_TS-0004_CoreProtocol_V0_5_4(rm).doc

### 6.3.2	Additional Data Types used in oneM2M

This clause defines the  data types that are defined by oneM2M for use in the oneM2M API.

Editor's Note: Tables under this clause need to be updated, reflecting new resource type definitions in clause 7.3 and Annex. D.

#### Simple Data Types

Table 6.3.2.1-1 describes oneM2M-specific simple data type definitions.

Table 6.3.2.1-1: oneM2M Simple Data Types

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |
| m2m:id | Generic ID | (TBD) | Used to represent generic IDs generated and used within oneM2M |
| m2m:nodeId | Node ID | (TBD) | Used for Node IDs. The constraints on this type are different from those on Generic IDs |
| m2m:requestId | Request ID | (TBD) | Used for Request IDs. This type includes the ID of the target CSE as well as a part that varies for each ID |
| m2m:acpType | ACP Type | (TBD) | Used to represent an AccessControlPolicy identifier. This can be either a URI or an opaque token |
| m2m:networkaccessIdentifier | Network Access Identifier | user@realm | The networkaccssIdentifier is a standard way of identifying users who request access to a network as specified at IETF RFC 4282 [18]. |
| m2m:mgmtLink | Management Link | mynode/cmdhPolicyInstance1 | m2m:id restricted to allowed types of instances of resource type <mgmtObj> |
| m2m:listOfM2MID | List of M2M identifiers |  | xs:list of elements of data type m2m:id |
| m2m:listOfEventCat | List of (applicable) Event Categories | (default bestEffort latest 1 10) | xs:list of elements of data type m2m:eventCat |
| m2m:listOfMinMax | List of Time Limits | (10 2560) | xs:list of two xs:long values defining min and max limits of time intervals in units of milliseconds (value -1 representing infinite time) |
| m2m:backOffParameters | List of Backoff Parameters | (100 100 2000) | Ordered sequence of 3 values of data type xs:nonNegativeInteger representing backoffTime, backoffTimeIncrement, maximumBackoffTime (in units of milliseconds) |
| m2m:listOfBoolean | List of allowed values in the boolean value space domain | “True“, "False“, or "True False“ | Used to define the value space of the attribute “limitsDelAggregation by imposing restrictions on the value space of xs:boolean |

#### 6.3.2.2 Enumeration Data Types

Table  6.3.2.2-1 describes oneM2M-specific enumeration data type definitions.

Table 6.3.2.2-1: oneM2M Enumeration Data Types

| XSD type name | Values | Description |
| --- | --- | --- |
| m2m:resourceType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, |  |
| m2m:commaList | TBD | Used for supportedResourceType attribute of <CSEBase> resource. |
| m2m:cseTypeID | “IN-CSE”, “MN-CSE”, “ASN-CSE” | Used for cseType attribute of <CSEBase> resource. |
| m2m:locationSource | “Network-based”, “Device-based”, “Sharing-based” | Used for locationSource attribute of <loationPolicy> resource. |
| m2m:eventCatType | “default“ “immediate”, “bestEffort”, “latest” | Used for ec parameter in request and eventCat attribute of <delivery> resource and cmdh policy resource types. |
| m2m:operation | “Create”, “Retrieve”, “Update”, “Delete”, “Notify” | Used for op parameter in request and operation attribute in <request> resource |
| m2m:responseType | “nonBlockingRequestSynch”, “nonBlckingRequestAsynch”, “blockingRequest” | Used for rt parameter in request and operation attribute in <request> resource |
| m2m:resultContent | “attributes”, “attributes+childResources”, “childResources”, “nothing”, “originalResources” | Used for rc parameter in request |
| m2m:discResType | “hierarchical”, “non-hierarchical”, “cseID+resourceID” |  |
| m2m:statusCode | See clause 6.5.4 | Used for cs parameter in response |
| m2m:requestStatus | TBD | Used for requestStatus attribute in <request> resource. |
| m2m:operationResult | TBD | Used for operationResult attribute in <request> resource. |
| m2m:memberType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, “mixed” | Used for memberType attribute in <member> resource. |
| m2m:consistencystrategy | TBD | Used for consistencyStrategy attribute in <group> resource. |
| m2m:cmdType | “RESET”, “REBOOT”, “UPLOAD”, “DOWNLOAD”, “SOFTWAREINSTALL”, “SOFTWAREUNINSTALL” | Used for cmdType attribute in <mgmtCmd> resource. |
| m2m: execReqArgsListType | TBD | Used for execReqArgsListType attribute in <mgmtCmd> and <execInstance resource. |
| m2m:execModeType | “IMMEDIATEONCE”, “IMMEDIATEREPEAT”, “RANDOMONCE”, “RANDOMREPEAT” | Used for execModeType attribute in <mgmtCmd> and <execInstance> resource. |
| m2m:execStatusType | “INITATED”, “STARTED”, “FINISHED”, “CANCELLING”, “CANCELLED” | Used for execStatusType attribute in <execInstance> resource. |
| m2m:pendingNotification | “sendLatest”, “sendAllPending” | This is used for pendingNotification attribute in <subscription> resource. |
| m2m:notificationContentType | “modifiedAttributes”, “wholeResource”, “referenceOnly” | This is used for notificationConentType attribute in <subscription> resource. |
| m2m:resourceStatus | “childCreated”, “childDeleted”, “updated”, “deleted” | This is used for eventNotificationCriteria. |
| m2m:operationMonitor | “Create”, “Retrieve”, “Update”, “Delete” | This is used for eventNotificationCriteria. |
| m2m:attribute | all common and resource specific attribute names specified in clause 7.3 |  |
| m2m:mgmtDefinition | "firmware” "software” "memory” "areaNwkInfo” "areaNwkDeviceInfo” "battery” "deviceInfo” "deviceCapability” "reboot“ "eventLog“ "cmdhPolicy", "activeCmdhPolicy", "cmdhDefaults", "cmdhBuffer", "cmdhLimits", "cmdhDefEcValue", "cmdhEcDefParamValues", "cmdhNetworkAccessRules", "cmdhNwAccessRule" |  |

--------------------- End of proposed modified text, part 2 -------------------

# Comments

This is RO attribute in Annex D.12.1. Should this be RW?

we don’t need this, right?