| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#3, WG#5 |
| Title:* | resources for mgmtObj |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | <2014-07-15> |
| Abstract:* | This contribution provides resource instance description for mgmtObj resource instances firmware, software, memory and battery in Annex D. |
| Agenda Item:* | PRO#12 and MAS#12 |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve to add proposed text to TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes to add the following description of resource data types in the annex for instances of mgmtObj.

## ----------------------- start of change 1 ---------------

#### D.2	[firmware] Resource

The detailed description can be found in clause D.2 of Architecture TS-0001 [1].

Table D.2-1 Data Type Definition of [firmware]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.2-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “firmware” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | xs:string |  |
| URL | M | O | O | NP | xs:anyURI |  |
| update | M | NP | O | NP | TBD |  |
| updateStatus | NP | O | O | NP | m2m:actionStatus | m2m:actionStatus is an enumeration type to indicate the result of a action in management. Values: Successful Failure InProcess |

Table D.2-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.3	[software] Resource

The detailed description can be found in clause D.3 of Architecture TS-0001 [1].

Table D.3-1 Data Type Definition of [software]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.3-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “software” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | list of xs:anyURI |  |
| URL | M | O | O | NP | xs:anyURI |  |
| install | NP | NP | O | NP | TBD |  |
| uninstall | NP | NP | O | NP | TBD |  |
| installStatus | NP | O | NP | NP | m2m:actionStatus |  |
| activate | NP | NP | O | NP | TBD |  |
| deactivate | NP | NP | O | NP | TBD |  |
| activateStatus | NP | O | NP | NP | m2m:actionStatus |  |

Table D.3-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.4	[memory] Resource

The detailed description can be found in clause D.4 of Architecture TS-0001 [1].

Table D.4-1 Data Type Definition of [memory]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.4-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “memory” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| memAvailable | M | O | O | NP | xs:unsignedLong | Range: Larger than 0 Unit: Byte, KB, MB |
| memTotal | M | O | O | NP | xs:unsignedLong | Range: Larger than 0 Unit: Byte, KB, MB |

Editor’s Note: How unit is carried in the attribute is FFS.

Table D.4-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### D.7	[battery] Resource

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table D.7-1 Data Type Definition of [battery]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.7-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “memory” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| batteryLevel | M | O | O | NP | xs：unsignedInt | Range: 0-100 Unit: Percent |
| batteryStatus | M | O | O | NP | m2m:batteryStatus | m2m:batteryStatus is an enumeration type to indicate the statues of the battery. Values: Normal: The battery is operating normally and not on power. Charging: The battery is currently charging. Charge Complete: The battery is fully charged and still on power. Damaged: The battery has some problem. Low Battery: The battery is low on charge. Not Installed: The battery is not installed. Unknown: The battery information is not available. |

Table D.7-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

## ----------------------- end of change 1 ---------------