| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG#3, WG#5 |
| Title:* | resources for mgmtObj |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | <2014-07-15> |
| Abstract:* | This contribution provides resource instance description for mgmtObj resource instances firmware, software, memory and battery in Annex D. |
| Agenda Item:* | PRO#12 and MAS#12 |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve to add proposed text to TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes to add the following description of resource data types in the annex for instances of mgmtObj.

## ----------------------- start of change 1 ---------------

#### D.2	[firmware] Resource

The detailed description can be found in clause D.2 of Architecture TS-0001 [1].

Table D.2-1 Data Type Definition of [firmware]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.2-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “firmware” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | xs:string |  |
| URL | M | O | O | NP | xs:anyURI |  |
| update | M | NP | O | NP | TBD |  |
| updateStatus | NP | O | O | NP | m2m:actionStatus |  |

#### D.3	[software] Resource

The detailed description can be found in clause D.3 of Architecture TS-0001 [1].

Table D.3-1 Data Type Definition of [software]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.3-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “software” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | list of xs:anyURI |  |
| URL | M | O | O | NP | xs:anyURI |  |
| install | NP | NP | O | NP | TBD |  |
| uninstall | NP | NP | O | NP | TBD |  |
| installStatus | NP | O | NP | NP | m2m:actionStatus |  |
| activate | NP | NP | O | NP | TBD |  |
| deactivate | NP | NP | O | NP | TBD |  |
| activateStatus | NP | O | NP | NP | m2m:actionStatus |  |

#### D.4	[memory] Resource

The detailed description can be found in clause D.4 of Architecture TS-0001 [1].

Table D.4-1 Data Type Definition of [memory]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.4-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “memory” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| memAvailable | M | O | O | NP | xs:unsignedLong | Unit: Byte. |
| memTotal | M | O | O | NP | xs:unsignedLong | Unit: Byte. |

#### D.7	[battery] Resource

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table D.7-1 Data Type Definition of [battery]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID |  | some note texts can be added here |

Table D.7-2  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | Fixed string “memory” |  |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| batteryLevel | M | O | O | NP | xs：unsignedInt | Range: 0-100 Unit: Percent |
| batteryStatus | M | O | O | NP | m2m:batteryStatus |  |

## ----------------------- end of change 1 ---------------

## ----------------------- start of change 2 ---------------

#### Enumeration Data Types

Table 6.3.2.2-1 describes oneM2M-specific enumeration data type definitions.

Table 6.3.2.2-1: oneM2M Enumeration Data Types

| XSD type name | Values | Description |
| --- | --- | --- |
| m2m:resoureType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, |  |
| m2m:commaList | TBD | Used for supportedResourceType attribute of <CSEBase> resource. |
| m2m:cseTypeID | “IN-CSE”, “MN-CSE”, “ASN-CSE” | Used for cseType attribute of <CSEBase> resource. |
| m2m:locationSource | “Network-based”, “Device-based”, “Sharing-based” | Used for locationSource attribute of <loationPolicy> resource. |
| m2m:eventCatType | “immediate”, “bestEffort”, “latest” | Used for ec parameter in request and eventCat attribute of <delivery> resource. |
| m2m:operation | “Create”, “Retrieve”, “Update”, “Delete”, “Notify” | Used for op parameter in request and operation attribute in <request> resource |
| m2m:responseType | “nonBlockingRequestSynch”, “nonBlckingRequestAsynch”, “blockingRequest” | Used for rt parameter in request and operation attribute in <request> resource |
| m2m:resultContent | “attributes”, “attributes+childResources”, “childResources”, “nothing”, “originalResources” | Used for rc parameter in request |
| m2m:discResType | “hierarchical”, “non-hierarchical”, “cseID+resourceID” |  |
| m2m:statusCode | See clause 6.5.4 | Used for cs parameter in response |
| m2m:requestStatus | TBD | Used for requestStatus attribute in <request> resource. |
| m2m:operationResult | TBD | Used for operationResult attribute in <request> resource. |
| m2m:memberType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, “mixed” | Used for memberType attribute in <member> resource. |
| m2m:consistencystrategy | TBD | Used for consistencyStrategy attribute in <group> resource. |
| m2m:cmdType | “RESET”, “REBOOT”, “UPLOAD”, “DOWNLOAD”, “SOFTWAREINSTALL”, “SOFTWAREUNINSTALL” | Used for cmdType attribute in <mgmtCmd> resource. |
| m2m: execReqArgsListType | TBD | Used for execReqArgsListType attribute in <mgmtCmd> and <execInstance resource. |
| m2m:execModeType | “IMMEDIATEONCE”, “IMMEDIATEREPEAT”, “RANDOMONCE”, “RANDOMREPEAT” | Used for execModeType attribute in <mgmtCmd> and <execInstance> resource. |
| m2m:execStatusType | “INITATED”, “STARTED”, “FINISHED”, “CANCELLING”, “CANCELLED” | Used for execStatusType attribute in <execInstance> resource. |
| m2m:actionStatus | “SUCCESSFUL”, “FAILURE”, “IN-PROCESS” | An enumeration type to indicate the result of a action in management. |
| m2m:batteryStatus | “NORMAL”, “CHARGING”, “CHARGE-COMPLETE”, “DAMAGED”, “LOW-BATTERY”, “NOT-INSTALLED”, “UNKNOWN” | An enumeration type to indicate the statues of the battery. Values: Normal: The battery is operating normally and not on power. Charging: The battery is currently charging. Charge Complete: The battery is fully charged and still on power. Damaged: The battery has some problem. Low Battery: The battery is low on charge. Not Installed: The battery is not installed. Unknown: The battery information is not available. |

## ----------------------- end of change 2 ---------------

# Comments

we don’t need this, right?