| CHANGE REQUEST |
| --- |
| Group Name:* | PRO#12 |
| Title: * | Synchronization of announced attribute |
| Source:* | ZTE, LG Electronics |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-07-28 |
| Contact:* | Hao Wu, ZTE, wu.hao18@zte.com.cn Rajesh Bhalla, ZTE, rabhalla@ztetx.com Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution corrects the procedures for the resource announcement. |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0004, ver 0.5.3 |
| Clauses/Sub Clauses* | 7.2.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The clause 9.6.25 of TS0001state:

“Synchronization between the attributes announced by the original resource and the announced resource is the responsibility of the original resource hosting CSE”

This contribution is trying to cover this in TS-0004.

### -----------------------Start of Change 1-------------------------------------------

##### 7.2.2.2.9	Update the addressed resource

An existing and accessible resource is addressed. For attributes that are not included in the content parameter, the hosting CSE shall not change such attributes. For attributes provided in the content parameter, The content of its attributes shall be updated with the following rules shall be applied:

If the announceTo attribute of the resource is updated, the hosting CSE  shall perform the resource announcement or de-announcement as specified in the clause 7.2.2.4.

If announceTo attribute is present in the resource, and if the attribute marked with MA or the attribute included in the announcedAttribute attribute is updated or deleted, the hosting CSE shall perform "synchronize the announced attribute " as specified in the clause 7.2.2.2.X.

M attribute

If the provided value is accepted, the server shall use the provided value in the resource representation of the updated resource.

O attribute

If a value is provided and the value is accepted, the server shall use the provided value in the resource representation of the updated resource.

If the attribute is not provided or accepted, but the attribute is marked M in the response, the hosting CSE shall assign default value or assign value based on local policy.

If this attribute is provided in the content parameter and does not exist in the target resource, the hosting CSE shall create such attribute with the provided value.

If this attribute is set to NULL in the content parameter and exists in the target resource, the hosting CSE shall delete such attribute if the deletion of the attribute is allowed by the local policy.

NP attribute

If the attribute is not present in the resource representation in the UPDATE request and the response column is marked M then the hosting CSE shall not update the attribute value. There is only one exception to this rule and that is the lastModifiedTime attribute. The hosting CSE shall set the lastModifiedTime to the current time whenever an update primitive is received.

If the attribute is present in the resource representation in the UPDATE request the presented value shall be ignored, i.e. the hosting CSE shall never update its resource representation based on the presence of an NP attribute value in an update.

If the expirationTime attribute is present and modified by the procedure and it is set to a non-negative time, then an expiration timer shall be re-started by the hosting CSE. At timer expiration the related resource is deleted by "Delete the addressed resource".

### -----------------------End of Change 1---------------------------------------------

### -----------------------Start of Change 2---------------------------------------------

##### 7.2.2.2.X	Synchronize the announced attribute

The hosting CSE shall:

Compose the UPDATE Request primitive as follows:

  - if the attribute that is marked with MA ,or included in the announcedAttribute attribute is updated, include the attribute with updated value.

  - if the attribute that is marked with MA ,or included in the announcedAttribute attribute is deleted, include the attribute with value setting to NULL.

Send a UPDATE Request to all CSE(s) represented by URI(s) in the announceTo attribute of the original resource.

Wait for Response primitive.

### -----------------------End of Change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?