| CHANGE REQUEST |
| --- |
| Group Name:* | PRO#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-16 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | Management Resource specific procedures |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0004, ver 0.5.2 |
| Clauses/Sub Clauses* | 6.5.4.1.x |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes the Management resource specific procedures regarding battery, deviceInfo, deviceCapability, reboot and eventLog.

### -----------------------Start of New Text 1-------------------------------------------

##### 6.5.4.1.X		[battery] Resource

#### 6.5.4.1.X.1	Introduction

The Resource [battery] is used to provide information regarding the battery.

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table 6.5.4.1.X-1: Data Type Definition of [battery]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-battery-v1_0_0-<<date of published>>.xsd |  |

Table 6.5.4.1.X-2:  Applicable Common Attributes on [battery]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | “mgmtObj” |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 6.5.4.1.X-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| mgmtDefinition | M | M | O | NP | See table 7.3.13.1-2 | "battery" |  |
| objectID | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| objectPath | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |  |
| batteryLevel | M | M | O | NP | xs:nonNegativeInteger | a range from 0 to 100 |  |
| batteryStatus | M | M | O | NP | xs:nonNegativeInteger | This attribute shall have one of the following values: 0: Normal. The battery is operating normally and not currently charging. 1: Charging. The battery is charging 2: Charge Complete. The battery is fully charged. 3: Damaged. The battery has some problem. 4: Not Installed. The battery is not installed. The value in the batteryLevel attribute shall be ignored. 5: Unknown. battery information is not available. The value in the batteryLevel attribute shall be ignored. |  |

Table 6.5.4.1.X.1-3: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### 6.5.4.1.X.2	Operations

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of New Text 1---------------------------------------------

### -----------------------Start of New Text 2-------------------------------------------

##### 6.5.4.1.X	[deviceInfo] Resource

#### 6.5.4.1.X.1	Introduction

The Resource [deviceInfo] is used to provide information regarding the device.

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table 6.5.4.1.X.1-1: Data Type Definition of [deviceInfo]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-deviceInfo-v1_0_0-<<date of published>>.xsd |  |

Table 6.5.4.1.X.1-2:  Applicable Common Attributes on [deviceInfo]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | “mgmtObj” |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 6.5.4.1.X.1-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| mgmtDefinition | M | M | O | NP | See table 7.3.13.1-2 | "deviceInfo" |  |
| objectID | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| objectPath | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |  |
| deviceLabel | M | M | O | NP | xs:string |  |  |
| Manufacturer | M | M | O | NP | xs:string |  |  |
| Model | M | M | O | NP | xs:string |  |  |
| deviceType | M | M | O | NP | xs:string |  |  |
| fwVersion | M | M | O | NP | xs:string |  |  |
| swVersion | M | M | O | NP | xs:string |  |  |
| hwVersion | M | M | O | NP | xs:string |  |  |

Table D.5-4: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### 6.5.4.1.X.2	Operations

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of New Text 2---------------------------------------------

### -----------------------Start of New Text 3-------------------------------------------

##### 6.5.4.1.X	[deviceCapability] Resource

#### 6.5.4.1.X.1	Introduction

The Resource [deviceCapability] is used to provide information regarding the device.

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table 6.5.4.1.X.1-1: Data Type Definition of [deviceCapability]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-deviceCapability-v1_0_0-<<date of published>>.xsd |  |

Table 6.5.4.1.X.1-2:  Applicable Common Attributes on [deviceCapability]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | “mgmtObj” |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 6.5.4.1.X.1-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| mgmtDefinition | M | M | O | NP | See table 7.3.13.1-2 | "deviceCapability" |  |
| objectID | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| objectPath | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |  |
| capabilityName | M |  | O | NP | xs:string |  |  |
| attached | M | M | O | NP | xs:boolean | true: currently attached to the device false: currently dettached to the device |  |
| capabilityActionStatus | M | M | O | NP | xs:boolean | true: the device capability is enabled false: the device capability is disabled |  |
| enable | O | O | O | NP | TBD | this attribute shall not have any values |  |
| disable | O | O | O | NP | TBD | this attribute shall not have any values |  |

Table D.5-4: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### 6.5.4.1.X.2	Operations

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of New Text 3---------------------------------------------

### -----------------------Start of New Text 4-------------------------------------------

##### 6.5.4.1.X	[reboot] Resource

#### 6.5.4.1.X.1	Introduction

The Resource [reboot] is used to provide information regarding the device.

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table 6.5.4.1.X.1-1: Data Type Definition of [reboot]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-reboot-v1_0_0-<<date of published>>.xsd |  |

Table 6.5.4.1.X.1-2:  Applicable Common Attributes on [reboot]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | “mgmtObj” |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 6.5.4.1.X.1-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| mgmtDefinition | M | M | O | NP | See table 7.3.13.1-2 | "reboot" |  |
| objectID | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| objectPath | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |  |
| reboot | M | M | O | NP | TBD | this attribute shall not have any values |  |
| factoryReset | M | M | O | NP | TBD | this attribute shall not have any values |  |

Table D.5-4: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### 6.5.4.1.X.2	Operations

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of New Text 4---------------------------------------------

### -----------------------Start of New Text 5-------------------------------------------

##### 6.5.4.1.X	[eventLog] Resource

#### 6.5.4.1.X.1	Introduction

The Resource [eventLog] is used to provide information regarding the device.

The detailed description can be found in clause D.7 of Architecture TS-0001 [1].

Table 6.5.4.1.X.1-1: Data Type Definition of [eventLog]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-eventLog-v1_0_0-<<date of published>>.xsd |  |

Table 6.5.4.1.X.1-2:  Applicable Common Attributes on [eventLog]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | “mgmtObj” |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 6.5.4.1.X.1-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| mgmtDefinition | M | M | O | NP | See table 7.3.13.1-2 | "eventLog" |  |
| objectID | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| objectPath | M | M | O | NP | See table 7.3.13.1-2 |  |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |  |
| logTypeId | M | M | O | NP | xs:string |  |  |
| logData | M | M | O | NP | m2m:logData | See table 6.3.2.3-1 |  |
| logActionStatus | M | M | O | NP | xs:boolean | true: the event is currently logged false: the event is not currenty logged |  |
| logStart | M | M | O | NP | TBD | this attribute shall not have any values |  |
| logStop | M | M | O | NP | TBD | this attribute shall not have any values |  |

Table D.5-4: Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <subscription> | xs:anyURI | 9.6.8 |

#### 6.5.4.1.X.2	Operations

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of New Text 4---------------------------------------------

### -----------------------Start of New Text 5---------------------------------------------

#### 6.3.2.3		Complex Data Types

Table 6.3.2.3-1 describes oneM2M-specific complex data type definitions.

Table 6.3.2.3-1: oneM2M Complex Data Types

| XSD type name | Element | Element Data Type | Description |
| --- | --- | --- | --- |
| xs:logData | type | xs:string | used to describe the event type |
|  | timestamp | xs:dateTime | used to indicate the date and time when the event occurs |
|  | info | xs:string | used to provide additional information regarding the event. The format of this element depends on the implementation. |

### -----------------------End of New Text 5---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?