| CHANGE REQUEST |
| --- |
| Group Name:* | PRO#12 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-7-16 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution provides the procedure related to the announced resource. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0004, ver 0.5.2 |
| Clauses/Sub Clauses* | 7.3.X |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides the procedure related to the announced resource.

### -----------------------Start of change 1-------------------------------------------

### 7.3.X	Announced Resource Type

### 7.3.X.1 Introduction

A resource can be announced to one or more remote CSEs to inform the remote CSEs of the existence of the original resource. An announced resource can have a limited set of attributes and a limited set of child resources from the original resource.  The announced resource includes a link to the original resource hosted by the original resource-hosting CSE.

All announced resources has the same procedures regardless of the announced resource types.

Table 7.3.X.1-1: Data Type Definition of Announced Resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-accessControlPolicy-v1_0_0-<<date of published>>.xsd CDT-remoteCSE-v1_0_0-<<date of published>>.xsd CDT-AE-v1_0_0-<<date of published>>.xsd CDT-container-v1_0_0-<<date of published>>.xsd CDT-contentInstance-v1_0_0-<<date of published>>.xsd CDT-schedule-v1_0_0-<<date of published>>.xsd CDT-locationPolicy-v1_0_0-<<date of published>>.xsd CDT-group-v1_0_0-<<date of published>>.xsd CDT- accessControlPolicy-v1_0_0-<<date of published>>.xsd |  |

Table 7.3.X.1-2:  Applicable Common Attributes on Announced Resource

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | M | O | NP | the resource type of the announced resource shall be provided. |  |
| resourceID | M | M | O | NP |  |  |
| parentID | M | M | O | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | O | O | O | NP |  |  |
| expirationTime | M | M | O | NP |  |  |
| lastModifiedTime | M | M | O | NP |  |  |
| labels | O | O | O | NP |  |  |
| link | M | M | O | NP |  |  |

Each announced resource type has the resource specific attributes that is the subset of the original resource.

| Attribute Name | Optionality | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- | --- |
|  | C | R | U | D |  |  |  |
| Attribute marked with MA | M | M | O | NP | the same data type defined at the original resource | this attribute shall be set to the same value with the attribute at the original resource |  |
| Attribute marked with OA | O | O | O | NP | the same data type defined at the original resource | this attribute shall be set to the same value with the attribute at the original resource |  |

### 7.3.X.2		Resource Specific Procedure on CRUD Operations

This clause describes announced resource specific procedure on Resource Hosting CSE for CRUD operations.

### 7.3.X.2.1	Create

Only the original resource hosting CSE shall create the announced resource as specified at the clause 7.2.2.2.12. The AE or other CSE can trigger the creation of the announced resource by using the announceTo attribute as specified in the clause 7.2.2.2.12.

### 7.3.X.2.2.	Retrieve

Originator: shall use the generic resource retrieve request procedure specified in the clause 7.2.1.2.2, and only for the announced resource, the rc information can be set to "original-resource". To set the rc information to "original-resource", In the Orig-R-1.0 step, the Originator compose the Request primitive with the rc information set to "original-resource".

Receiver: shall use the generic resource retrieve request procedure specified in the clause 7.2.1.2.2. In case of the rc information is set to the "original-resource", the Rcv-R-7.0 shall be changed as follows:

Rcv-R-7.0	"Read the original resource whose address is provided by the link attribute of the announced resource"

### 7.3.X.2.3.	Update

Only the original resource hosting CSE shall update the announced attribute by using the procedure given in the clause 7.2.1.2.3.

### 7.3.X.2.4.	Delete

Only the original resource hosting CSE shall delete the announced resource as specified at the clause 7.2.2.2.13. The AE or other CSE can trigger the deletion of the announced resource by using the announceTo attribute as specified in the clause 7.2.2.2.13.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?