| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO # 12 |
| Title:* | HTTP header mapping |
| Source:* | LG Electronics |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com |
| Date:* | 2014-07-21 |
| Abstract:* | normative text for HTTP header mapping |
| Agenda Item:* | TBD |
| Work item(s): | WI 0013 |
| Document(s) Impacted* | oneM2M-TS-0009 HTTP Binding TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Continuing from clause 5 – what are the mapping information specified in HTTP binding TS, this contribution proposes clause 6 - how to map them.

This contribution includes restructuring clause 6, aligning with the contribution for clause 5.

Clause 6 is normative.

.

### ----------------------- Start of change 1 -----------------------

# 6	HTTP Message Mapping

Mapping between HTTP message and oneM2M primitive shall be applied in the following cases:

- when the Originator sends a request primitive,

- when the Originator receives a response primitive ,

- when the Receiver receives a request primitive,

- when the Receiver sends a response primitive.

# The following sub-clauses specify how to map each oneM2M primitive parameter to an corresponding HTTP message field to compose a HTTP request/response message..

## 6.1	Request-Line

## 6.1.1	Method

The operation types of the primitive are specified as operation parameter (clause 7.2.1.1.1 [6]). Mapping between HTTP method in a HTTP request message and oneM2M operation in a request primitive shall be applied in the following cases:

- when the Originator sends a request primitive,

- when the Receiver receives a request primitive.

The oneM2M operations shall be mapped as follows.

Table 6.1.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT |
| Delete | DELETE |
| Notify | POST |

Editor’s Note: Update operation mapping is TBD until the attribute level manipulation scheme is resolved in TS-0001 and TS-0004.

### On the Receiver, upon receiving HTTP request message with POST method, it shall be mapped to Create or Notify request primitive depending on the value of operation parameter.

### 6.1.2	Request-URI

### Request-URI shall be mapped with to parameter of the request primitive. This may not include host and port number. Host and port number shall be carried in Host header (see clause 6.x.x.x).

### filterCriteria parameter of the request primitive shall be mapped with query in the Request-URI.

### 6.1.3	HTTP-Version

### This specification supports binding to HTTP 1.1, so the version field shall be “HTTP/1.1”.

## 6.2	Status-Line

### 6.2.1	HTTP-Version

This specification supports binding to HTTP 1.1, so the version field shall be “HTTP/1.1”.

### 6.2.2	Status-Code

### The oneM2M responseStatusCode shall be mapped to HTTP Status-Code. Since the responseStatusCode have been defined more specifically, one or more responseStatusCodes shall be mapped to Status-Code. The original responseStatusCode parameter shall be carried in Message-body (see clause 6.x.x.x).

### N:1 status code mapping from the oneM2M request primitive to HTTP request message shall be:

Table 6.2.2-1: Status Code Mapping

| oneM2M Response Status Codes | HTTP Status Codes |
| --- | --- |
| STATUS_OK | 200 |
| STATUS_CREATED | 201 |
| STATUS_ACCEPTED | 202 |
| STATUS_DELETED | TBD |
| STATUS_CHANGED | 204 |
| STATUS_CONTENT | 205 |
| STATUS_BAD_REQUEST | 400 |
| STATUS_UNAUTHORIZED | 401 |
| STATUS_FORBIDDEN | 403 |
| STATUS_NOT_FOUND | 404 |
| STATUS_METHOD_NOT_ALLOWED | 405 |
| STATUS_NOT_ACCEPTABLE | 406 |
| STATUS_REQUEST_TIMEOUT | 408 |
| STATUS_REQUEST_ENTITY_TOO_LARGE | 413 |
| STATUS_UNSUPPORTED_MEDIA_TYPE | 415 |
| STATUS_INTERNAL_SERVER_ERROR | 500 |
| STATUS_NOT_IMPLEMENTED | 501 |

### Editor’s Note: This table needs to be updated aligning with TS-0004.

### 6.2.3	Reason-Phase

### Reason-Phase shall be mapped with the description of the corresponding responseStatusCode of the response primitive (see clause 6.5.4.[6]).

## 6.3	Header fields

### Host header shall be included in a HTTP request message. Other headers may be included in a HTTP request/response message.

### 6.3.1	Accept

The Originator may use Accept header to indicate which content-type is supported.  The Accept header shall be set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

### 6.3.2	Content-type

Content-type header shall be set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

### 6.3.3	Content-Location

Content-Location shall be set to the URI of the resource of:

- the created resource, responding to the Create request primitive;

- the retrieved resource, responding to the Retrieve request primitive, if the retrieved resource location is different from the requested resource location;

- the updated resource, responding to the Update request primitive

Editor’s Note: Usage of this header needs more investigation.

Editor’s Note: How to indicate the oneM2M URI scheme is TBD

### 6.3.4	From

From shall be mapped with from parameter of the request/response primitive.

### 6.3.5	Host

Host shall be derived from to parameter of the request primitive. This shall consist of the host and optionally port number.

### 6.3.6	Location

Location shall be set to the URI of the resource of the created resource.

Editor’s Note: How to indicate the oneM2M URI scheme is TBD

### 6.3.7	Other Header Fields

Other HTTP header fields shall be mapped with oneM2M primitive parameters.

Editor’s Note: The list of the fields and details are FFS.

### ---------------------- End of change 1 -----------------------

### ----------------------- Start of change 2 -----------------------

### ----------------------- End of change 2 -----------------------