| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO # 12 |
| Title:* | HTTP Binding TS cleanup |
| Source:* | LG Electronics, InterDigital |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com Phil Brown, InterDigital, phil.brown@interdigital.com |
| Date:* | 2014-07-21 |
| Abstract:* | HTTP Binding TS cleanup |
| Agenda Item:* | TBD |
| Work item(s): | WI 0013 |
| Document(s) Impacted* | oneM2M-TS-0009 HTTP Binding TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Change1: editorial changes for clause 1, 2 and 3.

Change2: re-structuring from clause 5.1 to clause 5.4

Change3: following re-structuring for clause 5 after clause 5.4

Other discussion point:

- Do we make clause 5, overview, as informative? then we need to modify some texts.

In R01: moved the text in clause 5 into informative annex, some of the text have been modified.

In R02:

      - removed text for blocking and non-blocking, instead bring the message flow in PRO-2014-0350 and put it into informative annex.

      - moved “notification using WebSocket” into Annex B, with modification on the original text

      - moved “authentication on HTTP request message” into 7. Security Consideration with editorial modification on the original text, meaning it’s still normative text

### ----------------------- Start of change 1 -----------------------

# 1	Scope

The specification will cover the protocol specific part of communication protocol used by oneM2M compliant systems as RESTful HTTP binding.

The scope of this specification is (not limited to as shown below):

-	Binding oneM2M Protocol primitive types to HTTP method

-	Binding oneM2M response status codes (successful/unsuccessful) to HTTP response codes

-	Binding oneM2M RESTful resources to HTTP resources

This specification is depending on Core Protocol Technical Specification (TS-0004) for data types.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

[1]	RFC2616: “Hypertext Transfer Protocol - HTTP/1.1”, IETF, June 1999.

[2]	oneM2M TS-0001: Architecture TS

[3]	oneM2M TS-0004: Core Protocol TS

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	 RFC2617: “HTTP Authentication: Basic and Digest Access Authentication”, IETF, June 1999

[i.3]	RFC6750: “The OAuth 2.0 Authorization Framework: Bearer Token Usage”, IETF, October 2012.

[i.4]	RFC6455:“The WebSocket Protocol”, IETF, December 2011.

# 3	Definitions, symbols, abbreviations and acronyms

## 3.1	Definitions

## 3.2	Symbols

## 3.3	Abbreviations & Acronyms

For the purposes of the present document, the following abbreviations and acronyms apply:

### HTTP		Hyper Text Transfer Protocol

### ----------------------- End of change 1 -----------------------

### ----------------------- Start of change 2 -----------------------

# 5	Overview

This clause describes what oneM2M primitive parameters can be mapped to HTTP request/response messages.

### ----------------------- End of change 2 -----------------------

### ----------------------- Start of change 3 -----------------------

## Annex A (Informative): Example Procedures

## A.1	AE Registration

The following diagram is HTTP mapping of procedure described in clause 7.3.4.2.1.

Figure A.1-1 oneM2M HTTP Binding Example – AE Registration

## Annex B (Informative)	WebSocket

## B.1	Notification using WebSocket

WebSocket [3] can be used for transporting notifications to an AE/CSE. This can be useful for an AE/CSE which is not server-capable or cannot be reachable for delivery of unsolicited requests.

For example, when an AE needs to receive a notification message from the CSE, the AE establishes a WebSocket connection to a CSE. When a new notification message is generated, the notification will be sent to the AE as the data frame of the WebSocket.

### ----------------------- End of change 3 -----------------------

### ----------------------- Start of change 4 -----------------------

## 7	Security Consideration

## 7.1	Authentication on HTTP Request Message

When sending the credential to be checked by Registrar CSE, Proxy-Authorization header should be used as specified in HTTP/1.1 (see RFC2617).

When sending the credential to be checked by Hosting CSE, Authorization header should be used as specified in HTTP/1.1.

When the credential to be checked by Hosting CSE is an Access Token which is compatible with OAuth 2.0 framework, the Bearer authentication scheme shall be used as specified in RFC6750.

Note: TS-0003 [oneM2M Security Solutions] does not provide any details on usage or provisioning the token.

## 7.2	Transport Layer Security

oneM2M primitive parameters contained in HTTP messages may be protected by TLS as hop-by-hop manner, not end-to-end. For the details, see clause x.x.x [TS-0003]

### ----------------------- End of change 4 -----------------------