| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | Primitives Types mapping |
| Source:* | Hitachi, |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-07-21 |
| Abstract:* | This contribution proposes primitive types mapping of CoAP protocol binding. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

## 6.1	Primitive Types Mapping

The CoAP request method shall be mapped into oneM2M primitive types as following:

Editor’s Note: in this context, primitive types depend on operation.

Candidates of primitive types are <resource type name>CreateRequest/Response, <resource type name>RetrieveRequest/Response, <resource type name>UpdateRequest/Response, and <resource type name>DeleteRequest/Response. This shall be updated based on Protocol Core TS.

| Table 6.1-1: CoAP Method MappingCoAP Methods | oneM2M Primitive Types |
| --- | --- |
| POST | <resource type name>CreateRequest/Response |
| GET | <resource type name>RetrieveRequest/Response |
| PUT | <resource type name>UpdateRequest/Response |
| DELETE | <resource type name>DeleteRequest/Response |

Editor’s note: primitive types are for FFS, and detailed parts will be added when related TS finished

## 6.1.1 Request primitive to CoAP Request

The oneM2M request operation shall be mapped to a CoAP Method according to the table 6.1.1.-1.

The CoAP request shall be constructed using the selected CoAP method, selected options as described in options.

CoAP message includes the 8-bit Code.  In case of a request, the Code field indicates the Request Method.  The Code field is limited to indicate all oneM2M request code, so additional information should be carry via the CoAP payload field.

CoAP defines a single set of options that are used in both requests and responses.  In case of a request, if CoAP defined options is limited to indicate all oneM2M options, additional information should be carry in the CoAP payload field.

Table 6.1.1-1: oneM2M Operation Mapping

| oneM2M Operation | CoAP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT |
| Delete | DELETE |
| Notify | POST |

## 6.1.2 CoAP Request to Request Primitive

The CoAP request shall be mapped to a oneM2M request primitive according to the table Table 6.1.2-1..

Table 6.1.2-1: CoAP Method Mapping

| CoAP Method | oneM2M Operation |
| --- | --- |
| POST | Create or Notify |
| GET | Retrieve |
| PUT | Update |
| DELETE | Delete |

The oneM2M request shall be constructed using the selected method, selected options as described in options.

As CoAP message Code and Options are limited, sometimes additional information is carried in CoAP payload field. In that case, oneM2M request shall be constructed using that additional information.

--------------------- End of proposed modified text ---------------------