| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | Status Code Cleanup |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-07-23 |
| Abstract:* | Status Code Cleanup |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – Core Protocol (Draft version 0.8.3) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes simplifying response status codes.

Since Originator keeps the request until he gets response, we don’t need to provide operation information and resource type information.

========================Start of 1st Change==========================

#### Un-successful Responses

Table 6.8.4.2-1 specifies the RSCs for un-successful responses for each release. Ranges from 2000 to 3000 are used for generic errors, Ranges from 3000 to 4000 are used for operation specific errors, and Ranges from 4000 to 5000 are used for resource type specific errors.

Table 6.8.4.2-1: RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 2000 |  |  |  |  |  | X |  |
| Unsupported resource | 2001 | Resource URI |  |  | X | X |  |  |
| Unsupported attribute | 2002 | Attribute URI |  |  | X | X |  |  |
| Cannot forward, target not reachable | 2003 | Resource URI |  |  | X | X |  |  |
| Cannot forward, other reason TBD | 2004 | Resource URI |  |  | X | X |  |  |
| No privilege | 2005 | Resource URI |  |  | X | X |  |  |
| Create error - already exists | 3000 | Resource URI |  |  | X | X |  |  |
| Create error - missing mandatory parameter | 3001 | Missing parameter |  |  | X | X |  |  |
| Retrieve, Update, Delete error - Does not exist | 3002 | Target URI |  |  | X | X |  |  |
| Update error - unacceptable contents | 3003 | Attribute URI |  |  | X | X |  |  |
| Create delivery - not able to take on responsibility | 4000 |  |  |  | X | X |  |  |
| Create fanoutpoint - group request identifier exists | 4001 |  |  |  | X | X |  |  |
| Retrieve fanoutpoint - group request identifier exists | 4002 |  |  |  | X | X |  |  |
| Update fanoutpoint - group request identifier exists | 4003 |  |  |  | X | X |  |  |
| Delete fanoutpoint - group request identifier exists | 4004 |  |  |  | X | X |  |  |
| Create mgmtObj - memory shortage | 4005 | CSEBase URI |  |  | X | X |  |  |
| Cancel execInstance - not cancellable | 4006 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Cancel execInstance - already complete | 4007 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - not cancellable | 4008 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - already complete | 4009 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Retrieve CSEBase - format error | 4010 | CSEBase URI |  |  | X | X |  |  |
| CMDH rules -non compliant | 4011 |  |  |  |  |  |  |  |
|  | 4012 |  |  |  |  |  |  |  |
|  | 4013 |  |  |  |  |  |  |  |
|  | 4014 |  |  |  |  |  |  |  |

Editor's Note: The contents of this table are exemplary and are expected to be revised. In particular ARC discussions regarding UPDATE and attributes may impact argument1. Some of the exemplary RSCs may be equivalent and can be collapsed to fewer RSCs.

Editor's Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

========================End of 1st Change==========================

# Comments

ARC 8.5.2

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.2.1

ARC 10.1.2

ARC 10.1.3

ARC 10.1.3

ARC 10.1.3

ARC 10.4

ARC 10.1.4

10.2.4.2

10.2.6.6

ARC 10.2.6.7

ARC 10.2.6.8

ARC 10.2.6.9

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.3

ARC 10.2.7.4

ARC 10.2.7.4

ARC 10.2.7.5

ARC 10.2.7.5

ARC 10.2.7.6

ARC 10.2.7.6

ARC 10.2.8.7

ARC 10.2.8.7

ARC 10.2.8.

ARC 10.2.8.9

ARC 10.2.9.2