| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | Status Code Cleanup |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-07-23 |
| Abstract:* | Status Code Cleanup |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – Core Protocol (Draft version 0.8.3) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes simplifying response status codes.

Since Originator keeps the request until he gets response, we don’t need to provide operation information and resource type information.

========================Start of 1st Change==========================

#### Un-successful Responses

Table 6.6.4.2-1 specify the RSCs for un-successful responses for each release.

Table 6.6.4.2-1: RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | StatusDescription | Applicability |
| --- | --- | --- | --- |
|  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 2000 |  |  |  | X |  |
| Unsupported resource | 2001 | Resource URI | X | X |  |  |
| Unsupported attribute | 2002 | Attribute URI | X | X |  |  |
| Target not reachable | 2003 | Resource URI | X | X |  |  |
| Cannot forward, other reason TBD | 2004 | Resource URI | X | X |  |  |
| No privilege | 2005 | Resource URI | X | X |  |  |
| Already exists | 2006 | Resource URI | X | X |  |  |
| Create error - missing mandatory parameter | 2007 | Missing parameter | X | X |  |  |
| Does not exist | 2009 | Target URI | X | X |  |  |
| Update error - unacceptable contents | 2012 | Attribute URI | X | X |  |  |
| Create delivery - not able to take on responsibility | 2015 |  | X | X |  |  |
| group request identifier exists | 2016 |  | X | X |  |  |
| External object not reachable | 2022 | mgmtObj URI | X | X |  |  |
| Create mgmtObj - memory shortage | 2023 | CSEBase URI | X | X |  |  |
| External object not found | 2028 | MgmtObj URI | X | X |  |  |
| Cancel execInstance - not cancellable | 2031 | Name of mgmtCmd resource | X | X |  |  |
| Cancel execInstance - already complete | 2032 | Name of mgmtCmd resource | X | X |  |  |
| Delete execInstance - not cancellable | 2033 | Name of mgmtCmd resource | X | X |  |  |
| Delete execInstance - already complete | 2034 | Name of mgmtCmd resource | X | X |  |  |
| Retrieve CSEBase - format error | 2035 | CSEBase URI | X | X |  |  |
| CMDH rules -non compliant | 2036 |  |  |  |  |  |
| Target is not subscribable | 2037 |  |  |  |  |  |
| Cannot initiate subscription verification | 2038 |  |  |  |  |  |
| Subscription verification failed - Originator | 2039 | Originator ID |  |  |  |  |
| Subscription verification failed - Create | 4040 | creator |  |  |  |  |
| Max number of member exceeded | 2040 |  |  |  |  |  |
| Member type inconsistent | 2041 |  |  |  |  |  |
| Management session cannot be established | 2042 |  | X |  |  |  |
| Management session establishment timeout | 2043 |  | X |  |  |  |

Editor's Note: The contents of this table are exemplary and are expected to be revised. In particular ARC discussions regarding UPDATE and attributes may impact argument1. Some of the exemplary RSCs may be equivalent and can be collapsed to fewer RSCs.

Editor's Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

========================End of 1st Change==========================

# Comments

ARC 8.5.2

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.2.1

ARC 10.1.2

ARC 10.1.3

ARC 10.1.3

ARC 10.1.3

ARC 10.4

ARC 10.1.4

10.2.4.2

10.2.6.6

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.5

ARC 10.2.8.7

ARC 10.2.8.7

ARC 10.2.8.

ARC 10.2.8.9

ARC 10.2.9.2