| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | oneM2M_enumeration_types |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-07-29 |
| Abstract:* | This contribution proposed to add enumeration types and its notation in Core Protocol TS. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed to make following changes

---Change 0 STARTS---

6.3.2.2 Enumeration Data Types

#### 6.3.2.2.1	Introduction

The oneM2M Enumeration Types are defined as extention from ‘enumeration type’ which is defined in XML Schema definition [3].

The oneM2M Enumeration Types are based on <xs:integer>, and the numeric values are interpreted as specified in clause 6.3.2.2.

Table 6.3.2,1-1 shows the example of Enumeration Type Definition for m2m:enumFooType.

Table 6.3.2.1-1: Example of oneM2M Enumeration Type Definition

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Interpretation-1 |  |
| 2 | Interpretation-2 |  |
| 3 | Interpretation-3 |  |
| See Cluase x.x.x “title of cluase” |

The oneM2M Enumeration Type definition shall be implemented as part of 
CDT-enumeration-v1_0_0-<<date of publication>>.xsd.

Figure 6.3.2.1-1 shows the example of XSD representation of ‘m2m:enumFooType’.

Fig 6.3.2.1-1: Example of XSD version of oneM2M Enumeration Type

#### 6.3.2.2	Enumeration Type Definitions

6.3.2.2.1	m2m:enumFoo Type

Editor’s Note: This clause is just example , and MUST be removed when first definition is added.

#### 6.3.2.2.1 Enumeration Data Type Definitions

Editor’s Note: Each emnumeration types should be separately defined.

Table 6.3.2.1-1 describes oneM2M-specific enumeration data type definitions.

Table 6.3.2.2-1: oneM2M Enumeration Data Types

| XSD type name | Values | Description |
| --- | --- | --- |
| m2m:resourceType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, |  |
| m2m:commaList | TBD | Used for supportedResourceType attribute of <CSEBase> resource. |
| m2m:cseTypeID | “IN-CSE”, “MN-CSE”, “ASN-CSE” | Used for cseType attribute of <CSEBase> resource. |
| m2m:locationSource | “Network-based”, “Device-based”, “Sharing-based” | Used for locationSource attribute of <loationPolicy> resource. |
| m2m:eventCatType | “immediate”, “bestEffort”, “latest” | Used for ec parameter in request and eventCat attribute of <delivery> resource. |
| m2m:operation | “Create”, “Retrieve”, “Update”, “Delete”, “Notify” | Used for op parameter in request and operation attribute in <request> resource |
| m2m:responseType | “nonBlockingRequestSynch”, “nonBlckingRequestAsynch”, “blockingRequest” | Used for rt parameter in request and operation attribute in <request> resource |
| m2m:resultContent | “attributes”, “attributes+childResources”, “childResources”, “nothing”, “originalResources” | Used for rc parameter in request |
| m2m:discResType | “hierarchical”, “non-hierarchical”, “cseID+resourceID” |  |
| m2m:statusCode | See clause 6.5.4 | Used for cs parameter in response |
| m2m:requestStatus | TBD | Used for requestStatus attribute in <request> resource. |
| m2m:operationResult | TBD | Used for operationResult attribute in <request> resource. |
| m2m:memberType | “accessControlPolicy”, “AE”, “container”, “contentInstance”, “CSEBase”, “delivery”, “eventConfig”, “execInstance”, “fanOutPoint”, “group”, “locationPolicy”, “m2mServiceSubscription”, “mgmtCmd”, “mgmtObj”, “node”, “nodeInfo”, “pollingChannel”, “remoteCSE”, “request”, “schedule”, “statsCollect”, “statsConfig”, “subscription”, “mixed” | Used for memberType attribute in <member> resource. |
| m2m:consistencystrategy | TBD | Used for consistencyStrategy attribute in <group> resource. |
| m2m:cmdType | “RESET”, “REBOOT”, “UPLOAD”, “DOWNLOAD”, “SOFTWAREINSTALL”, “SOFTWAREUNINSTALL” | Used for cmdType attribute in <mgmtCmd> resource. |
| m2m: execReqArgsListType | TBD | Used for execReqArgsListType attribute in <mgmtCmd> and <execInstance resource. |
| m2m:execModeType | “IMMEDIATEONCE”, “IMMEDIATEREPEAT”, “RANDOMONCE”, “RANDOMREPEAT” | Used for execModeType attribute in <mgmtCmd> and <execInstance> resource. |
| m2m:execStatusType | “INITATED”, “STARTED”, “FINISHED”, “CANCELLING”, “CANCELLED” | Used for execStatusType attribute in <execInstance> resource. |
| m2m:pendingNotification | “sendLatest”, “sendAllPending” | This is used for pendingNotification attribute in <subscription> resource. |
| m2m:notificationContentType | “modifiedAttributes”, “wholeResource”, “referenceOnly” | This is used for notificationConentType attribute in <subscription> resource. |
| m2m:resourceStatus | “childCreated”, “childDeleted”, “updated”, “deleted” | This is used for eventNotificationCriteria. |
| m2m:operationMonitor | “Create”, “Retrieve”, “Update”, “Delete” | This is used for eventNotificationCriteria. |
| m2m:attribute | all common and resource specific attribute names specified in clause 7.3 |  |

---Change 0 ENDS ---

---Change 1 STARTS---

## 6.3 Common Data Types

(Skipped)6.3.2	Enumeration Types used in oneM2M

6.3.2.1	Introduction

The oneM2M Enumeration Types are defined as extention from ‘enumeration type’ which is defined in XML Schema definition [3].

The oneM2M Enumeration Types are based on <xs:integer>, and the numeric values are interpreted as specified in clause 6.3.2.2.

Table 6.3.2,1-1 shows the example of Enumeration Type Definition for m2m:enumFooType.

Table 6.3.2.1-1: Example of oneM2M Enumeration Type Definition

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Interpretation-1 |  |
| 2 | Interpretation-2 |  |
| 3 | Interpretation-3 |  |
| See Cluase x.x.x “title of cluase” |

The oneM2M Enumeration Type definition shall be implemented as part of 
CDT-enumeration-v1_0_0-<<date of publication>>.xsd.

Figure 6.3.2.1-1 shows the example of XSD representation of ‘m2m:enumFooType’.

Fig 6.3.2.1-1: Example of XSD version of oneM2M Enumeration Type

6.3.2.2	Enumeration Type Definitions

6.3.2.2.1	EnumXXXType

Editor’s Note: This clause is just example , and MUST be removed when first definition is added.

### 6.3.3 Additional Data Types used in oneM2M

---Change 1 ENDS ---

# Comments

we don’t need this, right?

# Text boxes

<xs:simpleType name="enumFooType">

<xs:restriction base="xs:integer">

<xs:enumeration value="1"/>

<xs:enumeration value="2"/>

<xs:enumeration value="3"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="enumFooType">

<xs:restriction base="xs:integer">

<xs:enumeration value="1"/>

<xs:enumeration value="2"/>

<xs:enumeration value="3"/>

</xs:restriction>

</xs:simpleType>