| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP Binding Options |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-07-28 |
| Abstract:* | CoAP Binding Options |
| Agenda Item:* | PRO |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | Technical Specification – CoAP Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes CoAP Options that is used in oneM2M.

========================Start of 1st Change==========================

## 6.2	Mapping of Options

This clause describes which request parameters are mapped to which CoAP options.

## 6.2.1	URI Options

The CoAP Uri-Host, Uri-Port, Uri-Path, Uri-Query and Proxy-Uri options are derived from the to parameter.

When addressing a resource on more than 0 hop, the to parameter shall be mapped to Proxy-Uri in CoAP.

When addressing a local resource (i.e., 0 hop), the host, port path and query part of the to shall be used as the value for the Uri-host,Uri-Port, Uri-Path and Uri-Query CoAP options.

For example, if the to has the following form:

coap://IN-CSEID.m2m.myoperator.org:6123/CSERoot/myAppX/myContainerY?label=one

Then if addressing a resource on more than 0 hop, Proxy-Uri shall be configured as below:

Proxy-Uri: IN-CSEID.m2m.myoperator.org:6123/CSERoot/myAppX/myContainerY?label=one

And Uri-Host, Uri-Port, Uri-Path and Uri-Query shall not be configured.

Then if addressing a resource on 0 hop, following options shall be configured as below:

Uri-Host: IN-CSEID.m2m.myoperator.org

Uri-Port: 6123

Uri-Path: /CSERoot/myAppX/myContainerY

Uri-Query: label=one

And Proxy-Uri shall not be configured.

## 6.2.2 Content Format Negotiation Options

The CoAP Accept option can be used to indicate which Content-Format is acceptable to an Originator. If a Hosting CSE supports the Content-Format specified in Accept option of the request, the Hosting CSE shall respond with that Content-Format. If the Hosting CSE doesn’t support the Content-Format specified in Accept option of the request, 4.06 "Not Acceptable" MUST be sent as a response, unless another error code takes precedence for this response.

Editor’s note: which content format supported in oneM2M needs to be clarified.

## 6.2.3 Token

Since Token option is used to match between a request and a response(s), the Token shall have one-to-one mapping with M2M-Request-ID.

========================End of 1st Change==========================