| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 - PRO |
| Title:* | Proposal for design principles on extensibility |
| Source:* | Institut Mines-Telecom |
| Contact: | Antonio M. Ortiz, IMT, antonio.ortiz_torres@it-sudparis.eu Noel Crespi, IMT, noel.crespi@mines-telecom.fr Eric Farnier, ECOMETERING, eric.farnier@gdfsuez.com |
| Date:* | 2014-07-16 |
| Abstract:* | This contribution provides the description for the protocol design principles on extensibility and expects to include the proposed text in Section 5.4 of the TS-0004 (oneM2M Core Protocol Specification). |
| Agenda Item:* | TBD |
| Work item(s): | WI 009, oneM2M Protocol Development |
| Document(s) Impacted* | oneM2M TS-0004, oneM2M Core Protocol Specification (V-0.4.2) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To include the proposed text in the TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Background

The WG3 (PRO) is currently developing the oneM2M Core Protocol Specification.  This TS contains the section on protocol design principles and requirements which are intended to provide design principles and specify aspects of protocol requirements.

One of key aspects is extensibility which has the following features and considerations.

- Extensibility is focused on considering future growth in the initial system design in order to allow a continued development, while minimizing the impact on the existing oneM2M protocol functions.

- The fast evolution of M2M systems states the need for future changes in the oneM2M protocol design and operation in order to deal with this ecosystem in continuous evolution.

- Extensible oneM2M protocols shall be designed to be able to facilitate future changes and adaptation to new situations in order to, for example, deal with a different number of devices, add, remove, or modify protocol functionality, etc.

We believe that extensibility in oneM2M is quite important and should be considered during protocol design and operation.

This contribution provides the description for the protocol design principles from key considerations for extensibility in oneM2M protocols.

2	Proposal

In this contribution, we propose to insert the following text in the Section 5.4 of the TS (v-0.5.4) on oneM2M Core Protocol Specification.

-------------------------------- Proposed Text --------------------------

# Protocol Design Principals and Requirements

## Design Principles

### Scalability

When considering scalability as a requirement in the design of oneM2M protocols, one or several of the following mechanisms could be used:

- Wherever possible, ensure direct addressability to the CSEs hosting target resources, to minimize network hops.

- Asynchrony in terms of data processing, with the ultimate objective of minimizing the number of discarded packets.

- Caching mechanisms that allow all the received packets to be processed.

- Efficient load distribution to avoid bottlenecks and data loss.

- Data compression and/or aggregation, in order to reduce the amount of data sent through the network.

### Extensibility

The oneM2M protocols will be designed to allow continued development and to facilitate changes by means of standardized extensions.

When considering extensibility, impact to the existing oneM2M protocol functions will be minimized.

As an example, extensibility can be related to one or more of the following aspects:

- Handling a different number of devices,

- Add, remove or modify oneM2M protocol functionality,

- New oneM2M protocol routines,

- New data types.

The design of extensible oneM2M protocols will consider and mitigate the risk of unintended consequences, such as interoperability issues, operational problems, or security vulnerabilities.

### Robustness

### Efficiency

Energy Efficiency:

•	As energy consumption directly affects the overall system performance, oneM2M protocols should consider energy efficiency, especially in resource constrained environments with battery-powered oneM2M devices.

•	Energy efficient oneM2M protocols will aim at reducing the overall energy consumption while maintaining the performance required by the oneM2M Applications.

### Security

<Text>