| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO 12.0 |
| Title:* | <schedule> resource default text |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com |
| Contact: |  |
| Date:* | 2014-07-29 |
| Abstract:* | This contribution proposes new text regarding the default procedure when the optional <schedule> type resource is not present, and resolves an editor’s note. |
| Agenda Item:* | TS-0004 contributions |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M Protocol Technical Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To accept this text and remove the editor’s note |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction:

In the ARC-TS, the default for when the optional <schedule> resource is not present is that the capability, which the presence of a <schedule> constrains, is unconstrained. See 6.2.9.2.

Reachability schedules; which are elements of a Node's policy, and specify when messaging can occur between Nodes. Reachability schedules can be used in conjunction with other policy elements. When reachability schedules are not present in a Node then that Node is expected to be always reachable.

Rather than put the default operation text in the <schedule> clause 7.3.8, since each context where <schedule> is used may choose different defaults, it is proposed to add default operation text to each place where <schedule> may be used. Which includes resources:

- CSEBase ( <schedule> child resource is missing )

- remoteCSE

- subscription

- cmdhNwAccessRule

The proposed implementation modifies the meaning of a column in the child resources tables.

Furthermore the following editor’s note is proposed to be removed.

Editor’s Note: defining default value sound in scope of stage 3, but may be subject to remove in future.

----------------------------Start change 1------------------------------------------------------------------

### 7.3.2	Resource Type CSEBase

#### 7.3.2.1 Introduction

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE. The detailed description can be found in clause 9.6.3 in Architecture TS([ref-Arch-TS]).

Table 1.1.1.1-1: Data Type Definition of cseBase

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Editor's Note: Data Type definition should be posted after general agreement on technical issues

Table 1.1.1.1-2: Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| supportedResourceType | m2m:commaList | (TBD) | Read-Only |

Table 1.1.1.1-3: Reference of child resources

| Child Resource Type Name | Multiplicity / Default | Ref . to in Resource Type Definition |
| --- | --- | --- |
| remoteCse(variable) | 0..n | Error! Reference source not found.Error! Reference source not found.Error! Reference source not found. |
| node(variable) | 0..n | Error! Reference source not found. |
| AE (variable) | 0..n | Error! Reference source not found.Error! Reference source not found. |
| container(variable) | 0..n | Error! Reference source not found. |
| group(variable) | 0..n | Error! Reference source not found.Error! Reference source not found.Error! Reference source not found.Error! Reference source not found. |
| accessControlPolicy | 0..n | Error! Reference source not found. |
| subscription(variable) | 0..n | Error! Reference source not found. |
| mgmtCmd(variable) | 0..n | Error! Reference source not found. |
| locationPolicy(variable) | 0..n | Error! Reference source not found. |
| statsConfig(variable) | 0..n | Error! Reference source not found. |
| statsCollect(variable) | 0..n | Error! Reference source not found. |
| schedule(variable) | 0..1 When not present, reachability of the node is not time-constrained. |  |

Table 6.x.1-1 Data Types for Request message parameters

----------------------------End change 1------------------------------------------------------------------

----------------------------Start change 2------------------------------------------------------------------

### Resource Type remoteCSE

#### Introduction

A <remoteCSE> resource shall represent a remote CSE that is registered to the Registrar CSE. <remoteCSE> resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

The detailed description can be found in clause 9.6.4 in Architecture TS.

Table 1.1.1.1-1: Data Type Definition of <remoteCSE>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| remoteCSEType | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd |  |

Table 1.1.1.1-2: Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| cseType | m2m:cseTypeID | TBD |  |
| pointOfAccess | xs:anyURI | None |  |
| CSEBase | xs:anyURI | None |  |
| requestReachability | xs:boolean | TRUE |  |

Table 1.1.1.1-3: Reference of child resources

| Child Resource Type and Name | Multiplicity /Default | Ref. to in Resource Type Definition |
| --- | --- | --- |
| <AE>(variable) | 0..n | Clause Error! Reference source not found. |
| <container>(variable) | 0..n | Clause Error! Reference source not found. |
| <group>(variable) | 0..n | Clause Error! Reference source not found. |
| <accessControlPolicy>(variable) | 0..n | Clause Error! Reference source not found. |
| <subscription>variable) | 0..n | Clause Error! Reference source not found. |
| <pollingChannel>(variable) | 0..n | Clause Error! Reference source not found. |
| <schedule>(variable) | 0..1 When not present, reachability to the remoteCSE is not time-constrained. | Clause Error! Reference source not found. |

----------------------------End change 2------------------------------------------------------------------

----------------------------Start change 3------------------------------------------------------------------

### Resource Type subscription

#### Introduction

The <subscription> resource contains subscription information for its subscribed-to resource. The subscription resource is a child of the subscribed to resource.

The detailed description can be found in clause 9.6.8 in Architecture TS.

Table 7.3.x.1.1 Data Type Definition of subscription

| Data Type ID | File Name | Note |
| --- | --- | --- |
| subscriptionType | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd |  |

Table 7.3.x.1-2 Applicable Common Attributes on subscription

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP |  |  |
| resourceID | NP | O | NP | NP |  |  |
| parentID | NP | O | NP | NP |  |  |
| accessControlPolicyIDs | O | O | O | NP |  |  |
| creationTime | NP | O | NP | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| lastModifiedTime | NP | O | NP | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 7.3.7.1-3 Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| eventNotificationCriteria | O | O | O | NP | m2m:eventNotificationCriteria |  |
| expirationCounter | O | O | O | NP | xs:positiveInteger |  |
| notificationURI | M | O | O | NP | list of xs:anyURI |  |
| groupName | O | O | O | NP | xs:anyURI |  |
| notificationForwardingURI | O | O | O | NP | xs:anyURI |  |
| batchNotify | O | O | O | NP | m2m:batchNotify |  |
| rateLimit | O | O | O | NP | m2m:rateLimit |  |
| preSubscriptionNotify | O | O | NP | NP | xs:positiveInteger |  |
| pendingNotification | O | O | O | NP | m2m:pendingNotification |  |
| notificationStoragePriority | O | O | O | NP | xs:positiveInteger |  |
| latestNotify | O | O | O | NP | xs:boolean |  |
| notificationContentType | O | O | O | NP | m2m:notificationContentType |  |
| notificationEventCat | O | O | O | NP | m2m:eventCat |  |
| creator | O | O | O | NP | m2m:id |  |
| subscriberURI | O | O | NP | NP | xs:anyURI |  |

Table 7.3.7.1.4 Reference of child resources

| Child Resource Type and Name | Multiplicity / Default | Ref. . to in Resource Type Definition |
| --- | --- | --- |
| notificationSchedule | 0..1 When not present, the subscription is not time-constrained from sending notifications. | Error! Reference source not found. |

----------------------------End change 3------------------------------------------------------------------

----------------------------Start change 4------------------------------------------------------------------

D.1.8 [cmdhNwAccessRule] Resource

The resource [cmdhNwAccessRule] defines limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests. The detailed description can be found in clause D.12.7 of Architecture TS-0001 [1].

Table A.1.1-1 Data Type Definition of [cmdhNwAccessRule]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-cmdhNwAccessRule-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Editor’s Note: Table entries will be filled after general agreement on technical issues is achieved in PRO WG

Table A.1.1-2: Optionality of operations by reference point

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | M | M | N/A |
| Retrieve | M | M | N/A |
| Update | M | M | N/A |
| Delete | M | M | N/A |

Table A.1.1-3:  Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows Operation |
| --- | --- | --- | --- |
| mgmtDefinition | Fixed string “cmdhNwAccessRule” |  |  |
| objectID | See Table 7.3.x.1.2 |  |  |
| objectPath | See Table 7.3.x.1.2 |  |  |
| Description | See Table 7.3.x.1.2 |  |  |
| targetNetwork | xs:string |  |  |
| minReqVolume | xs:nonNegativeInteger |  |  |
| backOffParameters | xs:complexType |  |  |
| otherConditions | TBD |  |  |
| allowedSchedule | m2m:mgmtLink | If the allowedSchedule link is not specified, then network access is not time-constrained. |  |

Editor’s Note: The backOffParameters attribute needs to be specified as a specific complexType data type consisting of three elements (BackoffTime, BackoffTimeIncrement, MaximumBackoffTime). It needs to be clarified how to document such attributes in the present Data Type Definition tables.

Editor’s Note: The otherConditions attribute needs to be clarified  in TS-0001 before we can determine the data type.

The resource [cmdhNwAccessRule] does not have any child resources other than the one referenced by m2m:mgmtLink type of attribute.

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.x.2 for the generic <mgmtObj> resource type apply.

----------------------------End change 4------------------------------------------------------------------

----------------------------Start change 5------------------------------------------------------------------

### Resource Type schedule

#### Introduction

The <schedule> resource shall represent scheduling information in the context of its parent resource. An Originator shall have the same access control privileges to the <schedule> resource as it has to its parent resource.

The detailed <schedule> resource description can be found in clause 9.6.9 of the Architecture TS.

Table 1.1.1.1-1: Data Type Definition of <schedule>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| scheduleType | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 1.1.1.1-2: Data Type for resource specific attribute

| Attribute Name | Data Type | Default Value and Constraints |
| --- | --- | --- |
| scheduleElement | Extended Crontab Data String | No default. See data type definition for constraints |

Editor’s note; How to represent multiplicity need to clarify. scheduleElement is 1..n

Editor’s Note: Optionality of Attributes should be referred in Arch-TS or self-contained ? scheduleElement is Optionally announced for <scheduleAnnc>

Editor’s Note: It is not clear where in the document the following data type definition should be located since it is <schedule> resource specific.

Editor’s Note: Shingo had some further suggestion about how better to show periods using additional fields.

The set of scheduleElement attributes together represent the defined schedule. All scheduleElement attributes shall be updated as a set. The set of scheduleElement attributes expresses time periods defined by second, minute, hour day of month, month, and year.

The “Extended Crontab Data String” Data Type is a string comprising 7 fields per Table below, separated by white space. The allowed values are used together with 6 special characters in each “scheduleElement”.

----------------------------End change 5------------------------------------------------------------------

# Comments

reference to Arch TS should be highlighted to check its consistency

Should be correct with reference to Core Protocol TS

bring a XSD