| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#12 |
| Title:* | response status code for management |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-7-29 |
| Abstract:* | The contribution corrects the response status code for management |
| Agenda Item:* | TBD |
| Work item(s): | WI0009 |
| Document(s) Impacted* | TS0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into TS0004 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### ********************* start of change 1*****************************

#### Management Common Operations

##### Identify the managed entity and the management protocol

The Hosting CSE shall identify the managed entity to be managed via the <node> resource which is the parent resource of the addressed <mgmtObj> resource. Through the <node> resource, the identifier of the device can be retrieved. Then the Hosting CSE shall determine the management protocol to be used for communicating with the managed entity based on the objectID of the addressed <mgmtObj> resource. If the managed entity cannot be identified, the Hosting CSE shall reject the request with the response status code set to " External object not reachable " in the Response primitive.

##### Locate the external management objects to be managed on the managed entity

The Hosting CSE shall locate the external management object information to be managed on the managed entity by the objectPath attribute of the <mgmtObj> resource addressed by the URI provided in the to primitive attribute. In the case that the to addresses an [objectAttribute] without objectPath attribute, the Hosting CSE shall locate the external management object information on the managed entity through the objectPath attribute of the <mgmtObj> resource of the addressed [objectAttribute], combining with their relative position in the external management object tree. If the external management object information cannot be located, the Hosting CSE shall reject the request with the response status code set to " External object not found " in the Response primitive.

##### Establish a management session with the managed entity

In the case that the management server is embedded with the CSE, if there is no existing management session between the Hosting CSE and the managed entity, the Hosting CSE shall also trigger the managed entity to establish a management session with the Hosting CSE by sending triggering message to the managed entity using the determined management protocol in case such triggering mechanism is supported by the external management technology. If the triggering mechanism is not supported by the external management technology, the Hosting CSE shall reject the request with the response status code “Management session cannot be established”.  If the management session cannot be established within a limited time span as per local policy, the Hosting CSE shall reject the request with the response status code set to " Management session establishment timeout " in the Response primitive.

Editor’s Note: The procedure to establish management session when management server is separate from the CSE is FFS.

##### Send the management request(s) to the managed entity corresponding to the received Request primitive

The Hosting CSE shall send the management request(s) to the managed entity in the established management session in order to perform the management operation as requested by the received Request primitive. The management request shall address the external management object information on the managed entity as determined in clause  7.2.2.4 or in the primitive specific clauses. The management request being used is specific to the external management technology according to a pre-defined mapping relationship with the Request primitive. The internal data structure of the external management object addressed by the management request shall be determined based on the mapping relationship of the <mgmtObj> resource and the external management objects or based on the generic mapping rule as specified in TS0001 clause 9.6.15, for any other <mgmtObj> resource instances. The Hosting CSE shall extract the management results received from the managed entity in order to prepare a Response primitive to be sent to the originator later. Unless explicitly stated, if the management request cannot be performed successfully, the Hosting CSE shall reject the Request primitive with the proper response status code in the Response primitive according to the mapping relationship with the external management technology.

Editor’s Note: The common operation for handling notification of external management technology from managed entity is FFS.

#### ********************* end of change 1*****************************

#### ********************* start of change 2*****************************

#### Un-successful Responses

Table 6.8.4.2-1 specify the RSCs for un-successful responses for each release.

Table 6.6.4.2-1: RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 2000 |  |  |  |  |  | X |  |
| Unsupported resource | 2001 | Resource URI |  |  | X | X |  |  |
| Unsupported attribute | 2002 | Attribute URI |  |  | X | X |  |  |
| Cannot forward, target not reachable | 2003 | Resource URI |  |  | X | X |  |  |
| Cannot forward, other reason TBD | 2004 | Resource URI |  |  | X | X |  |  |
| Create error - no privilege | 2005 | Resource URI |  |  | X | X |  |  |
| Create error - already exists | 2006 | Resource URI |  |  | X | X |  |  |
| Create error - missing mandatory parameter | 2007 | Missing parameter |  |  | X | X |  |  |
| Retrieve error - no privilege | 2008 | Resource URI |  |  | X | X |  |  |
| Retrieve error - does not exist | 2009 | Target URI |  |  | X | X |  |  |
| Update error - no privilege | 2010 | Resource URI |  |  | X | X |  |  |
| Update error - does not exist | 2011 | Resource URI |  |  | X | X |  |  |
| Update error - unacceptable contents | 2012 | Attribute URI |  |  | X | X |  |  |
| Delete error - does not exist | 2013 | Target URI |  |  | X | X |  |  |
| Delete error - no privilege | 2014 | Resource URI |  |  | X | X |  |  |
| Create delivery - not able to take on responsibility | 2015 |  |  |  | X | X |  |  |
| Create fanoutpoint - group request identifier exists | 2016 |  |  |  | X | X |  |  |
| Retrieve fanoutpoint - group request identifier exists | 2017 |  |  |  | X | X |  |  |
| Update fanoutpoint - group request identifier exists | 2018 |  |  |  | X | X |  |  |
| Delete fanoutpoint - group request identifier exists | 2019 |  |  |  | X | X |  |  |
| Create mgmtObj - not allowed | 2020 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - already exists | 2021 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - not reachable | 2022 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - memory shortage | 2023 | CSEBase URI |  |  | X | X |  |  |
| Retrieve mgmtObj - not found | 2024 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj - not reachable | 2025 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj - not found | 2026 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj - not reachable | 2027 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj - not found | 2028 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj - not reachable | 2029 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj - not found | 2030 | MgmtObj URI |  |  | X | X |  |  |
| Cancel execInstance - not cancellable | 2031 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Cancel execInstance - already complete | 2032 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - not cancellable | 2033 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - already complete | 2034 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Retrieve CSEBase - format error | 2035 | CSEBase URI |  |  | X | X |  |  |
| CMDH rules -non compliant | 2036 |  |  |  |  |  |  |  |
| Target is not subscribable | 2037 |  |  |  |  |  |  |  |
| Cannot initiate subscription verification | 2038 |  |  |  |  |  |  |  |
| Subscription verification failed | 2039 | Originator ID | creator |  |  |  |  |  |
| Management session cannot be established | 2042 |  |  |  |  |  |  |  |
| Management session establishment timeout | 2043 |  |  |  |  |  |  |  |

Editor's Note: The contents of this table are exemplary and are expected to be revised. In particular ARC discussions regarding UPDATE and attributes may impact argument1. Some of the exemplary RSCs may be equivalent and can be collapsed to fewer RSCs.

Editor's Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

#### ********************* end of change 2*****************************

# Comments

ARC 8.5.2

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.2.1

ARC 10.1.2

ARC 10.1.3

ARC 10.1.3

ARC 10.1.3

ARC 10.4

ARC 10.1.4

10.2.4.2

10.2.6.6

ARC 10.2.6.7

ARC 10.2.6.8

ARC 10.2.6.9

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.3

ARC 10.2.7.4

ARC 10.2.7.4

ARC 10.2.7.5

ARC 10.2.7.5

ARC 10.2.7.6

ARC 10.2.7.6

ARC 10.2.8.7

ARC 10.2.8.7

ARC 10.2.8.

ARC 10.2.8.9

ARC 10.2.9.2