| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | oneM2M_enumeration_types |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-07-31 |
| Abstract:* | This contribution proposed to update request and response formats, mainly reassigning response code. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed to make following changes

---Change 1 STARTS---

## Message parameter data types

This clause specifies the message parameter data types for messages, which cross the Mca and Mcc reference points.

Editor’s Note: This is per ARC TS, what about Mcc’?

### Request message parameter data types

The data Types of request message parameters are specified in this clause.

Detailed request message parameter descriptions and usage can be found in clause 8.1 of the Architecture TS [6].

Table 6.4.1-1:  Data Types for Request message parameters

| Request message parameter | Short Name | Data Type | Default? | Comment |
| --- | --- | --- | --- | --- |
| Content | cn | m2m:content |  |  |
| Delivery Aggregation | da | xs:boolean | False | If da is not included in the Request and the defaultDelAggregation attribute in the cmdhEcDefParamValues resource is not present, then this default value is used. |
| Discovery Result Type | dr | m2m:dateTime |  |  |
| Event Category | ec | m2m:dateTime |  |  |
| Filter Criteria | fc | m2m:filterCriteria |  |  |
| From | fr | xs:anyURI |  |  |
| Group Request Identifier | gri | xs:string |  |  |
| Name | nm | xs:string |  |  |
| Operation | op | m2m:char |  |  |
| Operational Execution Timestamp | oet | m2m:timestamp |  |  |
| Originating Timestamp | ort | m2m:timestamp |  |  |
| Request Expiration Timestamp | ret | m2m:timestamp |  |  |
| Request Identifier | ri | xs:string |  |  |
| Resource Type | rqt | m2m:resourceType |  |  |
| Response Type | rst | m2m;responseType |  |  |
| Result Content | rc | m2m:resultContent |  |  |
| Result Expiration Timestamp | ret | m2m:timestamp |  |  |
| Result Persistence | rp | xs:duration |  |  |
| Role | ro | xs:string |  | Editor’s Note: Missing procedure in ARC TS |
| To | to | xs:anyURI |  | See ARC TS 9.3.1 |

Table 6.4.1-2: Data Types for filterCriteria parameter

| Condition tag | Data Type | Default? | Note |
| --- | --- | --- | --- |
| createdBefore | xs:dateTime |  |  |
| createdAfter | xs:dateTime |  |  |
| modifiedSince | xs:dateTime |  |  |
| unmodifiedSince | xs:dateTime |  |  |
| stateTagSmaller | xs:string |  | (Same type as common stateTag attribute) |
| stateTagBigger | xs:string |  | (Same type as common stateTag attribute) |
| expireBefore | xs:dateTime |  |  |
| expireAfter | xs:dateTime |  |  |
| Labels | m2m:labels |  |  |
| resourceType | m2m:resourceType |  |  |
| sizeAbove | xs:int |  | (Same type as contentSize attribute of the <contentInstance> resource) |
| sizeBelow | xs:int |  | (Same type as contentSize attribute of the <contentInstance> resource) |
| contentType | xs:string |  |  |
| Limit |  |  |  |
| attributes | List of xs:string |  | Encoding of list of values are specified in protocol bindings |
| filterUsage | xs:string |  |  |
| NOTE1: |

Table 6.4.1.1-2: Enumerated values for response type parameter

| Parameter value | Encoding |  |  |
| --- | --- | --- | --- |
| nonBlockingRequestSynch |  |  |  |
| nonBlockingRequestAsynch |  |  |  |
| blockingRequest |  |  |  |
| NOTE1: |

Table 6.4.1.1-3:  Enumerated values for resource type parameter

| Parameter value | Encoding |  |  |
| --- | --- | --- | --- |
| activeCmdhPolicy |  |  |  |
| accessControlPolicy |  |  |  |
| contentInstance |  |  |  |
| AE |  |  |  |
| cmdhBuffer |  |  |  |
| cmdhDefaults |  |  |  |
| cmdhEcDefParamValues |  |  |  |
| cmdhDefEcValue |  |  |  |
| cmdhLimits |  |  |  |
| cmdhNetworkAccessRules |  |  |  |
| cmdhNwAccessRule |  |  |  |
| cmdhPolicy |  |  |  |
| container |  |  |  |
| CSEBase |  |  |  |
| delivery |  |  |  |
| eventConfig |  |  |  |
| execInstance |  |  |  |
| group |  |  |  |
| locationPolicy |  |  |  |
| fanOutPoint |  |  |  |
| mgmtCmd |  |  |  |
| mgmtObj |  |  |  |
| m2mServiceSubscription |  |  |  |
| Node |  |  |  |
| nodeInfo |  |  |  |
| parameters |  |  |  |
| pollingChannel |  |  |  |
| remoteCSE |  |  |  |
| Request |  |  |  |
| Schedule |  |  |  |
| statsCollect |  |  |  |
| statsConfig |  |  |  |
| subscription |  |  |  |
| NOTE1: |

### Response message parameter data types

The data types of response message parameters are specified in this clause.

Detailed response message parameter descriptions and usage can be found in clause 8.1 of the Architecture TS [6].

Table 6.4.2-1: Data Types for Response message parameters

| Request message parameter | Data Type |  | Comment |
| --- | --- | --- | --- |
| Content | m2m:content |  |  |
| From | xs:anyURI |  |  |
| Originating Timestamp | m2m:dateTime |  |  |
| Response Code | m2m:responseStatusCode |  | See clause 6.8 |
| Request Identifier | xs:string |  |  |
| Response Address | xs:anyURI |  | Editor’s Note: Partially deleted in ARC TS |
| Result Expiration Timestamp | m2m:timestamp |  |  |
| To | xs:anyURI |  | See ARC TS 9.3.1 |

---Change 1 ENDS ---

---Change 2 STARTS ---

## Response Status Codes

### Introduction

The present clause specifies the assignment of oneM2M Response Status Codes (RSC), which is returned as content of Response primitive when the Response type is other than Successful Response.

### RSC Framework Overview

Unsuccessful RSCs are categorised as one of three classes:

Originator Error:
The 4xxx class of status code is intended for cases in which the Request primitive sent from Originator has some problem.

Receiver Error:
The 5xxx class of status code is intended for cases in which the Receiver could not process the Request by some reason.

External System Error:

The 6xxx class of status code is intended for cases in which the Receiver could not process the Request due to error on calling external system thru Mcn reference point.

The term "native" is used to indicate that the RSC source originated as a result of a resource operation validation procedure before protocol mapping is applied.

Table 6.6.3-1 RSC Framework Overview

| Response Class | RSC Source | Numeric Code Range |
| --- | --- | --- |
| Un-successful | Current native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | 4000 - bbbb |
|  | Reserved for future native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped Interworking codes mapped vendor extensions | bbbb+1 - 7999 |
| Acknowledgements | Current native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | 1000 - 1999 |
|  | Reserved for future native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | cccc+1 - 9999 |

Editor's Note: Other terms rather than "current" and "reserved for future" may be preferred e.g. first release and subsequent release.

In Table X.3-1, 0<= aaaa <= 1999, 2000 <= bbbb <= 7999, 8000 <= cccc <= 9999

### Response Status Codes

The tables in the following clauses specify the RSCs for oneM2M releases. Each RSC includes: a response status description, a numeric code, arguments, and applicable APIs (indicated by reference points). The response status description shall be unique within the set of response status descriptions for a release. Response status descriptions may be re-used among RSCs associated with different releases.

#### Successful Responses

#### Un-successful Response Codes

Un-successful Response codes are classified in 4 categories:

Originator-Side Error

Receiver-Side Error

Table 6.8.4.2-1 specify the RSCs for un-successful responses for each release.

Table 6.6.4.2-1: RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 6000 |  |  |  |  |  | X |  |
| Unsupported resource | 5001 | Resource URI |  |  | X | X |  |  |
| Unsupported attribute | 5002 | Attribute URI |  |  | X | X |  |  |
| Cannot forward, target not reachable | 5003 | Resource URI |  |  | X | X |  |  |
| Cannot forward, other reason TBD | 5004 | Resource URI |  |  | X | X |  |  |
| Create error - no privilege | 5005 | Resource URI |  |  | X | X |  |  |
| Create error - already exists | 5006 | Resource URI |  |  | X | X |  |  |
| Create error - missing mandatory parameter | 4007 | Missing parameter |  |  | X | X |  |  |
| Retrieve error - no privilege | 5008 | Resource URI |  |  | X | X |  |  |
| Retrieve error - does not exist | 5009 | Target URI |  |  | X | X |  |  |
| Update error - no privilege | 5010 | Resource URI |  |  | X | X |  |  |
| Update error - does not exist | 5011 | Resource URI |  |  | X | X |  |  |
| Update error - unacceptable contents | 5012 | Attribute URI |  |  | X | X |  |  |
| Delete error - does not exist | 5013 | Target URI |  |  | X | X |  |  |
| Delete error - no privilege | 5014 | Resource URI |  |  | X | X |  |  |
| Create delivery - not able to take on responsibility | 6015 |  |  |  | X | X |  |  |
| Create fanoutpoint - group request identifier exists | 6016 |  |  |  | X | X |  |  |
| Retrieve fanoutpoint - group request identifier exists | 6017 |  |  |  | X | X |  |  |
| Update fanoutpoint - group request identifier exists | 6018 |  |  |  | X | X |  |  |
| Delete fanoutpoint - group request identifier exists | 6019 |  |  |  | X | X |  |  |
| Create mgmtObj - not allowed | 6020 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - already exists | 6021 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - not reachable | 6022 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj - memory shortage | 6023 | CSEBase URI |  |  | X | X |  |  |
| Retrieve mgmtObj - not found | 6024 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj - not reachable | 6025 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj - not found | 6026 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj - not reachable | 6027 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj - not found | 6028 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj - not reachable | 6029 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj - not found | 6030 | MgmtObj URI |  |  | X | X |  |  |
| Cancel execInstance - not cancellable | 6031 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Cancel execInstance - already complete | 6032 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - not cancellable | 6033 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance - already complete | 6034 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Retrieve CSEBase - format error | 5035 | CSEBase URI |  |  | X | X |  |  |
| CMDH rules -non compliant | 4036 |  |  |  |  |  |  |  |
| Target is not subscribable | 5037 |  |  |  |  |  |  |  |
| Cannot initiate subscription verification | 4038 |  |  |  |  |  |  |  |
| Subscription verification failed | 4039 | Originator ID | creator |  |  |  |  |  |

Editor's Note: The contents of this table are exemplary and are expected to be revised. In particular ARC discussions regarding UPDATE and attributes may impact argument1. Some of the exemplary RSCs may be equivalent and can be collapsed to fewer RSCs.

Editor's Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

#### Acknowledgement Responses

Table 6.8.4.3-1 specify the RSCs for acknowledgement responses for each release.

Table 6.6.4.3-1: RSCs for Acknowledgement Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
|  | 1000 |  |  |  |  |  |  |  |
|  | 1001 |  |  |  |  |  |  |  |
|  | 1002 |  |  |  |  |  |  |  |
|  | 1003 |  |  |  |  |  |  |  |
|  | 1004 |  |  |  |  |  |  |  |
|  | 1005 |  |  |  |  |  |  |  |
|  | 1006 |  |  |  |  |  |  |  |

---Change 2 ENS ---

# Comments

Is it a reference? If yes, they should be added in the reference clause.

ARC 8.5.2

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.2.1

ARC 10.1.2

ARC 10.1.3

ARC 10.1.3

ARC 10.1.3

ARC 10.4

ARC 10.1.4

10.2.4.2

10.2.6.6

ARC 10.2.6.7

ARC 10.2.6.8

ARC 10.2.6.9

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.3

ARC 10.2.7.4

ARC 10.2.7.4

ARC 10.2.7.5

ARC 10.2.7.5

ARC 10.2.7.6

ARC 10.2.7.6

ARC 10.2.8.7

ARC 10.2.8.7

ARC 10.2.8.

ARC 10.2.8.9

ARC 10.2.9.2