| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | FUJITSU |
| Format:* | ordinary meeting |
| Date:* | 2014-09-25 |
| Contact:* | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | For improvement Readability and Ease on document development, and allowing anonymous structured data. |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | TS-0004 V0.6.2 |
| Clauses/Sub Clauses* | 6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

For improvement Readability and Ease on document development, and allowing anonymous structured data.

### -----------------------Start of change 1-------------------------------------------

#### 6.3.2 oneM2M Simple Data Types

Table 6.3.2.1-1 describes oneM2M-specific simple data type definitions.

(Snipped)

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 6.3.3 oneM2M Enumerated Data Types

##### 6.3.3.1 Introduction

The oneM2M Enumeration Types are defined as extention from ‘enumeration type’ which is defined in XML Schema definition [3]. The oneM2M Enumeration Types are based on <xs:integer>, and the numeric values are interpreted as specified in clause 6.3.2.2. Table 6.3.2.2.1-1 shows the example of Enumeration Type Definition for m2m:enumFooType.

(Snipped)

##### 6.3.3.2 Enumeration Type Definitions

###### 6.3.3.2.1 m2m:resourceType

(Change should be implemented as same)

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 6.3.4 oneM2M Complex Data Types

#### The present clause defines structured information for specific use in oneM2M protocol.

#### Editor’s Note: explanation of table notations and example should be provided later.

#### 6.3.4.1 m2m:filterCriteria

#### Used for fc (filter criteria) parameter in a request.

Table 6.3.4.1-1: Type Definition of m2m:filterCriteria

| Element Path |  | Element Data Type | Mutiplicity | Note |
| --- | --- | --- | --- | --- |
| createdBefore |  | xs:dateTime |  |  |
| createdAfter |  | xs:dateTime |  |  |
| modifiedSince |  | xs:dateTime |  |  |
| unmodifiedSince |  | xs:dateTime |  |  |
| stateTagSmaller |  | xs:positiveInteger |  |  |
| stateTagBigger |  | xs:nonNegativeInteger |  |  |
| expireBefore |  | xs:dateTime |  |  |
| expireAfter |  | xs:dateTime |  |  |
| labels |  | xs:token |  |  |
| resourceType |  | m2m:resourceType |  |  |
| sizeAbove |  | xs:nonNegativeInteger |  |  |
| sizeBelow |  | xs:positiveInteger |  |  |
| contentType |  | m2m:typeOfContent |  |  |
| limit |  | xs:positiveInteger |  |  |
| attribute |  | m2m:attribute |  |  |
| filterUsage |  | m2m:filterUsage |  |  |

#### 6.3.4.2 eventCat

Used for ec parameter in request and eventCat attribute of <delivery> resource.

Table 6.3.5.2-1: Type Definition of m2m:eventCat

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| eventCatType |  | m2m:eventCatType |  |  |
| eventCatNo |  | xs:nonNegativeInteger |  |  |

#### 6.3.4.3 deliveryMetaData

#### Used for deliveryMetaData attribute in <delivery> resource.

TBD

#### 6.3.4.4 aggregatedRequest

Used for aggregatedRequest attribute in <delivery> resource.

TBD

#### 6.3.4.5 metaInformation

Used for metaInformation attribute in <request> resource.

TBD

#### 6.3.4.6 content

Used for cn parameter in request/response and content attribute in <request> resource.

TBD

#### 6.3.4.7 batchNotify

Used for batchNotify attribute in <subscription> resource.

Table 6.3.4.7-1: Type Definition of m2m:batchNotify

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| number |  | xs:nonNegativeInteger |  |  |
| duration |  | xs:duration |  |  |

#### 6.3.4.8 eventNotificationCriteria

Used for eventNotificationCriteria of a <subscription> resource.

Table 6.3.4.8-1: Type Definition of m2m:eventNotificationCriteria

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| createdBefore |  | xs:dateTime |  |  |
| createdAfter |  | xs:dateTime |  |  |
| modifiedSince |  | xs:dateTime |  |  |
| unmodifiedSince |  | xs:dateTime |  |  |
| stateTagSmaller |  | xs:positiveInteger |  |  |
| stateTagBigger |  | xs:nonNegativeInteger |  |  |
| expireBefore |  | xs:dateTime |  |  |
| expireAfter |  | xs:dateTime |  |  |
| sizeAbove |  | xs:nonNegativeInteger |  |  |
| sizeBelow |  | xs:positiveInteger |  |  |
| resourceStatus |  | m2m:resourceStatus |  |  |
| operationMonitor |  | m2m:operation |  |  |
| Attribute |  | m2m:attribute |  |  |

#### 6.3.4.9 aggregatedNotification

Table 6.3.4.9-1: Type Definition of m2m:aggregatedNotification

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| notification |  | m2m:singleNotification |  |  |

#### 6.3.4.10 singleNotification

Table 6.3.4.10-1: Type Definition of m2m:singleNotification

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| notificationEvent |  | m2m:notificationEvent |  |  |
| verificationRequest |  | xs:boolean |  |  |
| subscriptionDeletion |  | xs:boolean |  |  |
| subscriptionReference |  | xs:anyURI |  |  |
| creator |  | m2m:id |  |  |
| notificationForwardingURI |  | xs:anyURI |  |  |

#### 6.3.4.11 notificationEvent

Used for representation of resource at notification event.

Table 6.3.4.11-1: Type Definition of m2m:notificationEvent

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| all resource specific attributes of subscribable resource types. |  | data type of each attribute (This is defined in the sub-clauses of clause 7.3) |  | Used for representation of resource at notification event. |
| resourceStatus |  | m2m:resourceStatus |  |  |
| operationMonitor |  | m2m:operationMonitor |  |  |

#### 6.3.4.12 operationMonitor

Table 6.3.4.12-1: Type Definition of m2m:operationMonitor

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| operation |  | m2m:operation |  |  |
| originator |  | m2m:id |  |  |

#### 6.3.4.13 externalID

Table 6.3.4.13-1: Type Definition of m2m:externalID

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| accessId |  | m2m:networkaccessIdentifier |  | The identifier of the node for the underlying network provider. In 3GPP case, the accessId is mapped to External Identifier as specified in TS 23.003 [17]. |
| MSISDN |  | xs: string |  | The identifier of the node as specified in TS 23.003 [17], |

#### 6.3.4.14 actionStatus

Table 6.3.4.14-1: Type Definition of m2m:actionStatus

| Element Path |  | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- | --- |
| action |  | xs:anyURI |  | Reference to the action (represented by a resource attribute) being performed |
| status |  | m2m:status |  | Indicates the status of the operation is successful, failure or in process. See Table 6.3.2.2 1 |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Removing this level and children of this clauses are 1 level up